## Slide 1: Rel-17 feature on hybrid duplex operation for PC2 FDD bands
Apple
3GPP TSG-RAN #96-e
Budapest, Hungary, June 6th – 9th, 2022
RP-221573

## Slide 2: Background (1)
PC2 for FDD bands has been introduced in Rel-17 for n1 and n3 [1].
One of the main concerns for PC2 FDD bands is the REFSENS impact due to uplink transmission self-interference for bands with narrow duplex gap such as n3 which is expected to be aggravated with increasing transmit output power.
It has been analyzed that for PC2 n3, the MSD can be up to 25 dB for 50MHz channel BW, and for PC2 n8, the MSD can be up to 25 dB for 35MHz channel BW with UL restricted to 20 MHz [2].
As more PC2 FDD bands are foreseen to be introduced in Rel-18 basket WID [3], such as n5, n8, n26, and n28 which could suffer from even higher MSD impact under PC2 operation, MSD mitigation other than UL RB allocation restriction is deemed necessary, or the benefit of PC2 operation for certain FDD bands may not be realized.

## Slide 3: Background (2)
To mitigate the MSD issue for CA and DC combinations, RAN4 has defined capability signaling for simultaneous/non-simultaneous Rx/Tx as illustrated in the following example band combination.
For the same reason, “hybrid duplex operation” feature has been proposed to mitigate the MSD issue for PC2 FDD bands where half-duplex operation can be scheduled when UL power is above certain threshold such as 23 dBm [4].
n40
2300MHz
2400MHz
n7 UL
n7 DL
2500MHz
2570MHz
2620MHz
2690MHz
MSD due to insufficient
cross-band isolation
Non-simultaneous Rx/Tx capability can be signaled by UE for CA_n7-n40 for MSD mitigation

## Slide 4: Justifications for hybrid duplex operation
The half-duplex operation for FDD bands is no different from non-simultaneous Rx/Tx operation for CA or DC combinations. The scheduling is within the same cell which should not be more complicated than cross-cell scheduling for inter-band CA or DC.
Half-duplex operation is already supported by RedCap UE for FDD bands which shares the common network with non-RedCap UE.
Hybrid duplex operation only operates half-duplex mode when UL power is above certain threshold which is more efficient than CA or DC constantly operating under non-simultaneous Rx/Tx operation.
Scheduling can be transparent to UE. Therefore, no additional UE RF requirement is needed.
It is a per-band optional feature. For UE which has no concern of MSD issue under PC2 operation can always choose not to signal the support of the feature.

## Slide 5: Other benefits for hybrid duplex operation
Half-duplex mode totally avoids the REFSENS impact. Therefore, the UL traffic can be transmitted in intermittent short time bursts with full UL allocation. This not only reduces the UL duty cycle to mitigate the SAR issue under HPUE, but also help reduce UL power consumption.
Without UL self-interference under half-duplex mode, DL with sufficient SNR may potentially be scheduled with higher order modulation to enhance data rate and spectrum efficiency.
If half-duplex operation can be indicated to UE by gNB (non-transparent operation), UE implementation may take the advantage to bypass duplexer when in half-duplex mode, which not only help reduce the insertion loss for Tx, but also alleviate the thermal stress to duplexer due to high power transmission which could cause duplexer long-term damage and result in performance degradation. The non-transparent operation can be considered as an enhancement of the proposed hybrid duplexer operation feature in Rel-18 or later while the Rel-17 feature can be restricted to transparent operation only.

## Slide 6: Proposals
Proposal 1: Introduce an optional hybrid duplex operation feature in Rel-17.
Proposal 2: The Rel-17 hybrid duplex operation is restricted to transparent operation only where no RAN1 specifications impact is anticipated.

## Slide 7: References
[1] RP-212633 “New WID on high power UE (power class 2) for NR FDD band”, China Unicom, 3GPP TSG-RAN Meeting #93-e, September 13th – 17th, 2021
[2] R4-2200441 “NR FDD HPUE MSD and system performance analyses”, Apple, 3GPP TSG-RAN WG4 Meeting #101bis-e, January 17th – 25th, 2022
[3] R4-2207702 “New WID on high power UE (power class 2) for NR FDD bands”, China Unicom, 3GPP TSG-RAN WG4 Meeting #103-e, May 9th – 20th, 2022
[4] R4-2203690 “On hybrid duplex operation for PC2 FDD bands”, Apple, 3GPP TSG-RAN WG4 Meeting #102-e, Feb 21st – March 3rd, 2022