## Slide 1: Discussion on co-channel scenarios and adjacent-channel scenarios for duplex operation
3GPP TSG RAN Meeting #96
Budapest, Hungary, June 6-9, 2022
Source: ZTE, Sanechips
Agenda: 9.2.6
RP-221646

## Slide 2: Background: SID (1/2)
[1]. RP-220633, Revised SID: Study on evolution of NR duplex operation, RAN#95-e, CMCC
The objective of this study is to identify and evaluate the potential enhancements to support duplex evolution for NR TDD in unpaired spectrum. In this study, the followings are assumed: • Duplex enhancement at the gNB side • Half duplex operation at the UE side • No restriction on frequency ranges The detailed objectives are as follows: • Identify applicable and relevant deployment scenarios (RAN1). • Develop evaluation methodology for duplex enhancement (RAN1). • Study the subband non-overlapping full duplex and potential enhancements on dynamic/flexible TDD (RAN1, RAN4). - Identify possible schemes and evaluate their feasibility and performances (RAN1). - Study inter-gNB and inter-UE CLI handling and identify solutions to manage them (RAN1). Consider intra-subband CLI and inter-subband CLI in case of the subband non-overlapping full duplex. - Study the performance of the identified schemes as well as the impact on legacy operation assuming their co-existence in co-channel and adjacent channels (RAN1). - Study the feasibility of and impact on RF requirements considering adjacent-channel co-existence with the legacy operation (RAN4). - Study the feasibility of and impact on RF requirements considering the self-interference, the inter-subband CLI, and the inter-operator CLI at gNB and the inter-subband CLI and inter-operator CLI at UE (RAN4). - Note: RAN4 should be involved early to provide necessary information to RAN1 as needed and to study the feasibility aspects due to high impact in antenna/RF and algorithm design, which include antenna isolation, TX IM suppression in the RX part, filtering and digital interference suppression. - Summarize the regulatory aspects that have to be considered for deploying the identified duplex enhancements in TDD unpaired spectrum (RAN4). Note: For potential enhancements on dynamic/flexible TDD, utilize the outcome of discussion in Rel-15 and Rel-16 while avoiding the repetition of the same discussion.

## Slide 3: Background: Discussion in RAN1#109-e (2/2)
[1]. R1-2205540, Summary# of email discussion on evaluation of NR duplex evolution, RAN1#109-e, Moderator (CMCC).
[2]. R1-2205374, Summary #4 of [109-e-R18-Duplex-04] Email discussion on dynamic/flexible TDD, RAN1#109-e, Moderator (LG Electronics)
During the discussion in RAN1#109-e meeting, companies have different understandings whether/how to treat co-channel scenarios and adjacent-channel scenarios for duplex operation in RAN1. Basically, there are the following three alternatives mentioned during the RAN1 discussion. Alt.1: Study co-channel scenarios and adjacent-channel scenarios in RAN4 only Alt.2: Study co-channel scenarios and adjacent-channel scenarios in both RAN1 and RAN4, with the understanding that these scenarios are considered as lower priority Alt.3: Study co-channel scenarios and adjacent-channel scenarios in both RAN1 and RAN4, with the understanding that these scenarios are considered as high priority (i.e., the same priority as duplex scenarios without any co-existence) Similar issues happen to dynamic TDD. Companies have different understandings on whether adjacent-channel scenarios should be discussed in RAN1 considering that RAN4 has done similar work in Rel-16 CLI. Note1: “Co-channel scenarios” refer to SBFD/Dynamic TDD co-existence with co-channel legacy TDD system Note2: “Adjacent-channel scenarios” refer to SBFD/Dynamic TDD co-existence with adjacent-channel legacy TDD system

## Slide 4: Proposals
Sub-band full duplex Considering that co-channel scenarios and adjacent-channel scenarios are clearly listed in the existing Rel-18 Duplex SID and they are the main challenges for the deployment of sub-band full duplex, it is suggested to study co-channel scenarios and adjacent-channel scenarios in both RAN1 and RAN4, with the understanding that these scenarios are considered as high priority in RAN1 (i.e., the same priority as duplex scenarios without any co-existence). Tight coordination between RAN1 and RAN4 may be needed to avoid duplicated discussion. Proposal#1: For Rel-18 sub-band full duplex, study co-channel scenarios and adjacent-channel scenarios in both RAN1 and RAN4 and consider co-channel scenarios and adjacent-channel scenarios as high priority in RAN1 (i.e., the same priority as duplex scenarios without any co-existence) Dynamic TDD For dynamic TDD scenarios in Rel-18 Duplex SID, it is suggested to also study adjacent-channel scenarios as high priority in RAN1. Because Rel-16 CLI study only focus on the homogeneous network scenarios and only large scale channel models are used in the simulation, to fully investigate the potential of dynamic TDD, Rel-18 study for dynamic TDD can consider more scenarios including Hetnet, more sophisticated channel model (e.g., including small scales parameters) and more sophisticated solutions to address the CLI. Proposal#2: For Rel-18 dynamic TDD in Duplex SID, study adjacent-channel scenarios in both RAN1 and RAN4 and consider adjacent-channel scenarios as high priority in RAN1 (i.e., the same priority as co-channel scenarios).

## Slide 5: Thank you