## Slide 1
Title: On the work scope of Rel-18 NR NTN enhancements
Agenda item: 9.3.2.7
Source: Samsung
Document for: Decision
3GPP TSG RAN Meeting #97-e
Electronic Meeting, September 12 – 16, 2022
RP-222234

## Slide 2: Background: Description in WID
RAN1 have studied the following as described in WID
<omitted>
The evaluation should also take into account any related requirements, e.g., ITU limitation of power flux density.
Have a 1-TU 6-month study phase focusing on the following (to derive clear & limited scope):
Evaluate the coverage performance and identify the candidate physical radio channels that have coverage issues specific to NTN with following target services taking into account the studies in TR38.830 where appropriate, as well as general coverage enhancement techniques specified in Rel-18 [RAN1,RAN2,RAN4]
<omitted>

## Slide 3: Discussion in RAN1#110
Physical channel / signal | RAN1 conclusion & observation
PUCCH format 1 | Enhancement is unnecessary
PUCCH format 3 | Enhancement is unnecessary
PUCCH for Msg4 HARQ-ACK | It should be enhanced to meet the coverage requirements
PUSCH for low data rate of 3 kbps | Enhancement is unnecessary
PUSCH for VoIP | Enhancement may be needed to meet the coverage requirements, when DMRS bundling is not applied. (When DMRS bundling is applied, 4 companies observed to meet the coverage requirements while 1 company observed not to meet the coverage requirement)
Msg3 PUSCH | Enhancement is unnecessary
RAN1 has studied on whether or not it is necessary to enhance coverage with the assumption of LEO (1200km), LOS, -5dBi UE antenna gain and satellite configuration (set-1). The following table is summary of what RAN1 observed and concluded from study.
Also, there was a discussion about regulatory requirements, e.g., ITU limitation of power flux density (PFD) but RAN1 couldn’t make consensus on whether the satellite transmission power reduction is to be applied or not

## Slide 4: Proposals
Proposal 1: As per RAN1 conclusion, coverage enhancement for Rel-18 NTN is focused on PUCCH for Msg4 HARQ-ACK.
Proposal 2: Rel-17 coverage enhancements schemes for TN are reused for PUSCH for VoIP in Rel-18 NTN.
Proposal 3: Discussion on the PFD (power flux density), i.e., whether satellite transmission power reduction is applied or not is postponed to next release.