## Slide 1: Agenda Item: 9.3.1.5 Source: xiaomi Title: Views on scope of NR sidelink evolution WI Document for: Discussion and decision
3GPP TSG RAN Meeting #97-e
Electronic Meeting, September 12-16, 2022
RP-222247

## Slide 2: Background
Objective 1 and 3 in WID are put on hold until further checking in RAN#97
  1.Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4] (This part of the work is put on hold until further checking in RAN#97)
    Support only LTE sidelink CA features for NR (i.e., SL carrier (re-)selection, synchronization of aggregated carriers, handling the limited capability, power control for simultaneous sidelink TX, packet duplication)
    The work is limited to FR1 licensed spectrum and ITS band in FR1.
    No specific enhancements of Rel-17 sidelink features with sidelink CA support.
    This feature is backwards compatible in the following regards
      A Rel-16/Rel-17 UE can receive Rel-18 sidelink broadcast/groupcast transmissions with CA for the carrier on which it receives PSCCH/PSSCH and transmits the corresponding sidelink HARQ feedback (when SL-HARQ is enabled in SCI)
  3.Study and specify enhanced sidelink operation on FR2 licensed spectrum [RAN1, RAN2, RAN4] (This part of the work is put on hold until further checking in RAN#97)
    Update evaluation methodology for commercial deployment scenario
    Work is limited to the support of sidelink beam management (including initial beam-pairing, beam maintenance, and beam failure recovery, etc) by reusing existing sidelink CSI framework and reusing Uu beam management concepts wherever possible.
      Beam management in FR2 licensed spectrum considers sidelink unicast communication only.

## Slide 3: WI progress and observation
Unitl RAN1#110 meeting, the progress on both objective 2 (SL unlicensed) and objective 4 (co-channel coexistence) in RAN1 are not fast as expected
  The study on SL unlicensed is to be completed until RAN#98e
  The study on dynamic resource sharing for co-channel coexistence is still going on
    The feasiblity and effective of proposed solutions are still to be concluded
  RAN1 conclued that TDMed based semi-static resource pool partitioning based on Rel-16/17 specification is one possible solution
Observation
  The progress in RAN1 would be further slow down if all the four objectives are progressing simultaneously
  If both objective 1 and objective 3 starts from RAN#97 meeting, the workload in RAN1 would be too high and there is high risk that the WI cannot be completed on time

## Slide 4: Limit the work scope
Following options can be considered to limit the scope of the WI
  Option 1: Downselect one objective between objective 1 and objective 3 to start from RAN#97
    The other objective is removed from Rel-18
  Option 2: Remove the study of dyanmic resource sharing from objective 4, and complete objective 4 with the current RAN1 conclusion
    Objective 1 and objective 3 both start from RAN#97
  Option 3: Keep objective 1 and objective 3 on hold until RAN#98
    Determine whether to start objective 1 and/or objective 3 based on the progress until RAN#98 meeting
Proposal 1: The workscope of Rel-18 sidelink evolution shall be further limited

## Slide 5: Thanks