## Slide 1
3GPP TSG RAN Meeting #97-e RP-222361
Electronic Meeting, September 14-18, 2022
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.6.1.1
Discussion on 4Rx for 6GHz bands

## Slide 2
In RAN#96 meeting, the WF on 4Rx RP-221869 was discussed and WF was finally noted, with the conclusion that proposal 2 is endorsed:
    Proposal 2: Topic of 4Rx support in 6 GHz range is RAN-level discussion.
In RAN#78 meeting, the WF RP-172788 concluded that 4Rx is mandatory for some specific Rel-15 bands:
    For NR Bands n7, n38, n41, n77, n78, and n79 the UE shall be equipped with 4Rx ports as a baseline
      Applicability to other NR bands is FFS
      For certain UE types/categories, some exceptions to this requirement may be applicable in future
However, it is clear that the agreements is only applicable for the above specific bands, but not all the bands above 3GHz, other NR bands is FFS.
  Discussions on 4Rx
Observation: Rel-15 4RX mandatory is just applicable to specific NR bands, but not all TDD bands above 3GHz.

## Slide 3
For UE antenna implementation, there would be separate antenna for band n78/n79 (3.5GHz/5GHz) and band n104 (close to 7GHz), considering the difficulty of antenna sharing with other bands, to make 4Rx mandatory for 7GHz frequency would be less flexible.
In addition, for 6GHz unlicensed bands, 2Rx was decided as mandatory. From UE design perspective, it is valuable to align the same applicability for the similar frequency bands to reduce UE implementation burden.
  Discussions on 4Rx, cont.
Proposal: 4Rx support is optional for the licensed operation in 6GHz range.