## Slide 1: Discussion on the scope of Rel-18 NR SL positioning
3GPP TSG RAN Meeting #97-e
Electronic Meeting, September 12 - 16, 2022
Source: ZTE, Sanechips
Agenda: 9.2.5
RP-222450

## Slide 2: Background
    In the SID RP-221814 for Study on expanded and improved NR positioning, there is a note for checkpoint at RAN#97 meeting on Rel-18 NR SL positioning scope.
Note: When the bandwidth requirements have been determined and the study of sidelink communication in unlicensed spectrum has progressed, it can be reviewed whether unlicensed spectrum can be considered in further work. Checkpoint at RAN#97 to see if sufficient information is available for this review.

## Slide 3: Current RAN1 status
    RAN1 SL positioning study is ongoing in NR Rel-18 positioning agenda. Most progress of evaluation is for simulation assumptions. The performance evaluation collection/summary has not been started yet.
      Bandwidth requirements and simulation assumptions include larger bandwidth, e.g. 100MHz which is not supported in ITS bands in FR1.
      Bandwidth requirements and simulation assumptions also include FR2
    The study for support of SL communication excluding positioning on unlicensed spectrum is on going in NR Rel-18 SL evolution agenda, where RAN1 study phase focuses on FR1 unlicensed bands (n46 and n96/n102) to be completed by RAN1#111 in November 2022.
    Enhancement of SL communication on FR2 has not been started yet.
      It may likely be down-scoped in NR Rel-18

## Slide 4: Proposals
    Views:
      The workload of Rel-18 NR positioning including 7 sub-agendas in RAN1 is already very high .
      Rel-17 standards do not support SL communication on unlicensed spectrum. Overlapping/colliding discussion may happen if the discussions for SL positioning on unlicensed spectrum and for SL communication on unlicensed spectrum are allowed in different Rel-18 agendas.
      Study on FR2 SL positioning is hard because the study on support of basic SL communication in FR2 has not been started yet in Rel-18.
    Proposal: Rel-18 NR SL positioning should be based on Rel-17 Uu positioning and Rel-17 SL communication:
      Unlicensed spectrum should not be included in the scope
      FR2 should not be included in the scope

## Slide 5: Thanks