## Slide 1
3GPP TSG RAN Meeting #98e RP-223096
e-Meeting, December 12th – 16th , 2022
Finalization of Rel-18 RAN AI/ML representative sub use cases
Source: vivo
Document for: Discussion
Agenda Item: 9.2.8

## Slide 2
Background
The following was arranged on how to proceed Rel-18 RAN AI/ML use case discussion when WID is drafted
RAN1 followed the guidance and conducted study on representative sub-use cases

## Slide 3
Agreements from RAN1
Agreement
Spatial-frequency domain CSI compression using two-sided AI model is selected as one representative sub use case.
Note: Study of other sub use cases is not precluded.
Note: All pre-processing/post-processing, quantization/de-quantization are within the scope of the sub use case.
Agreement
Time domain CSI prediction using UE sided model is selected as a representative sub-use case for CSI enhancement.
Note: Continue evaluation discussion in 9.2.2.1.
Note: RAN1 Defer potential specification impact discussion at 9.2.2.2 until the RAN1#112b-e, and RAN1 will revisit at RAN1#112b-e whether to defer futher till the end of R18 AI/ML SI.
Note: LCM related potential specification impact follow the high level principle of other one-sided model sub-cases.
Agreement
For AI/ML-based beam management, support BM-Case1 and BM-Case2 for characterization and baseline performance evaluations
BM-Case1: Spatial-domain DL beam prediction for Set A of beams based on measurement results of Set B of beams
BM-Case2: Temporal DL beam prediction for Set A of beams based on the historic measurement results of Set B of beams
Agreement
For AI/ML based positioning accuracy enhancement, direct AI/ML positioning and AI/ML assisted positioning are selected as representative sub-use cases.

## Slide 4
Proposals
    Confirm the following RAN1 agreed sub-use cases as representative sub-use cases for characterization and baseline performance evaluations for Rel-18 RAN AI/ML study:
  CSI feedback enhancement
    Spatial-frequency domain CSI compression using two-sided AI model
    Time domain CSI prediction using UE sided model
  Beam management
    Spatial-domain DL beam prediction for Set A of beams based on measurement results of Set B of beams
    Temporal DL beam prediction for Set A of beams based on the historic measurement results of Set B of beams
  Positioning accuracy enhancements for different scenarios
    direct AI/ML positioning
    AI/ML assisted positioning