## Slide 1
3GPP TSG RAN Meeting #98-e RP-223103
Electronic Meeting, December 12-16, 2022
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.3.2.1
Discussion on scope of Rel-18 further mobility enhancement WI

## Slide 2
In the WID [1] for further mobility enhancement in Rel-18, one of the objectives as below is to study the feasibility of improvement in FR2 SCell/SCG setup delay.
  To study the following, with completion targeted by RAN#98 meeting [RAN4]:
    The impact of FR2 RRM mobility measurement acquisition and reporting on FR2 SCell/SCG setup/resume delay for a UE connecting from idle/inactive mode.
    The level of feasible improvement in FR2 SCell/SCG setup delay from defining new UE measurement procedures and RRM core requirements, and whether additional information from the network would help the UE to perform those measurements effectively. The following sequence of events should be assumed.
      The UE initiates and performs improved measurements when it requests RRC connection setup/resume.
      After acquiring those improved measurements, the UE subsequently reports those measurements to the network to support SCell/SCG setup.
  Study objective on FR2 Scell/SCG setup delay improvement

## Slide 3
RAN4 has performed the studies in the past three work group meetings. It was concluded in [2] there are potential directions that are feasible to improve FR2 SCell/SCG setup delay.
Agreement RAN4 #105:
  Enhancements on UE behavior in IDLE/INACTIVE mode are not in the scope of the WI
  The following aspects can be further studied
    Using measurement results obtained during IDLE/INACTIVE mode for measurements during RRC connection procedure
    Note: enhancements on IDLE/INACTIVE mode measurements are not in the scope
From RAN4 conclusion, following observations can be made.
Observation 1: It is feasible to improve FR2 Scell/SCG setup delay by using measurement results, which are obtained during IDLE/INACTIVE mode for measurements, during RRC connection procedure with defining new measurement procedures and RRM core requirements.
Observation 2: It is feasible to improve FR2 Scell/SCG setup delay by enhancements on UE behavior in IDLE/INACTIVE mode. However, such enhancements are not in the current scope of the WI.
  RAN4 feasibility study conclusion

## Slide 4
Since feasibility study of original objective is concluded, it is reasonable to move on to WI phase of the objective for FR2 SCell/SCG setup delay improvement.
Proposal 1: Defining new UE measurement procedures and RRM core requirements for improvement in FR2 SCell/SCG setup delay during RRC connection setup procedure under following sequence of events.
  The UE initiates and performs improved measurements when it aware of RRC connection setup/resume.
  UE uses measurement results obtained during IDLE/INACTIVE mode for further improved measurements
  After acquiring those improved measurements, the UE subsequently reports those measurements to the network to support SCell/SCG setup.
Regarding enhancement on UE measurement in IDLE/INACTIVE mode, we don’t think it is necessary. In addition, it is not in the scope of current WI.
Proposal 2: Not to enhance measurement requirements and procedures on UE behavior in IDLE/INACTIVE mode measurement.
  Next step

## Slide 5
The objective of WI phase for FR2 SCell /SCG setup delay improvement is proposed as follows.
  Defining new UE measurement procedures and RRM core requirements during RRC connection setup/resume for FR2 SCell/SCG setup delay improvement [RAN4, RAN2]:
    The UE initiates and performs improved measurements when it is aware of RRC connection setup/resume.
    UE uses measurement results obtained during IDLE/INACTIVE mode for further improved measurements
    After acquiring those improved measurements, the UE subsequently reports those measurements to the network to support SCell/SCG setup.
  Objective of the WI phase

## Slide 6
R4-2220734 LS on improvement in FR2 SCell/SCG setup delay, MediaTek, RAN4, RAN4#105
R4-2220734 Revised WID on Further NR mobility enhancements, MediaTek Inc., RAN#96
  Reference