## Slide 1
3GPP TSG RAN Meeting #98-e RP-223110
Electronic Meeting, December 12-16, 2022
Source: vivo
Document for: Discussion
Agenda Item: 9.3.4.12
Discussions on Rel-18 MIMO OTA enhancement

## Slide 2
Background
For Rel-18 MIMO OTA enhancement, WID RP‑222668, there is a check point for FR2 requirement framework:
Hybrid of simulation results and measurement results will be considered as the starting point in FR2 requirement definition
  - Note: Revisit in RAN#98 to check the feasibility and progress of hybrid simulation and measurement approach.
In RAN4#104-bis-e and RAN4#105 meeting, some progress have been made on the framework for FR2 requirement definition, a general framework in R4-2220273 was agreed as a starting point.
However, many key aspects are still undefined, whether current FR2 framework is feasible to define FR2 requirement is not confirmed.
In addition, in RAN4#105 meeting, there are some agreements related to FR1 MIMO OTA working scope, the conclusion should be properly reflected in the WID.

## Slide 3
RAN4 progress on general FR2 framework R4-2220273
In the framework, there are two approaches to define FR2 MIMO OTA requirements, i.e. pure measurement approach and Hybrid approach
  Pure measurement approach means the same way as FR1 MIMO OTA to derive measured CDF and final requirements
  Hybrid approach uses both simulation results and measurement results based on simulation campaign and measurement campaign
For both of above two approaches, it is confirmed that several common actions are needed:
  FR2 lab alignment activity
  FR2 MIMO OTA Channel model validation activity
  FR2 smartphone measurement results from aligned test labs
Fig. 1. Work flow of FR2 MIMO OTA performance requirements development in R4-2220273

## Slide 4
Feasibility of Pure measurement approach
For lab alignment activity
  The framework is still under discussion and targeted for finalization till RAN4#106
  No sufficient number of FR2 smartphone is confirmed. By now, only one volunteer device is collected with no UE panel and antenna pattern information being shared.
Finalize the framework for the lab alignment no later than RAN4 106 meeting (Feb. 2023).
At least [3] participating labs and at least [2-4] Performance Alignment Devices (PADs) per band are required.
For FR2 measurement campaign
  The minimum number of commercial devices for defining requirements is [8-15] per band, no sufficient number of FR2 smartphones is confirmed for now.
Observation 1: The feasibility of pure measurement approach to define FR2 MIMO OTA requirement is not confirmed.

## Slide 5
Feasibility of Hybrid approach
For Simulation Platform Validation Activity
  The feasibility of FR2 lab alignment for simulation platform validation is not confirmed
  How to implement the antenna pattern into FR2 simulation activity is FFS
[The lab alignment is required for the validation activity, i.e., the measurement results used for the validation activity should come from the aligned lab(s).]
  Further check the feasibility of the lab alignment for the validation activity
Observation 2: The feasibility of hybrid approach to define FR2 MIMO OTA requirement is not confirmed.
Measurement results that will be selected to validate simulation models, should be accompanied by its antenna system radiation pattern, the format in which the radiation pattern is provided will be based on simulation platform proponents’ requirements.
  Further discuss how to obtain the antenna system radiation patterns
  FFS on other impact such as baseband capability

## Slide 6
Potential Objectives update for FR2 MIMO OTA
For both pure measurement approach and hybrid approach, the feasibility is not confirmed, which should be concluded till RAN#99 meeting.
Besides, to specify the final FR2 MIMO OTA requirement, single approach should be adopted, down-selection needs to be done in RAN4 before performance part starts.
Therefore, it is suggested to update the FR2 objectives as following:
Proposal 1: Update the WID to further check FR2 framework feasibility, and down-selection of the approaches is needed.

## Slide 7
Potential Objectives update for FR1 MIMO OTA
In agreed WF R4-2220612, it was agreed that RAN4 concludes no need to introduce new channel models for FR1 MIMO OTA in Rel-18.
It is suggested to update the WID accordingly:
  Introduce more FR1 channel models based on operator requests
Proposal 2: Update the WID with removing the scope of introducing more FR1 channel models.

## Slide 8
Conclusion
Observation 1: The feasibility of pure measurement approach to define FR2 MIMO OTA requirement is not confirmed.
Observation 2: The feasibility of hybrid approach to define FR2 MIMO OTA requirement is not confirmed.
Proposal 1: Update the WID to further check FR2 framework feasibility, and down-selection of the approaches is needed.
Proposal 2: Update the WID with removing the scope of introducing more FR1 channel models.