## Slide 1
Way forward on the support of 2Rx for XR device for Rel-18 XR WI
Apple, ABS, APT, ASR, CATT, FGI, Google, HONOR, Lenovo, Meta, New H3C, Qualcomm, Samsung, Tencent, Verizon, vivo, Xiaomi, …
  3GPP TSG-RAN #98-e
  e-Meeting, December 12th-16th 2022
  Agenda Item: 9.1.2
  Document for: Discussion/Decision
  RP-223208

## Slide 2
Rel-18 XR WI | Proposed Way Forward
Proposed Way Forward: For 3GPP Rel-18 XR Work Item, include the following objective
  Specify mechanism to support new device type (XR) that is only mandated to support 2Rx antenna ports in the NR bands in which 4Rx antenna ports is mandated in legacy [RAN4, RAN2]

## Slide 3
Rel-18 XR WI | Background
In current NR, for NR Bands n7, n38, n41, n77, n78, and n79, the UE is mandated to support 4Rx ports (RP-172788).
  Except for vehicular UE and RedCap UE
Current NR already supports relaxation for vehicular and RedCap UE such that vehicular and Redcap UE is only mandated to support 2Rx ports in NR Bands n7, n38, n41, n77, n78, and n79. Following is the quote from TS38.101
It is crucial for 3GPP to support a new type of devices, such as XR wearable considering the following factors
  4Rx antennas may not be feasible due to the form factor limitation
  Large BW (e.g., 100MHz in FR1) and CA is feasible and important for high demanding XR services
  Detailed explanation and analysis can be found in RP-223207.
“Vehicular UE: A UE embedded in a vehicle, permanently connected to an embedded antenna system that radiates externally for NR operating bands. NOTE: Vehicular UE does not refer to other UE form factors placed inside the vehicle. NOTE 1: Four Rx antenna ports shall be the baseline for this operating band except for two Rx vehicular UE. Four Rx antenna ports for RedCap UE is not supported for this operating band.”