## Slide 1: Moderator's summary of discussion [98e-05-R18-NES] Final Summary
3GPP RAN WG1 Chair
Younsun Kim
RP-223538

## Slide 2: What was handled in [98e-05-R18-NES]
Contributions in RP-222902, RP-222919, RP-222974, RP-222990, RP-223003, RP-223004, RP-223021, RP-223031, RP-223043, RP-223131, RP-223162, RP-223182, RP-223188, RP-223200, RP-223224, RP-223241, RP-223335, RP-223340, RP-222914, RP-222988, RP-223084, RP-223094, RP-223152, RP-223261
Flag on Rel-18 network energy savings study item status report in RP-223002
Discussion and approval of work item on Rel-18 network energy savings
The following slides summarize the outcome of the discussions on [98e-05-R18-NES]

## Slide 3: Extending the study on Rel-18 NES
The following alternative was agreed with regards to the discussion on whether/how to have additional study on NES techniques.
Flag on Rel-18 network energy savings study item status report in RP-223002 was resolved after taking Alternative 3 and confirmation on the Rel-18 schedule
Alternative 3
  Start the normative work on network energy savings in 2023.Q1. There is no extension on the study of network energy savings techniques.

## Slide 4: RAN1-led: Spatial and power domain NES enhancements
The following WID objective was endorsed in the Wednesday GTW session
Proposal 1
  Specify necessary enhancements on CSI and beam management related procedures including measurement and report, and signaling to enable efficient adaptation of spatial elements (e.g. antenna ports, active transceiver chains) [RAN1, RAN2]
  Specify necessary enhancements on CSI related procedures including measurement and report, and signaling to enable efficient adaptation of power offset values between PDSCH and CSI-RS [RAN1, RAN2]
  Note: Above objectives are only for UE specific channels/signals
  Note: Legacy UE CSI/CSI-RS capabilities applies when considering total number of CSI reports and requirements

## Slide 5: RAN2/RAN3-led enhancements (1/2)
The following WID objectives were endorsed in the Wednesday GTW session
Proposal 3
  Specify mechanism(s) to prevent legacy UEs camping on cells adopting the Rel-18 NES techniques, if necessary [RAN2]
  Specify inter-node beam activation and enhancements on restricting paging in a limited area [RAN3]
Proposal 5
  Specify CHO procedure enhancement(s) in case source/target cell is in NES mode [RAN2]

## Slide 6: RAN2/RAN3-led enhancements (2/2)
The following WID objectives were endorsed by email
Proposal 4
  Specify SSB-less SCell operation for inter-band CA for FR1 and co-located cells, if found feasible by RAN4 study, where a UE measures SSB transmitted on PCell or another SCell for an SCell’s time/frequency synchronization (including downlink AGC), and L1/L3 measurements, including potential enhancement on SCell activation procedures if necessary [RAN4, RAN2]
Proposal 2
  Specify enhancement on cell DTX/DRX mechanism including the alignment of cell DTX/DRX and UE DRX in RRC-CONNECTED mode, and inter-node information exchange on cell DTX/DRX [RAN2, RAN1, RAN3]
    Note: No change for SSB transmission due to cell DTX/DRX
    Note: The impact to IDLE/INACTIVE UEs due to the above enhancement should be avoided

## Slide 7: Work Item
The endorsed work item on Rel-18 network energy savings is in RP-223540.