## Slide 1
RAN WG3 Chair: Yin Gao
RAN WG3 Vice-Chairs: Angelo Centonza, Gen Cao
RAN3 Secretary: Seonggu Shim
Status Report for RAN WG3
3GPP TSG RAN #99, Rotterdam, Netherlands
March 20th – 23th, 2023
RP-230007

## Slide 2: Executive Summary
Total 721 Tdocs at submission deadline (excluding LSin received from other groups) in Q1
  9% LSs and related documents
  25% Maintenance: Rel-17 & earlier
  4% Corrections and enhancements: Rel-18
  62% Documents to Rel-18 WIs/SIs
Updated endorsed guidelines for f2f meeting with remote access: R3-230106
TR30.531 Work Plan and Working Procedures - RAN WG3 was updated and approved in R3-230797
The R18 NR NCR WI (led by RAN1) was completed in RAN3.
LS on required normative work for SA2 related Rel-18 topics to RAN agreed in R3-230954.
RAN3#119 | Feb 27th – Mar 3rd, 2023 Athens, Greece
RAN #99 | Mar 20th – 23th, 2023

## Slide 3: Tdoc submitted to RAN3
The total number of contributions around 700 for each RAN3 meeting is affordable
Notes: w

## Slide 4: Tdocs for each Topic

## Slide 5: Overview of RAN3-led Rel-18 NR SI/WIs
UID | Name (acronym) | Acronym | Target completion | Old % (the same as in WI/SI SR) | WID | New % | Change or comments
941009 | Mobile IAB (Integrated Access and Backhaul) for NR WI | NR_mobile_IAB | 23/12/2023 | 20% | WID: RP-222671 | 40% | RAN3 provides the answer to SA2’s requests on points #1, #2, #6, and #7 in the reply LS agreed in R3-231011
941008 | Enhancement on NR QoE management and optimizations for diverse services WI | NR_QoE_enh | 23/12/2023 | 30% | WID: RP-223488 | 40% | From RAN3 perspective, there is no need to send assistance information to UE upon RAN overload, LS was agreed in R3-231028
941010 | Artificial Intelligence (AI)/Machine Learning (ML) for NG-RAN WI | NR_AIML_NGRAN | 23/06/2023 | 30% | WID: RP-220635 | 45% | 
941007 | Further enhancement of data collection for SON (Self-Organising Networks)/MDT (Minimization of Drive Tests) in NR standalone and MR-DC (Multi-Radio Dual Connectivity) WI | NR_ENDC_SON_MDT_enh2 | 23/12/2023 | 30% | WID: RP-221825 | 40% | 
940088 | Enhancement for resiliency of gNB-CU-CP SI | FS_gNB_CU_CP_resiliency | 22/09/2022 | 100% | SID: RP-221438 SR: RP-222250 |  | 
WI: Black SI: Blue Completed WI/SI: Red

## Slide 6: RAN3 CRs to RAN
List of RAN3 CRs to RAN in RP-23xxxx, which includes:
  83 CRs were agreed in Q1.
  1 Rel-15 Cat.F CR
  15 Rel-16 Cat.F CRs, 1 Cat. A CR
  66 Rel-17 CRs: 14 Cat.A CRs, 50 Cat.F CRs, 2 Cat.B CR
    2 Cat.B:
      R3-230909 Introduction of two PHR mode [NR_feMIMO-Core]
      R3-230907 Missing transmission bandwidth configurations in F1AP [NR_FR1_35MHz_45MHz_BW]
    18 Non-Backwards-Compatible (NBC) CRs for Rel-16 and Rel-17
    R3-230213, R3-230214, R3-230981, R3-230982, R3-230501, R3-230502, R3-231016, R3-230472, R3-231002, R3-230311, R3-230828, R3-230295, R3-230296, R3-230297, R3-230881, R3-230911, R3-230940, R3-230830
    (Here is how 3GPP works with NBC changes)
  5 endorsed draftCRs to RAN2 specs.
  Heavy TEI handling in this meeting!

## Slide 7: Experience for GTW Usage in f2f meeting
RAN3 had one meeting room for main session, it costed time to find the shared breakout room with other WGs before the meeting. RAN3 continued to use the shared breakout room with RAN2 and maintained the time slot table for the shared breakout room during the meeting week. RAN3 needs a seperate breakout room for f2f meeting.
The voice quality of microphone used by delegates in the meeting was not friendly to remote participants in the first two meeting days. In general, the number of remote participants for main session is limited, less than 20.
The audio device test for remote access needs to be performed before daily session starts.
MCC and IT support during the meeting is sufficient.

## Slide 8: R18 SON/MDT WI
Progress in the last quarter
For SHR and SPCR:
  RAN3 sees benefits to support inter-RAT SHR from LTE to NR for T304 trigger with no impact on LTE in Rel-18.
  Take Option 3 (The receiving node forwards the inter-RAT SHR to corresponding node which generates the SHR trigger condition that triggers the inter-RAT SHR) as baseline for SHR forwarding mechanism in Rel-18.
  For classic addition/CPA, SN- and MN-initiated classic PSCell change/CPC, the target SN node decides the T304 trigger and performs root cause analysis.
  For intra-SN classic PSCell change/CPC, the source SN decides SPR triggers of T310 and T312 and performs root cause analysis.
  If the trigger is T312/310, the objective of SPR is to optimize lower layer issues of source PSCell and to optimize PSCell change configuration during mobility.
  If the trigger is T312/310, for MN-initiated classic PSCell change/CPC, at least the MN who sent the SPR configuration to the UE is involved in SPR related optimizations.
For MRO:
  Update the definition to wrong PSCell change/addition should be splitting to sub cases: 1) the wrong candidate cell comes from the cell in the list provided by the initiating node or 2) the wrong candidate cell is selected by the target node.
  Information available in the network nodes should not be included in the SCGFailureInformation.
  Reusing R17 signalling mechanism to report CPA/CPC failure/ related information over Xn from MN to source SN or last serving SN.
  Sub-Case b1/Sub-Case b2 would not be considered for MRO for fast MCG recovery failure.
  For MRO for CPC and CPA, if there are multiple events configured for CPA/CPC, the UE reports the first triggered CPAC event, and the time duration between the two triggered CPAC events.
  It is beneficial for the UE to report at least PSCell where SCG failure happened, the cause of the fast MCG recovery failure (at least T316 expiry, SCG failure, SCG was deactivated or other cases that SCG is not available), and also if the problem is SCG failure, the SCG failure type (at least t310-Expiry, randomAccessProblem, rlc-MaxNumRetx).

## Slide 9: R18 SON/MDT WI
Progress in the last quarter
For RACH enhancement:
  Using non-UE associated sigalling for RACH Indication over F1.
For SON/MDT Enhancements for Non-Public Networks:
  Agree to the addition of a CAG list inside and outside the current choice structure for the MDT Area Scope
For SON for NR-U:
  DU shall report the UL COT to CU in resource status report procedure when it is requested by CU, how to obtained this information by DU is up to implementation.
  The granularity of UL COT reporting in F1 interface should be NR-U channel level.
Next steps
Continue to work on stage2 and stage3.

## Slide 10: R18 QoE WI
Progress in the last quarter
No RRC state info when UE collects the uploaded QoE data for MBS BC. FFS for MBS MC.
MBS BC QoE measurements can proceed after UE switches from IDLE/INACTIVE to CONNECTED.
At least QoE reference and MCE info shall be available in the new gNB.
If the SN is interested in configuring a UE with an m-based QoE measurement configuration, it should send the request to the MN via a UE-associated procedure.
The MN should inform the SN that a UE is configured with an m-based QoE measurement.
For an m-based QoE configuration in the case SN is interested in configuring a UE with an m-based QoE measurement configuration, the MN can decide and notify the SN whether:
The MN shall send the configuration information to the UE, or
The SN should send the configuration to the UE directly, or
The SN should send the configuration information to the UE via the MN (inside a container).
The MN is responsible for RRC ID allocation for m-based sessions configured by the MN or SN, and notifies the allocated RRC ID(s) to the SN.
To determine which node(s) provide the bearers carrying an application session, a node can configure RVQoE measurements at a UE in NR-DC:
For the first RVQoE configuration, it is blindly configured by MN or SN.
From the PDU session ID and QFI in the first RVQoE report this node determines which node(s) provide the bearer(s) associated to the corresponding application session.
After the node determines which node(s) carry the session including bearer type change, the RVQoE configuration may be modified.
If a node receives an RVQoE report from a UE in NR-DC, and determines that the bearers for the application session are also or only provided by the peer node, this node can send the received RVQoE report to the peer node.

## Slide 11: R18 QoE WI
Progress in the last quarter
Turn WA to agreement: SN can send an RVQoE configuration to the UE.
RAN3 to await the further progress of SA4 and ITU-T before proceeding further on the topic of RVQoE value.
In case assistance information for handling of QoE reporting upon RAN overload is sent to the RAN, it is sent together with QoE measurement configuration. RAN3 to further discuss what the assistance information is. From RAN3 perspective, there is no need to send assistance information to UE.
Introduce the deactivation of RAN visible QoE information transfer via F1. No need to introduce pause/resume mechanism in Release 18.
Impacts and dependencies on other WGs
The agreement on assistance information for RAN overload handling in RAN3 would have impact on RAN2 discussion.
Next steps
Further discussion on other QoE configuration info for MBS BC QoE shall be available in new gNB.
Further discussion on how to support the high mobility scenario and the new QoE service types.
Further discussion on whether/how to enhance the QoE area scope for MBS.
Further discussion on the reporting leg switch of QoE and/or RVQoE in NR-DC.
Further discussion on mobility senario, MDT and QoE alignment in NR-DC.
Further discuss the assistance information for RAN overload, and DU participation for RVQoE measurement and reporting.
Further work on stage-2 and stage-3 details in this WI.

## Slide 12: R18 AI RAN WI
Progress in the last quarter
Solutions for AI/ML information exchange over the NG interface are not considered as part of Rel-18.
The agreed class1 procedure (AI/ML INFORMATION REQUEST/RESPONSE, the name needs further discussion) is used to configure UE performance feedback reporting.
Introduce into the agreed new request message (AI/ML INFORMATION REQUEST, the name needs further discussion), an indication that UE performance feedback is provided after handover event. Whether the indication is in implicit or explicit way needs to be further discussed.
Introduce a trigger indication in the HO request message to indicate that UE performance feedback is requested after HO completion. The details of indication need to be discussed.
The agreed new class2 non-UE associated procedure (AI/ML INFORMATION UPDATE, which name is FFS) is used for UE performance feedback reporting.
Partial reporting mechanism is supported in the agreed AI/ML information procedures (AI/ML INFORMATION REQUEST/RESPONSE/UPDATE, which name is FFS). The solutions need to be discussed.
For AI/ML based mobility optimization:
There is no need to include predicted RRC state in the cells in the predicted UE Trajectory in this release.
There is no need to include beam index information in the predicted UE Trajectory in this release.
For AI/ML based Energy Saving:
Introduce the metric of Energy Cost (EC) as the AI/ML metric to be shared over the Xn interface among gNBs.
The metric of Energy Cost (EC) exchanged between NG-RAN nodes can be an inferred energy consumption related to an additional load or an actual energy consumption value from a neighboring node for either additional load or current load (The details to be further discussed). EC is a value at gNB level.

## Slide 13: R18 AI/ML for NG-RAN
Progress in the last quarter
For MDT enhancment:
WA: There are the benefits in enabling UEs to continuously collect MDT measurement across RRC states and to provide to the network such continuous time series of data for the purpose of AI/ML Training/Retraining. The evaluation of gains vs impacts related to the use cases in R18 coming from potential solutions needs to be further discussed.
Next steps
Continue the discussion on the presence of Predicted Time UE Stays in Cell.
Further discussion on whether predicted UE Trajectory spans across multiple NG-RAN nodes or it is limited within a single target NG-RAN node.
Further discussion on the details of UE performance feedback procedure and partial reporting mechanism.
Continue to work on stage2 and stage3.

## Slide 14: R18 mobile IAB WI
Progress in the last quarter
With respect to mobile IAB, for issues concerning the control of UE access to MBSR using CAG function no enhancement is needed and no replies are foreseen from RAN3 on this matter.
NGAP Initial Context Setup Request, UE Context Modification Request and HO Request to include an IE with code points “mobile-IAB authorized”, “mobile-IAB not-authorized”.
When triggering the F1 Setup procedure on the mIAB-node, the source logical mIAB-DU’s CU to include the information of target logical mIAB-DU’s CU (e.g. IP address, gNB-ID).
The IAB-node can inform the source logical mIAB-DU’s CU via F1AP about the successful F1 Setup with the target logical mIAB-DU’s CU, and it can include the IDs of the cells activated by the target logical mIAB-DU’s CU.
In case the target logical mIAB-DU’s CU is different from the mIAB-MT’s CU, the target logical mIAB-DU’s CU needs to be informed about the mIAB-MT’s CU ID and the mIAB-MT ID so that it can initiate the Xn TMM procedures towards mIAB-MT’s CU.
The HO of UEs from the source logical mIAB-DU′s CU to the target logical mIAB-DU′s CU should happen after the completion of the F1 setup. When to trigger the HO is up to source logical mIAB-DU′s CU implementation.
After all UEs have been handed over, the source logical mIAB-DU’s F1AP association can be released by the source logical mIAB-DU or by the source logical mIAB-DU’s CU.
Target donor CU selection for mIAB-DU migration and triggering conditions for F1 setup can be up to source CU implementation (unless it is justified that this is not possible) or based on OAM configuration at the source CU.
RAN3 not to work on solutions addressing use cases where inter donor IP connectivity is not available.
Capture on stage 2 that the TAC/RANAC broadcast by the mobile IAB-DU can be changed in order to reflect the mIAB-node’s physical location.

## Slide 15: R18 mobile IAB WI
Impacts and dependencies on other WGs
The reply LS to SA2 on FS_VMR is agreed in R3-231011.
Next steps
With respect to mIAB-DU migration and partial migration, RAN3 to discuss how the mobile IAB-DU’s parameters are (re-)configured.
It needs to be further discussed how the mobile IAB-DU’s TAC/RANAC is changed and what Stage 3 impacts are (if any).
For scenarios without Xn, RAN3 to investigate whether IAB-related Xn signaling for partial migration and DU migration can be carried via NG using a container to avoid the impact on the AMF.

## Slide 16: R18 Mobility Enh. WI
Progress in the last quarter
For intra-DU LTM, the gNB-CU assigns a new UL GTP TEID for each DRB and provides it to the gNB-DU via UE Context Modification Request message(s). The gNB-DU assigns the new DL GTP TEIDs per DRB per candidate cell (whether it should be per candidate cell needs to be further discussed) and provides them back to the gNB-CU in UE Context Modification Response message(s).
For inter-DU LTM, the gNB-CU assigns a new UL GTP TEID for each DRB and provides it to the target gNB-DU via UE Context Setup Request message(s). The target gNB-DU assigns the new DL GTP TEIDs per DRB per candidate cell (whether it should be per candidate cell needs to be further discussed) and provides them back to the gNB-CU in UE Context Setup Response message(s).
Intra-CU UP case: CU will start data transmission after LTM cells switch signaling from DU including target cell ID.
Confirm the early data forwarding for CHO with multiple SCGs is a new problem.
Enhance XnAP and F1AP signaling to support NR Selective Activation.
Introduce a new indicator to the S-NODE ADDITION REQUEST message over Xn to indicate that the request is for Selective Activation.
Impacts and dependencies on other WGs
More RAN2 input is expected and helpful.
Next steps
Continue to work on stage2 and stage3.

## Slide 17: R18 MBS WI
Progress in the last quarter
Progress based on SA2 result on both multicast reception for UE in RRC_INACITVE, and network sharing for broadcast. (with LS back and forth)
For MOCN, it is up to NG-RAN node implementation to decide how many NG-U tunnels to be setup.
For MOCN, It is up to the NG-RAN node implementation on how to handle different S-NSSAI received for the same shared service from different PLMNs (i.e. same Associated Session ID).
Transfer the Associated Session ID together the MBS Session ID.
Support a per UE per MBS session indication from CN to RAN.
Stage 2 BL CR agreed accordingly.
Impacts and dependencies on other WGs
Potential dependency on SA2 on both multicast reception for UE in RRC_INACITVE, and network sharing for broadcast, e.g., interpretation on the assistant info from 5GC, and the Associated Session ID.
RAN2 on how PTM configuration is delivered to UE on Uu, to support multicast reception for UE in RRC_INACITVE; and how mobility is supported across cell and nodes, how UE is notified upon events, including e.g., session status change.
Next steps
Further study on whether the indication from 5GC at least means that the UE is preferred to be kept in RRC_CONNECTED.
Further study on the granularity of Associated Session ID, per TMGI or per TMGI per Area Session ID.
Further study the RAN sharing case with multiple cell ID.
Further study multicast reception for UE in RRC_INACTIVE based on RAN2 progress.
Stage 3 (based on companies TP).

## Slide 18: R18 Sidelink Relay WI
Progress in the last quarter
NG-RAN receives the multi-path authorization from the AMF. The multi-path authorization can be added in the 5G ProSe Authorized IE if it is needed.
Endorsed R3-230896(NGAP)/R3-230897(XnAP)/R3-230898(F1AP) as BL CR.
During direct to indirect and indirect to indirect path switch procedures, the source gNB sends a list of candidate relay UEs belonging to the same target cell in the HO REQ message.
At least Remote UE L2 ID and a list of candidate target relay UE IDs should be included in the XnAP HANDOVER REQUEST message.
Add Inter-DU Direct Path Addition and Inter-DU Indirect Path Addition procedures in TS 38.401. FFS on other procedures.
Turn the following WAs into agreement.
  WA: The direct path and indirect path cannot be configured for a remote UE simultaneously in this release, depending on RAN2 decision.
  WA: For inter-DU case, legacy DC based data split/duplication mechanism can be reused as baseline for split DRB/SRB.
  WA: The RAN3 will specify the details of the path change procedure after introducing the procedure of the direct/indirect path addition.
Next steps
Stage-3 details can be figured out next meeting, for example, whether the Remote UE L2 ID is already included in the inter-node message.
Following legacy HO procedure, RAN3 does not set any restriction on whether the target candidate relay UEs belong to the same target gNB or not. The same applies for the target cell.
Continue to work on stage2 and stage3.

## Slide 19: R18 NR NTN WI
Progress in the last quarter
Turn WA into agreement: The Uu cell ID is used as target cell ID in the handover signaling.
Introducing time-based parameters for NG HO follows legacy CHO configuration over Uu interface without any RAN2 impact.
Next steps
Whether to use Uu cell ID or mapped cell ID over Xn configuration update procedure.
The idea of the solutions to support time-based NG HO needs to be further checked.

## Slide 20: R18 IoT NTN WI
Progress in the last quarter
There is no need to enhance the existing S1AP procedure to support the tracking area reported by RAN before AN release.
The time-based CHO over X2 should be supported.
Next steps
Further discuss the potential RAN3 impact based on the progress in SA2 if any.
Align with the progress in NR NTN WI.

## Slide 21: R18 UAV WI
Progress in the last quarter
NULL
Next steps
Proper TU allocation in RAN3 to be discussed.

## Slide 22: R18 NR MT-SDT WI
Progress in the last quarter
RAN3 starts to initiate NR MT-SDT WI.
MT-SDT can be triggered by DL SDT user data and/or DL SDT signalling.
Upon reception of DL SDT user data, the gNB-CU-UP may include the assistance information (e.g., Data size) in E1AP DL Data Notification message to gNB-CU-CP. FFS on MT-SDT indicator.
When receiving DL SDT data, the anchor gNB may send MT-SDT information IE to the neighbour gNBs within the RNA, via XnAP RAN paging message. The encoding and the name of MT-SDT information IE is FFS.
The gNB that receives MT-SDT information within the RNA takes into account this information received in the XnAP RAN PAGING message from the anchor gNB to decide whether to trigger MT-SDT Uu paging.
Upon reception of MT-SDT information via XnAP RAN paging message from the anchor gNB-CU, the gNB-CU may send F1 MT-SDT information to the gNB-DU via F1AP Paging message. FFS on F1AP MT-SDT information.
BLCRs are allocated and TPs are agreed.
Impacts and dependencies on other WGs
More RAN2 input is expected and helpful.
Next steps
Continue to work on stage2 and stage3.

## Slide 23: R18 NR NCR WI
Progress in the last quarter
The NCR may be configured with a list of allowed and/or forbidden cells.
RAN validation is not supported in R18.
The NG-RAN node selects an appropriate AMF for a NCR accesses to the network with the assumption that the NCR indication is received from NCR in MSG5.
gNB-CU shall indicate the NCR authorization info explicitly to gNB-DU once a NCR device is authorized by UE context setup request message and UE context modification request message.
Stage3 CRs for TS 38.473 and TS 38.401 have been approved. Stage 2 pCR for TS 38.300 has been endorsed.
Impacts and dependencies on other WGs
The WI is completed from RAN3 perspective.
Next steps
RAN3 may further discuss NCR aspects based on other WGs processing.

## Slide 24: R18 NR Network ES WI
Progress in the last quarter
Support beam level activation over Xn and F1.
Impacts and dependencies on other WGs
Discuss cell DTX/DRX according to the progress on RAN1 and RAN2.
Next steps
Further discuss procedure and signaling enhancements on beam level activation.
Further discuss paging enhancements for network energy saving.

## Slide 25: TEI Corrections
Progress in the last quarter
R17 MBS corrections:
  Corrections made to F1AP/E1AP (e.g., MBS QoS Flow Information provisioning, misc correction), and TS 38.401 (e.g., broadcast session establishment)
  LS among WGs (e.g., SA2, CT4, RAN Plenary, SA Plenary) on leftover issues (e.g., shared NG-U tunnel applicability to broadcast)
  potential PDCP issues and the impacts to network interface are to be continued.
R17 Positioning corrections:
  Enhance the NRPPA POSITIONING INFORMATION UPDATE message to indicate that the UE is no longer transmitting UL SRS.
  Stage2 corrections on adding SRS configuration text.

## Slide 26: TEI Corrections
Progress in the last quarter
R17 SONMDT corrections:
  Corrections made to NGAP (e.g., user consent in PATH SWITCH REQUEST ACKNOWLEDGE message, SON Configuration Transfer)
  Corrections made to XnAP(e.g., MDT Configuration-EUTRA IE, MDT Configuration-NR IE,FAILURE INDICATION, Slice Available Capacity tabular alignment,MDT activation, MDT area scope)
  Corrections made to F1AP (e.g., M6 Configuration,NR-U Channel ID)
  Corrections made to E1AP (e.g., Mandatory extension container in E1AP Resource Status Update)
R17 SCG and CPAC corrections:
  Completion of the work on CHO-CPC coordination, corresponding CRs are agreed and endorsed.
  Clarifications on prepared PSCell addition by candidate SN, draftCR to TS37.340 is endorsed.
  Correction to conditional MCG configuration in CPAC , F1AP CR is agreed.
  Additional, some CRs for detailed correction are also agreed.

## Slide 27: My Heartfelt Thanks To:
Angelo Centonza, Gen Cao (RAN WG3 Vice-Chairs)
  For chairing the corresponding sessions and all the support during the meeting!
Seonggu (RAN WG3 Secretary)
  For impressive hard work and completion of his first RAN3 meeting challenge as RAN3 secretary, which is not an easy job!
Philippe G, Chenghock, Miaoqi, Mingzeng, Geetha, Jiajun, Hongzhuo
  For their positive and hard work on moderating some tough email discussions and good support!
All rapporteurs and moderators
  For their efforts to R18 WIs/SIs and R17 maintenance!
  Work on RRC container reference cleanup
All RAN3 delegates
  For their positive, constructive and cooperative spirit and patience!