## Slide 1: Views on the scope of XR WI
March , 2023
3GPP TSG RAN Meeting #99
RP-230123
Agenda Item: 9.3.2.9
Source: Xiaomi
Document for : Discussion and decision

## Slide 2: Summary of Rel-18 SI on XR
In RAN2#121 meeting, RAN2 considers the Rel-18 XR SI complete.
RAN is suggested to consider updating the following objectives for XR Awareness:
Specify the enhancements related to power saving: - DRX support of XR frame rates corresponding to non-integer periodicities (through at least semi-static mechanisms e.g. RRC signalling) (RAN2). Specify the enhancements related to capacity: - Multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration (RAN1, RAN2); - Dynamic indication of unused CG PUSCH occasion(s) based on UCI by the UE (RAN1); - BSR enhancements including at least new BS Table(s); (RAN2); - Delay reporting of buffered data in uplink; (RAN2); - Provision of XR traffic assistance information for DL and UL (e.g. periodicity); (RAN2); - Discard operation of PDU Sets (RAN2); Specify the enhancements for XR Awareness (RAN2, RAN3): TBD (detailed objectives will be further clarified at RAN#99 based on the conclusions of TR38.835, and work to be started only after RAN#99) Note: Impacts to RAN3 will be assessed at RAN#99

## Slide 3: Discussing on WID scope of XR-awareness (1)
  In RAN2#121 meeting, RAN2 discussed the UL jitter and thinks UL jitter may be present for XR (e.g. for tethering use cases). It is unclear how network would use UL jitter information.
  In our understanding, UL jitter is not taken into account in Rel-18 XR WI for the following reasons:
      It is difficult to identify characteristics for UL jitter since it heavily depends on how the tethered device(s) are connected to UE, e.g., WIFI, bluetooth. Coordination with SA WG4 might be needed.
      In SA2, Round-Trip latency requirements only considers the latency between UE and N6 termination point at the UPF and UL jitter is not taken into account.
      =>Xiaomi’s view:
      In the WI phase, UL jitter is not taken into account Rel-18 XR.

## Slide 4: Discussing on WID scope of XR-awareness (2)
  In RAN2#120 meeting, RAN2 has agreed to support timer-based discarding of UL transmit side of PDCP PDU/SDUs of a PDU set. FFS how this is modelled in PDCP specification, can be discussed in WI phase.
  In RAN2#121 meeting, RAN2 aims to introduce a mechanism to allow UE to handle discarding of packets with different PSI in case of congestion. FFS for other cases.
  According to the defemination of PHISI(When the PSIHI is set for a QoS flow, as soon as one PDU of a PDU set is known to be lost, the remaining PDUs of that PDU Set can be considered as no longer needed by the application and may be subject to discard operation), discarding of a PDU within a PDU set also happens when a PDU loss due to unsuccessful delivery over air interface.
  In RAN2#121 meeting, RAN2 has no intention to pursue PDU prioritization which should not be in the WID scope.
  In RAN2#121 meeting, RAN2 has no intention to support of RLC bearer splitting based on new XR-specific functionality which should not be in the WID scope
      =>Xiaomi’s view:
      RAN is suggested to specify discard operation of PDU Sets (e.g., timer-based discarding, PSI-based discarding in presence of congestion, unsuccessful delivery -based discarding).

## Slide 5: Discussing on WID scope of XR-awareness (3)
  According to the conclusion of SA2’s TR 23.700-60 v18.0.0, the following aspects are identified with RAN impacts for XR-awareness in NG-RAN:
      For RAN information exposure in SA2‘s KI#3, RAN3 needs to discuss how to measure the congestion and how to exposure the congestion information to the 5GC.
      For PDU Set based QoS handling in SA2’s KI#4 and KI#5, RAN3 needs to discuss how to support and handle the PDU set QoS parameters in Control Plane and PDU Set related information in User Plane.
      For XR power saving SA2’s Ki#8, RAN3 needs to discuss the signalling support of transmission of assistance information from 5GC to NG-RAN.
      =>Xiaomi’s view:
      For RAN3’s objectives, it’s suggested to focus on the following aspects.
      Support of RAN information exposure, including congestion information, etc..
      Support of PDU Set based QoS handling, including control plane and user plane enhancement.
      Signalling support of assistance information from 5GC to NG-RAN for XR power saving.

## Slide 6: Summary
  Proposal 1: RAN is suggested to consider updating the following objectives for Rel-18 XR WID:
Specify the enhancements related to power saving: - DRX support of XR frame rates corresponding to non-integer periodicities (through at least semi-static mechanisms e.g. RRC signalling) (RAN2). Specify the enhancements related to capacity: - Multiple CG PUSCH transmission occasions in a period of a single CG PUSCH configuration (RAN1, RAN2); - Dynamic indication of unused CG PUSCH occasion(s) based on UCI by the UE (RAN1); - BSR enhancements including at least new BS Table(s); (RAN2); - Delay reporting of buffered data in uplink; (RAN2); Provision of XR traffic assistance information for DL and UL (e.g. periodicity); (RAN2); - Discard operation of PDU Sets (RAN2); Specify the enhancements for XR Awareness (RAN2, RAN3): - Discard operation of PDU Sets (RAN2, RAN3); - Support of RAN information exposure, including congestion information, etc., as required by other WGs (RAN3); - Support of PDU Set based QoS handling, including control plane and user plane enhancement (RAN3); - Signalling support of assistance information from 5GC to NG-RAN for XR power saving (RAN3).

## Slide 7
THANKS!