## Slide 1: Discussion on Rel-18 NR sidelink evolution
NTT DOCOMO, INC.
3GPP TSG RAN #99
Rotterdam, Netherlands, March 20th - 23rd, 2023
Agenda Item: 9.3.1.5
Document for: Decision
RP-230357

## Slide 2: Background
WID description (RP-222806)
4 Objective 4.1 Objective of SI or Core part WI or Testing part WI Specify mechanism to support NR sidelink CA operation based on LTE sidelink CA operation [RAN2, RAN1, RAN4] (This part of the work is put on hold until further checking in RAN#99) Support only LTE sidelink CA features for NR (i.e., SL carrier (re-)selection, synchronization of aggregated carriers, handling the limited capability, power control for simultaneous sidelink TX, packet duplication) The work is limited to FR1 licensed spectrum and ITS band in FR1. No specific enhancements of Rel-17 sidelink features with sidelink CA support. This feature is backwards compatible in the following regards A Rel-16/Rel-17 UE can receive Rel-18 sidelink broadcast/groupcast transmissions with CA for the carrier on which it receives PSCCH/PSSCH and transmits the corresponding sidelink HARQ feedback (when SL-HARQ is enabled in SCI) …

## Slide 3: Discussion
Checkpoint for SL-CA, Discussion of scope
  There would be no/little room to add another objective
    SL-U/Coex/SL-FR2 were discussed at WG meetings so far. It seems that SL-U/Coex requires most time from the allocated TUs to complete specifying these topics in Rel-18. Rather, it is questionable whether SL-U/Coex can be completed, e.g., within 3 meetings for RAN1
    All the remaining time will be consumed for SL-FR2 study
  Discussion on WI scope is required
    Based on the above situation, at least SL-CA should be dropped from Rel-18 SL evo WI
    For SL-U, it seems that there are a lot of discussion topics including non-essential features (e.g., FBE, contiguous RB-based structure, 60 kHz SCS, OCB exemption, etc.). RAN guidance to deprioritize one or more of these features is desirable
    For coex, meanwhile, an essential topic - higher SCS support - has been blocked on the grounds of RAN1 workload. Higher SCS is a key feature compared to LTE-SL. RAN guidance makes them possible to support this essential feature and to avoid increase of RAN1 workload

## Slide 4: Discussion
  Proposal: For NR sidelink evolution,
  SL-CA is dropped from Rel-18
  Discuss to deprioritize some features for SL-U
  Conclude that RAN1 specify LTE/NR coexistence for NR higher SCS with the following as discussed in RAN1#112
    NR SL UE can use a NR resource if the NR transmission is not overlapped in time with any LTE reserved resource, or if starting timing of the first symbol is aligned with that of LTE reserved resource(s) overlapped in time
    NR SL UE does not use a NR resource if starting timing of the first symbol is not aligned with that of LTE reserved resource(s) overlapped in time, and if the previous NR resource(s) in the same frequency resources that is overlapped with the same LTE reserved resource(s) in time will not be used by the NR SL UE
    Note: Minimum specification impact is assumed