## Slide 1
3GPP TSG RAN Meeting #99 RP-230498
Rotterdam, NL, March 20-23, 2023
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.3.1.7
Discussion on missing RLM/BFD relaxation requirements for RedCap UEs

## Slide 2
In Rel-17 UE power saving enhancements WI, RLM/BFD relaxation is specified and applicable for both non-RedCap UE and RedCap UE
In Rel-17 RedCap WI, RAN4 discussed whether and how to specify RLM/BFD relaxations from Rel-17 UE power-saving enhancements WI for Redcap UEs. However, it is understood that the relaxed RLM/BFD requirements are not yet specified for Redcap.
In Rel-18 Redcap enhancement WI scope, RAN4 has the following objectives:
    Power saving/energy efficiency enhancements
      Enhanced eDRX in RRC_INACTIVE (>10.24s) [RAN2, RAN3, RAN4]
    Complexity/cost reduction
      Further reduced UE complexity in FR1 [RAN1, RAN2, RAN4]
On RRM aspects, small specification work is expected, while total 2.25TU is reserved for R4RD.
    At RAN4#106 meeting (R4-2303259), the mainly identified RRM impact is to specify requirements for eDRX cycle > 10.24 sec in FR1 and FR2.
    It was agreed that no RRM impact from the UE peak data rate reduction for FR1.
    It is expected that RRM impact due to baseband reduction is not big given the 5MHz BB bandwidth is only applied to data channels (PDSCH/PUSCH) for Rel-18 eRedCap.
  RLM/BFD relaxation requirements for RedCap UEs

## Slide 3
Observation:
    The RRM scope for Rel-18 RedCap enhancement is limited, while affluent TU for R4RD is reserved, i.e., 0.5 TU per meeting is allocated from RAN4 106bis to RAN4 109.
    Rel-17 RLM/BFD relaxation requirements are still missing although it should be applicable to RedCap UEs.
Proposal 1: Update Rel-18 Redcap enhancement WI scope to include the following objective:
    Specify the RLM/BFD relaxation requirements for RedCap UEs in Rel-18 RedCap enhancement WI. [RAN4]
Proposal 2: To specify the RLM/BFD relaxation requirements for RedCap UEs in Rel-18 RedCap enhancement WI without TU increase.
  RLM/BFD relaxation requirements for RedCap UEs