## Slide 1: Discussion on user virtualization and collaboration
Source: ZTE, Sanechips
Agenda: 9.13
3GPP TSG RAN Meeting #99
Rotterdam, Netherlands, March 20– 23, 2023
RP-230626

## Slide 2
The UE aggregation has been studied in R18 where the UE is connected to the network via direct path and via another UE using a non-standardized UE-UE interconnection as shown below [1].
However, this is far from enough. R18 UE aggregation is based on PDCP layer for intra-gNB scenario. The inter-gNB scenario, the service continuity for mobility scenario, the aggregation with more than two UEs as well as aggregation at lower layer have not been touched.
On the other hand, more UE collaboration scenarios are emerging which require multiple devices to form a virtual user and these devices can collaboratively transmit and receive data from the network.
[1] RP-223501 Revised WID on NR sidelink relay enhancements.
This multi-path relay solution can also be utilized to for UE aggregation where a UE is connected to the network via direct path and via another UE using a non-standardized UE-UE interconnection. UE aggregation aims to provide applications requiring high UL bitrates on 5G terminals, in cases when normal UEs are too limited by UL UE transmission power to achieve required bitrate, especially at the edge of a cell. Additionally, UE aggregation can improve the reliability, stability and reduce delay of services as well, that is, if the channel condition of a terminal is deteriorating, another terminal can be used to make up for the traffic performance unsteadiness caused by channel condition variation.
Motivations

## Slide 3
IIoT scenario
  Multiple coordinative devices (e.g., monitors) are connected together.
  Collaborative transmission can enable more robust transmission.
Personal IoT scenario
  A user has multiple devices with different capabilities, such as mobile phone, laptop, wearable devices.
  Media (audio/video) can be shared among all the devices belonging to the same PIN.
Multi-modality scenario
  A user has multiple devices with multi-modality service.
  Synchronization and coordination of multi-flow services are required for multiple UEs.
Extended relay scenario
  A remote UE is power limited for high data rates at the edge of a cell.
  Inter-gNB aggregation and aggregation with more than one indirect paths are desirable.
More Scenarios for user collaboration

## Slide 4
Enhancements for UE aggregation at PDCP layer (1/2)
In addition to the intra-gNB UE aggregation, it is suggested to extend the following aggregation scenarios on top of R18 UE aggregation:
  Inter-gNB aggregation
    Direct path and indirect path are served by different gNBs.
  Multi-UE aggregation
    In addition to one direct path, more than one indirect paths may be supported via different relay UEs to jointly improve the data rate, reliability and stability.
(a) Inter-gNB UE aggregation
(b) Multi-UE aggregation

## Slide 5
Moreover, the following aspects may be considered for the UE aggregation at PDCP layer:
  Group mobility
    The remote UE and relay UE move and perform HO together to neighboring gNB
  Service continuity for inter-gNB HO and path switch
    The lossless delivery of data packet during inter-gNB HO and path switch
  Network controlled UE aggregation association
    Network authorization for the UE association
  UE interoperability
    Multi-vendor support for relay UE and remote UE
(c) Group mobility
Enhancements for UE aggregation at PDCP layer (2/2)

## Slide 6
UL transmission
    gNB schedules the anchor UE and assistant UE to transmit the same TB.
      The same resources can be used to reduce half of the resource utilization in PHY.
      Different resources can be considered for better diversity.
Mechanism
  DL transmission
    The gNB transmits the same TB to both the anchor UE and the assistant UE.
      Similar as multicast transmission, the same resources can be scheduled to reduce half of resource utilization in PHY (preferred).
      Different resources can be considered for scheduling flexibility.
Support UE aggregation at lower layer: Data duplication (1/2)

## Slide 7
PDCP aggregation
    The data is always transmitted on more than one legs since the anchor UE cannot know the transmission status at the assistant UE.
    PDSCH/PUSCH would be transmitted on the different resources.
    No combining gain at lower layer.
    HARQ re-transmission is always needed if the initial transmission fails in PHY.
Lower layer aggregation
    The gNB knows the transmission status of the transport blocks for the anchor UE and assistant UE.
    PDSCH/PUSCH can be transmitted on the same resources to reduce resource overhead and enhance UE antenna capability.
    Decoding performance can be improved due to combining gain at lower layer.
    HARQ re-transmission is not needed as long as transmission on one UE succeeds, which can reduce the latency and avoid unnecessary re-transmission.
Benefits over PDCP aggregation: Lower resource consumption, higher throughput, higher reliability and lower latency.
Support UE aggregation at lower layer: Data duplication (2/2)

## Slide 8
UL transmission
    gNB decides how to split the data from anchor UE via separate UL grants to anchor UE and assistant UE respectively.
    The anchor UE and assistant UE transmit the different TBs to the gNB.
Mechanism
  DL transmission
    The gNB transmits different TBs for the anchor UE via two DL grants to the remote UE and the assistant UE respectively.
    The assistant UE forwards the received TB to the anchor UE.
Support UE aggregation at lower layer: Data split (1/2)
Support UE aggregation at lower layer: Data split (1/2)

## Slide 9
PDCP aggregation
    UE decides how to split, and the PDCP packet split cannot fully take into account the physical layer capabilities and physical link conditions.
Lower layer aggregation
    gNB decides how to split, and the data can be split dynamically and efficiently according to instant channel conditions and available physical resources (e.g., time/ frequency resources or rank or power).
Benefits over PDCP aggregation: Higher throughput and lower latency
Support UE aggregation at lower layer: Data split (2/2)
Support UE aggregation at lower layer: Data split (2/2)
Notes: 30 32

## Slide 10
Objectives
Enhancements for UE aggregation at PDCP layer
  UE aggregation with more than one indirect paths and inter-gNB UE aggregation
  Mobility support for aggregated UEs and service continuity
  Network controlled UE association for aggregation
  UE interoperability support
Support of UE aggregation at lower layer
  Identification of UE aggregation at lower layer for both data split and data duplication
  Scheduling enhancements
      Scheduling via separate DCIs or one DCI (e.g., similar as multicast transmission or singe DCI based M-TRP transmission)
Work Scope

## Slide 11: Thanks