## Slide 1: R18 measurement Gap Enhancements: on left-over items
3GPP TSG RAN 99 RP-230637
Rotterdam, Netherlands, March 20-23, 2023 Agenda Item 9.3.4.7
MediaTek inc., Intel corporation, Apple

## Slide 2: Introduction
In RAN#97, the WID for NR_MG_enh2 was revised to RP-222337. In Objective 1), Notes 2 and 3 were added.
In our understanding, both notes considers more complicated scenarios.
  Note 2 considers the hybrid requirements when both Pre-MG and NCSG are configured to UE
  Note 3 considers the other possibilities, such as pre-configured NCSG and the joint requirements with gaps configured for NTN measurements
In this contribution, we provide our view about Notes 2 and 3
1) Enhancements of pre-configured MGs, multiple concurrent MGs and NCSG Define RRM requirements for UEs configured with a combination of pre-configured MGs, and/or concurrent MGs and/or NCSG [RAN4] Prioritize at least joint requirements for UE configured with Case 1: Pre-configured MG(s) and concurrent MG(s) (i.e., the network has provided UE with multiple measurement gap patterns where at least one gap pattern is a Pre-configured MG) Case 2: NCSG and concurrent MG(s) (i.e., the network has provided UE with multiple measurement gap patterns where at least one gap pattern is a NCSG) Note 1: Gaps that are configured for NTN are precluded in Case 1 and Case 2 Note 2: The requirement discussions on the scenarios that NCSG is considered in Case 1 and that Pre-configured MG is considered in Case 2 will be started after RAN#99. Note 3: Prioritization among other possible combinations of pre-configured MG, concurrent MG, NTN gaps and NCSG can be discussed after RAN#99 Note 4: This WID does not include any inter-working with MUSIM gaps

## Slide 3: Discussions
We suggest not considering the complicated scenarios in Note 2 and 3, because
  Current progress is not mature enough to start hybrid cases. One evidence is the gap combination configurations. So far RAN4 only agreed to take Rel-17 gap combination configurations (Table 9.1.8-1 in TS38.133) as formatting baseline for further study in Case 1 and Case 2 (R4-2303197). Many details are still FFS. Without a clear foundation of Case 1 & 2, it is not possible to start any discussions for hybrid cases.
  The TU of this WI will be reduced from 1 to 0.5, starting from RAN4#107 (May) meeting. It recommended to focus CR drafting to ensure the spec quality rather than extending the scope for more complicated scenarios.
RAN4 meeting | RAN4 meeting |  |  |  |  |  |  |  | 
 | 104 | 104b | 105 | 106 | 106b | 107 | 108 | 108b | 109
TU | 1 | 1 | 1 | 1 | 1 | 0.5 | 0.5 | 0.5 | 0.5

## Slide 4: Proposal
Proposal: Revise Note 2 and Note 3 in the Objective 1) of the NR_MG_enh2 as below
    Note 2: The scenarios that NCSG is considered in Case 1 and that Pre-configured MG is considered in Case 2 are precluded in this WI.
    Note 3: Except Case 1 and Case 2, other possible combinations of pre-configured MG, concurrent MG, NTN gaps and NCSG are precluded in this WI.

## Slide 5: Thank You!