## Slide 1: Off line discussion on NR_NTN_enh
Sources: Thales
3GPP TSG RAN #99
March xx - xx, 2023
Agenda: xxxx
TDOC: RP-23xxxx
For: discussion

## Slide 2: WI revision (to be revised in RP-230728)
Proposal 1: Agree all revisions except
  the frequency range of the exemplary band in clause 4.1.2
  The last note in clause 4.1.2
Proposal 2: Agree following corrections
  Study and identify NTN example bands in [17.3 – 20.2 GHz and 27.5 – 30.0 GHz] range: Analysis of regulations and adjacent channel co-existence scenarios.
Proposal 3: Agree on the addition in clause 4.1.2
  Note: Additional bands may be introduced in a release-independent manner but with a separate work item.
Source RP-230120
=Off line outcome> Proposal 1 is agreeable, Proposal 2 and 3 are not agreeable

## Slide 3: UL coverage enhancements
Proposal: In clause 4.1.1 “Coverage enhancements”, the WID is revised as follow:
The detailed objectives are for NTN:
  [Option 1] To specify PUCCH enhancements for Msg4 HARQ-ACK (e.g. repetition) [RAN1, RAN4]
  [Option 2] To specify PUCCH enhancements for Msg4 HARQ-ACK (e.g. repetition) PUCCH transmission when dedicated PUCCH resource configuration is not provided[RAN1, RAN4]
Source RP-230358
=Off line outcome> Option 2 is not agreeable, Option 1 is agreeable

## Slide 4: DL Coverage enhancements - 1
Proposal 1: Remove in clause 4.1.1 of WID the following text
  The following sentence will be revisited in RAN#99 as part of the DL enhancements discussion:
  “The evaluation should also take into account any related regulatory requirements, e.g., ITU limitation of power flux density.” No work on this topic will take place in RAN WGs before the discussion on DL enhancements in RAN#99.
Proposal 1bis: add in the chair notes that
  « no PFD limit applicable worldwide
  Addressing the potential restrictions is an operational issue »
Source RP-230618
=Off line outcome> Proposal 1 & 1bis are agreeable

## Slide 5: DL Coverage enhancements - 2
Proposal 2: For DL coverage enhancement solutions, satellite parameters assumptions (i.e. Transmission power per beam and coverage capability or number of active beams at a time) need to be clarified for system-level coverage
Source RP-230568
=Off line outcome> Although triggered interest, the Proposal 2 is not agreeable at this meeting

## Slide 6: DL Coverage enhancements - 3
Proposal 3: For DL coverage enhancements the following two steps approach should be considered
  Study the issues taking into system level coverage aspects
    Identify which enhancements are needed
    Identify the target link margin improvement
Source RP-230610
=Off line outcome> Although triggered interest, the Proposal 3 is not agreeable at this meeting

## Slide 7: DL Coverage enhancements - 4
Proposal 4: Low hanging fruit DL coverage enhancements should be considered in 3GPP especially for
  PDSCH (Msg4) and PDSCH (Msg 2) which the worst DL channel in terms of SNR requirements compared to PDSCH VoIP channel, for example
  Hence ~6 dB improvement is needed
Proposal 5: Revice clause 4.1.1 in WID with the addition of:
  To specify mechanism to enhance downlink coverage by 6 dB for PDSCH for Msg4. (i.e. PDSCH repetition/slot-aggregation adopted for RRC Connected mode)
Rational:
  Improve the DL radio link availability for UE in areas with low SNR (i.e. in car, in pocket of pedestrian) for mobile terminated (MT) call or messaging
  address satellite network deployment scenarios where transmit power per beam is limited
Source RP-230610
=Off line outcome> Proposal 4/5 raised many questions and hence are not agreeable

## Slide 8: Conclusion for on line discussion
Proposal 1: Endorse the revised WID in RP-230728
  (Implementing the corrections agreed on slides 2 & 4 of this document)
Proposal 2: add in the RAN#99’s chair notes that
  « no PFD limit applicable worldwide
  Addressing the potential restrictions is an operational issue »