## Slide 1
RWS-210033
3GPP TSG RAN Rel-18 workshop
June 28 - July 2, 2021
GRUPPO TIM
3GPP R18 RAN Requirements

## Slide 2
Timeplan Rel 18 – TIM proposal
2021
2022
Q3
Q4
Q1
Q2
Q3
Q4
2023
Q1
Q2
Q3
Q4
ASN.1 freeze
Rel 17
ASN.1 freeze
Rel 18
Stage 1 freeze
Stage 3 freeze
Stage 1 (Requirements and Service aspects) freeze in Dec. 2021 [tbc]
Stage 2 (Architecture and Technical design) freeze in Sept. 2022 [tbc]
Stage 3 (Detailed Specification) freeze June 2023 (R1) / Sept. 2023
ASN.1 freeze in Dec. 2023

## Slide 3
Rel 18 contents – Key pillars
Enlarge the ecosystem
Address shortcomings of previous Releases
Network automation
Define procedures and interfaces to measure, report/expose in a standard format
Improve performance and efficiency
Sustainable solutions
Energy efficiency
Future proof solutions

## Slide 4
Rel 18 contents – General aspects
3GPP Rel 18 should focus on solving issues found in deployed networks
Focus on green economy
Ensure alignment with SA
New use cases should be defined based on market demand
Enhancements of existing features should be limited only if there are clear requirements based on feedbacks from deployed networks
Enhancements of features not yet deployed should be avoided, waiting for feedbacks from deployed networks

## Slide 5
Current Rel-18 stage 1 requirements (SA1 activity up to Sept ‘21)
Expansion to New Verticals
Even more Extreme KPIs
New System Enablers
New Networking Scenarios
5G Smart Energy and Infrastructure
5G Railway Communication System (Smart Stations)
Guidelines for Extra-territorial 5G systems (HAPS, Satellite, Aeronautical, …)
AI/ML model transfer and distribution
Tactile and multi-modality communication services (immersive realtime experience)
Low Power High Accuracy Positioning for industrial IoT scenarios (1~2 years battery lifetime)
5G Timing Resiliency System (Timing and synchronization as a service for Transportation, Energy, Finance… )
Ranging services («point your phone & play»)
Enhanced Support of Network Slice
Data Integrity (to protect IoT communication)
Support for Service Function Chaining
Evolution of IMS multimedia telephony service (XR)
Enhancements for Residential 5G (devices behind Residential Gateway, small indoor base stations, …)
Personal IoT Networks (home IoT, wearables, …)
Vehicle mounted Relays
Access to Localized Services (“on demand”, temporary Neutral Host scenarios …)
Activities not expected to affect RAN are shown in Italics
High priority items for RAN (TIM view)

## Slide 6
Proposal #1 “improve energy efficiency”
Energy consumption is a key component in network OPEX
The impact of new features on the level of energy consumption should be evaluated
In 3GPP Rel 16 and 17 the proposals to study solutions to improve energy efficiency of base stations was not approved
Define KPIs based on energy efficiency to be associated to any new proposal
Define solutions to improve gNB and network energy consumption
PROBLEM
PROPOSAL

## Slide 7
UL performance, latency and TDD Frame Flexibility
In FR1 the current regulation in Europe imposes inter-operator frame synchronization to avoid co-channel (at the border between countries) and adjacent-channel interference (within a country)
Frame format mandated in Italy and other European Countries
Fully flexible frame format
The “regulated” frame structure has a major impact on performance (latency and throughput)
TDD Frame Format | DL [Mbps] | UL [Mbps]
n78, SCS 30 kHz, TDD 80 MHz | 256 QAM, MIMO 4x4 | 64 QAM, no MIMO
DDDDDDDSUU (8:2 Italy) | 1380 | 80
Latency:
RTT 3.42 ms (eMBB devices)
RTT 3.02 ms (URLLC devices)
TR 37.910, frame format DDDSU, 0% PER
Note: format DDDDDDDSUU has worse performance

## Slide 8
Proposal #2 “improve TDD performance – fixed frame format”
In FR1 the current regulation in Europe imposes inter-operator frame synchronization to avoid co-channel (at the border between countries) and adjacent-channel interference (within a country)
The “regulated” frame structure has a major impact on performance (latency and throughput)
Many applications are “deterministic” (i.e. traffic characteristics known “a priory” and known propagation environment)
Improve performance when fixed frame format is imposed
Optimize for “deterministic” applications
UL throughput
  Support of multiple Tx antennas in the UE
  Improve UL Carrier Aggregation / Dual Connectivity techniques
  Evaluate solutions for UEs not-power limited and not-size limited
RTT latency
  By defining resource allocation (e.g. the by pre-allocating PRBs)
Manage latency Jitter
PROBLEM
PROPOSAL

## Slide 9
Proposal #3 “improve TDD performance – allow flexible frame format”
In FR1 the current regulation in Europe imposes inter-operator frame synchronization to avoid co-channel (at the border between countries) and adjacent-channel interference (within a country)
The “regulated” frame structure has a major impact on performance (latency and throughput)
Define techniques to allow flexible frame format in FR1 TDD operations
  Ensure feasibility of non-synchronous networks in different scenarios (macro-macro, macro-pico)
  Enhancements of Cross Link Interference management techniques
  Intra and inter-operator coordination
  Definition of interfaces to exchange information between different PLMNs to manage cross-operators interference (inter-operator RRM)
  Note: this technique could also be used to minimize interruption time at the border between countries
PROBLEM
PROPOSAL

## Slide 10
Proposal #4 “Future proof devices”
The life cycle of a device in the industry is much longer than the average 3GPP Release
Legacy devices are causing a major barrier to switch off old technologies
  IoT applications for e.g. remote control of heating systems, alarms
  eCall
Devices should be designed to allow over the air upgrade to the new 3GPP Releases / Technologies
  3GPP should define performance requirements and conformance testing to ensure that UE upgraded over the air are still compliant to 3GPP specifications and to the regulatory requirements
  Requirements for multi standard UEs
PROBLEM
PROPOSAL

## Slide 11
Proposal #5 “Base stations performance and testing”
The base station architecture is becoming more flexible (CU-DU split, CP-UP split). Testing methodologies should be specified to ensure compliance of the overall chain, including test mode interfaces
Active antennas are a key element of base stations. OTA performance requirements and test methodologies should be specified
  Testing methodologies should be specified to ensure compliance of the overall chain, including test mode interfaces
  Specify OTA performance requirements and test methodologies
PROBLEM
PROPOSAL

## Slide 12
Proposal #6 “EMF management”
The emission limits are regulated to avoid harmful effects on the populations
  ICNIRP defined the limits for the non-ionizing radiation, but several countries are imposing much stringent limits
  This affect the possibility to deploy new base stations, add new technologies in existing sites and/or exploit site sharing
  Define procedures to measure, report/expose in a standard format and adjust if required the emission limits
    Work done in other bodies should be the basis for 3GPP activity (not re-invent the wheel)
  Define procedures to shape the antenna pattern and emitted power to ensure the emission limits are respected, e.g. by reducing the EIRP in a given direction if a building is too close to the mast (see next slide)
PROBLEM
PROPOSAL

## Slide 13
Proposal #6 “EMF management”
E > X V/m
Emission limits respected by shaping the antenna radiation pattern
Emission limits not respected

## Slide 14
Proposal #7 “UE RF performance indicator”
In 3GPP it is difficult to specify UE RF performance requirements due to competing needs:
Network operators want good performance to ensure good coverage and QoS
UE manufacturers want to apply the principle “never fail a good UE”
  Define a scale of UE RF performance based on OTA TRP and TRS measurements
  The classification, as in the case of energy efficiency, allows the customer to discriminate devices
  For example:
  Outperforming devices are classified class “A” or above
  Class “D” devices are underperforming and service may not be available in all the network
PROBLEM
PROPOSAL

## Slide 15
Grazie