## Slide 1: 5G-SOLUTIONS: Verticals’ requirements to 3GPP RAN Rel18
This project has received funding from the European Union’s Horizon 2020 research and innovation programme under Grant Agreement No. 856691
RWS-210034
3GPP TSG RAN Rel-18 workshop
June 28 - July 2, 2021
Notes: Per cambiare l'immagine in questa diapositiva, selezionarla ed eliminarla. Quindi fare clic sull'icona Immagini nel segnaposto per inserire l'immagine desiderata.

## Slide 2: Living Labs
Five different living labs will be trialed
Smart Factories
Smart Energy
Smart City / Ports
Media & Entertainment
Multi-living lab

## Slide 3: Living Lab 1: Factories of the Future (FoF)
Use Case 1.1: Time-critical process optimisation inside digital factories
Use Case 1.2: Non-time-critical communication inside factories
Use Case 1.3: Remotely controlling digital factories
Use Case 1.4: Connected goods
Use Case 1.5: Rapid deployment, auto/re-configuration and testing of new robots
Use Case |  | KPIs |  |  |  |  |  | 
 | Data Rate (Mbps) | Mobility (km/h) | Latency (ms) | Density (devices/m2) | Reliability (%) | Positioning Accuracy (m) | Coverage (%) | Autonomy (days)
UC 1.1 | >100 | <10 | <5 | >0.1 | >99.999 | <0.5 | >99 | -
UC 1.2 | >10 | <10 | <100 | >0.1 | >99.99 | <0.5 | >99 | >30
UC 1.3 | >500 | <10 | <5 | >10-2 | >99.99 | <0.5 | >99 | -
UC 1.4 | >10 | >30 | <10 | >10-4 | >95 | <10 | >99.9 | >30
UC 1.5 | >100 | <50 | <1 | >1 | >99.999 | <0.1 | >99.9 | >30

## Slide 4: Living Lab 2: Smart Energy
Use case 2.1 – Industrial Demand Side Management
Use case 2.2 – Electrical Vehicle Smart Charging
Use case 2.3 – Electricity Network Frequency Stability
Use Case | Indicative KPIs |  |  | 
 | Data Rate (kbps) | Latency (ms) | Reliability (%) | Coverage
UC 2.1 | Not critical | <10 | >99.999 | >99.9% Indoor
UC 2.2 | Not critical | <10 | >99.999 | >99.9% Outdoor
UC 2.3 | Not critical | <10 | >99.999 | >99.9% Outdoor

## Slide 5: Living Lab 3: Smart Cities & Ports
Use Case 3.1: Intelligent street lighting
Use Case 3.2: Smart parking
Use Case 3.3: Smart city co-creation
Use Case 3.4: Smart buildings – smart campus
Use Case 3.5: Autonomous assets & logistics for smart port
Use Case 3.6: Port safety: monitor & detect irregular sounds
Use Case | KPIs |  |  |  |  |  |  | 
 | Data Rate (Mbps) | Mobility (km/h) | Latency (ms) | Density (devices/m2) | Reliability (%) | Positioning Accuracy (m) | Coverage (%) | Service provisioning time (minutes)
UC 3.1 | - | - | <100 | >1 | >99 | - | >99 | -
UC 3.2 | - | <100 | <100 | >0.1 | >95 | <10 | >95 | -
UC 3.3 | >10 | <50 | <10 | >1 | >99.99 | <1 | >95 | <90
UC 3.4 | >100 | - | <10 | >1 | >99.99 | <1 | >99.9 | -
UC 3.5 | >100 | <50 | <10 | >1 | >99.99 | <0.5 | >99.9 | -
UC 3.6 | >100 | <10 | <10 | >0.1 | >99.99 | <10 | >99.9 | -

## Slide 6: Living Lab 4: Media & Entertainment (M&E)
Use Case 4.1: Ultra High-Fidelity Media;
Use Case 4.2: Multi CDN selection;
Use Case 4.3: On-site Live Event Experience;
Use Case 4.4: User & Machine Generated Content;
Use Case 4.5: Immersive and Integrated Media and Gaming
Use Case 4.6: Cooperative Media Production.
Use Case | KPIs |  |  |  |  |  | 
 | Data Rate (Mbps) | Mobility (Km/h) | Latency (ms) | Density (Devices per m²) | Reliability (%) | Coverage (%) | QoE (MOS)
UC 4.1 | <1000 | <100 | <100 | >1 | >99.99 | >99.9 | >4.3
UC 4.2 | >100 | <1 | <50 | >10-2 | >99 | >99 | >4.3
UC 4.3 | <1000 | <1 | <50 | >1 | >99 | >95 | >4.3
UC 4.4 | >100 | <100 | <100 | >1 | >95 | >99.9 | >4.3
UC 4.5 | <200 | <1 | <10 | >0.1 | >99 | >99 | >4.3
UC 4.6 | <1000 | <100 | <50 | >0.1 | >99.99 | >95 | >4.3

## Slide 7: Multi Living Lab (MLL): Multi-vertical concurrent usage of eMM, mMTC & URLLC
Use Case | SC 5.1 eMBB | SC 5.2 mMTC | SC 5.3 URLLC
LL1: Factories of the Future |  |  | 
UC 1.1 Time-critical process optimisation inside digital factory | C2 | C2 | C2
UC 1.2 Non time-critical communication inside factory | - | C2 | -
UC 1.3 Remotely controlling digital factories | C2 | - | C2
UC 1.4 Connected goods | - |  | C2
UC 1.5 Rapid deployment, auto/re-configuration and testing of new robots | B2 | B2 | B2
LL2: Smart Energy |  |  | 
UC 2.1 Industrial Demand Side Management | - | - | A1
UC 2.2 Electric Vehicle Smart Charging | - | - | A1
UC 2.3 Electric network frequency stability | - | - | A1
LL3: Smart Cities & Ports |  |  | 
UC 3.1 Intelligent street lighting | - | B1 | -
UC 3.2 Smart parking | - | B2 | -
UC 3.3 Smart city co-creation | B2 | B2 | B2
UC 3.4 Smart buildings – smart campus | C3 | C3 | C3
UC 3.5 Autonomous assets and logistics for smart harbour/port | B2 | B2 | B2
UC 3.6 Port safety: Monitor & detect irregular noise | B2 | B2 | B2
LL4: Media & Entertainment |  |  | 
UC 4.1 Ultra High-Fidelity Media | C1 | C1 | -
UC 4.2 Multi CDN selection | C1 | - | -
UC 4.3 On-site Live Event Experience | B1, C1 | B1, C1 | -
UC 4.4 User Generated & Machine Generated Content | C1 | C1 | -
UC 4.5 Immersive and Integrated Media and Gaming | C1 | C1 | C1
UC 4.6 Cooperative Media Production | C1 | C1 | -
A1= 5G-EVE Turin by TIM; B1= 5G-VINNI Norway;
B2= remote 5G RAN node by TNOR connected to 5G-VINNI Norway;
C1=5G-VINNI Patra;
C2= 5G private node by UOP;
C3=remote 5G RAN node by UOP connected to 5G-VINNI Patra

## Slide 8: General aspects
Based on the experience of the living labs the following aspects should be considered when planning the contents of Release 18
In most Living Labs, a mix of “deterministic networks” and “non-deterministic networks” are present (*)
  a mix of “deterministic communications” and “non-deterministic communications”
  both static and dynamic network configuration
A mix of traffic characteristics and UE classes is present in every Lab
Network management and orchestration of multi-tenant networks
(*) in 5G-SOLUTION two aspects define a “deterministic network”:
deterministic communications refer to the fact that the served applications may generate traffic every N ms and require transmission delay stable within certain bounds
static network configuration is a configuration that stay fixed for a sufficiently long period of time: fixed number of UEs and gNBs, without mobility (e.g., the network of charging point for electric cars or the sensor network in a production line)

## Slide 9: Requirements
Manage a mix of deterministic and non-deterministic networks
Identify and manage a “deterministic” slice
Optimize performance of the deterministic slice taking into consideration
  The devices are not moving
  The traffic pattern is known in advance
  A device can support applications requiring both deterministic and non-deterministic communications

## Slide 10: Requirements
Improve upload throughput
Several use cases are UL unbalanced (upload requirements higher than download) and must operate in macro-cells with DL unbalanced frame structure
Take into account that in some scenarios UEs are not power limited (e.g., a UE embedded in a charging point is not power limited)
Take into account that in some scenarios UEs are power limited

## Slide 11: Requirements
The life cycle of UEs in the Living Labs is 5-10 years
The design of the UEs should be future proof to ensure the capability to operate in radio networks based on future releases (e.g., capability to upgrade over-the-air the device to a new Release)
The design of the UEs should be future proof to ensure the capability to operate with different Core Networks (e.g., by upgrading over-the-air the device)

## Slide 12: Requirements
Ensure network management in a multi-tenant environment
Network management functions should be exposed via open interfaces
Orchestration of radio resources should be supported in a multi-tenant network (e.g., radio owned by the factory, Core owned by the public operator)