## Slide 1: OPPO views on Rel-18 package
3GPP TSG RAN Rel-18 Workshop RWS-210041
Electronic Meeting, 22 June – 02 July, 2021
Agenda Item: 4
Document for: Discussion

## Slide 2: Timeline (R18 and so on)
Rel18 could last 18 months for WGs i.e. 2022 Q1~2023Q3 for RAN1

## Slide 3: Vision on sidelink

## Slide 4
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 5: Sidelink over unlicensed spectrum
Sidelink:
  Latency reduction, traffic offloading, higher spectrum efficiency and coverage extension
  Part of solution for CV2X and commercial use cases e.g. NCIS and IIoT together with Uu
    but not all requirements are addressed e.g. sensor information sharing in CV2X and XR gaming etc.
More spectrums:
  Wide bandwidth of unlicensed spectrum e.g. few hundred MHz in 5G and 6GHz, few GHz in 60GHz
    No co-existence issue with e.g. wifi is identified
  More FR1 bands and FR2 are expected
Technical enablers:
  High order MIMO, beamforming, carrier aggregation, power saving techniques etc.

## Slide 6: Unlicensed spectrum

## Slide 7: scenarios
Scenarios:
  Support in-coverage, partial coverage and out of coverage scenarios
Resource allocation：
  At least support mode 1 and mode 2 and new resource allocation scheme introduced in R17
  LBT should be specified on top of resource allocation scheme
For multiple carriers operation, apart from between licensed carries, supporting:
  Unlicensed and licensed carrier or
  Unlicensed carrier and unlicensed carrier

## Slide 8
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 9: R18 SL Relay: U2U Relay
  R17 study phase (in both RAN and SA) and concluded the feasibility of U2U relay (L2, L3)
  But U2U has been excluded from normative phase due to the limited capacity
  U2U Relay is clearly motivated for public safety use case, and thus have to supported in R18
 | RAN2 |  | SA2 | 
 | L2 | L3 | L2 | L3
Discovery | Studied |  | Model A, Model B | 
(re-)selection | Studied |  | Studied (Sol#8, Sol#50) | 
Authorization | No RAN2 impact |  |  | 
Protocol Stack | Studied | Up to SA2 | Studied (Sol#9) | Studied (Sol#10, Sol#32, Sol#49)
QoS | No AS impact | Up to SA2 | Studied (Sol#31, Concluded) | Studied (Sol#31)
Security | Studied | Up to SA2 | Up to RAN2 and SA3 | Up to SA3
Service Continuity | N.A. | N.A. | N.A. | N.A.
CP | Dependent on PC5-S design by SA2 | Up to SA2 | Studied (Sol#9) | Studied (Sol#8, Concluded)

## Slide 10: R18 SL Relay: R17 Leftovers for U2N Relay
Enhanced service-continuity : to improve L2 U2N relay performance
  inter-gNB, direct/direct switching, Group-mobility
Architecture enhancement): to extend L23 U2N Relay applicable scenarios
  X-RAT control, MR-DC
R17 | R18
Intra-gNB mobility for U2N | Inter-gNB mobility for U2N
Service continuity between direct and indirect | Service continuity between indirect1 and indirect2
No support for group-mobility | Support for group-mobility
gNB only, i.e., NR-Uu only | Cross-RAT control for eNB, i.e., LTE-Uu
NR SA, i.e., no support on DC | DC-compatible, i.e., (NG)EN/NE/NR-DC

## Slide 11: R18 SL Relay: New enablers
Multi-hop: In 22.261 (as shown in the table), KPI for multi-hop UE-to-Network Relay has been provided
Multi-path (UP and/or CP): Of major interest in general during R17 SI phase
The benefit can be scheme/scenario-dependent, i.e., robustness/throughput
MBS-based Relay:
  MBS-oriented Relaying helps at least Public Safety and V2X use case
  Although in LTE UE-based Relay from Day-1, but not in R17 due to the parallel MBS work in R17
Scenario | Estimated number of hops
InHome Scenario | 2 to 3
Factory Sensors | 2 to 3
Smart Metering | 2 to 5
Containers | 3 to 9
Freight Wagons | 10 to 15
Public Safety | 2 to 4
Wearables | 1 to 2

## Slide 12
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 13: R18 SL Positioning
  In R17, RAN-level study on use cases/requirements/deployment will complete by RAN#93e.
  Accurate positioning technique for V2X/public safety/commercial use cases is still a missing piece for sidelink.
  In order for C-V2X technology based on NR sidelink to be competitive as a total solution for road safety, and also useful for mission critical and industrial / commercial applications, it is paramount that accurate positioning technique based on NR sidelink should be developed in 3GPP.

## Slide 14
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 15: Redcap-wearable device
  To enable locating users in any time e.g. children and old person with reasonable accuracy
  To introduce Redcap device with higher throughput to support e.g. Video service
  To introduce Redcap device with less complexity e.g. ring, wristlet etc.
  To enable much longer battery life
Positioning:
  May have different positioning performance requirement compared to normal UE
  Potential enhancement on PRS configuration, measurement and report
More bandwidth capabilities
  Support 40MHz
  Support 5MHz, 10MHz for FR1
Wearable devices of sidelink
  With reasonable bandwidth and complexity
Very long battery life:
  Wake up signal and power harvest

## Slide 16
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 17: NTN enhancement
  Rel17 NTN maybe able to support VoNR but with limited performance
  Some of NTN features are not specified in Rel17 due to lack of time
Enhancement on VoNR service:
  Focus on coverage，capacity and NTN specific power saving
Support UE without pre-compensation capability using GNSS
Support re-generative payload
  NTN with CA
  Supporting CA will be provide more data rate and better utilization of spectrum
More efficient Beam management (BM)
  Existing BM focused on UE mobility
  In NTN, mobility is rather on satellite side

## Slide 18: IOT-NTN enhancement
Motivation
  R17 IOT-NTN only addresses very specific use case
    i.e. sporadic small package with delay tolerance
Supporting wider use cases with comparable performance of NT IoT
HARQ enhancement
HARQ codebook design for reporting more HARQ-ACK information
More HARQ process number, transmission without ACK feedback
Other Rel17 leftover (up to Rel17 discussion)

## Slide 19
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 20: NR XR/Cloud Gaming
  Motivation
    R17 SI identifies fundamental challenge of XR/Cloud Gaming :
      Large data rate/capacity with limited latency
      Large power consumption
    R18 WI specifies potential enhancements
Efficient and low-latency scheduling/resource allocation
  SPS/CG transmission enhancement, e.g. adaptive CG configuration and non-integer period configuration
  Multiple TBs scheduling
CSI enhancement
Power saving in UE
  Compatible search space configuration and mechanism
  Search space switching and PDCCH skipping (Depending R17 outcome)
Mobility enhancement
  Mechanism to further reduce interruption time for lossless HO with reasonable complexity

## Slide 21: MIMO enhancement
  Motivation:
    To further improve spectrum efficiency for both DL and UL
Motivation:
  To further improve spectrum efficiency for both DL and UL
  To improve user throughput to enable new service
UL enhancement:
  Higher-order SU-MIMO up to 8 layers
    Frequency domain selective precoding
CSI further enhancement :
  Overhead reduction of CSI via time-domain compression
  Introduction of higher resolution codebook
Multiple-TRP:
  Multi-panel simultaneous transmission of UE
  Power saving enhancement e.g. reduction of PDCCH blind decoding
Beam Management :
  L1-event-driven beam management techniques
  UE initiated beam management

## Slide 22: Enhancement for mm Wave spectrum
Motivation:
  Some high-end service e.g. XR/CG etc. demand high throughput which can only be met by mm Wave smoothly
  More frequent mobility event is foreseen considering local dense network deployment
  There is some room left till Rel17 to enhance mm Wave performance e.g. latency, coverage, power saving etc.
Mechanism to deal with too frequent mobility event
  L1/L2 centric mobility
    Focusing on intra-frequency and cover inter-frequency case as well
    Covering both intra-DU and inter-DU case
Coverage enhancement:
  Leftover of Rel17 e.g. PRACH and PDCCH
Performance improvement:
  Fast SCell activation(up to RAN1 progress)
  Fast SCG activation
  Enhancement of TCI state switch

## Slide 23: XDD mode
Potential Motivation
  More efficient utilization of spectrum
  More flexible radio resource adjustment between UL and DL to e.g.
    Reduce feedback latency
    Improve uplink throughput and/or coverage
Identify potential use cases, operation scenarios
  Identify typical frequency band(s) and corresponding XDD mode
  Feasibility study ,including:
  Spectrum regulations
  Interference self-cancellation in network side
XDD mechanism study, including
  Identify the gap between current spec and potential identified issues
  Interference management
    Cross-link interference measurement and reporting
    Interference mitigation and coordination
Note1: No impact on UE RF and demodulation requirement is assumed in this study
Note2: No new XDD mode from UE point of view shall be assumed

## Slide 24: 52.6 -71 GHz (60GHz) enhancement
Motivation
  Make 60GHz applicable for diverse use cases
Rel-17 leftover (up to Rel17 discussion)
  E.g., Rx-assisted directional LBT, beam management enhancement
  Support URLLC service over 60GHz
  Extend unlicensed band URLLC/IIoT operation to 60GHz with potential enhancement
  Coverage enhancement for unlicensed spectrum
  Rel-17 coverage enhancement is a starting point
  Sidelink over 60GHz unlicensed spectrum

## Slide 25
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 26: AI by 5G, for 5G and of 5G
Key issues are studied in SA1(AMMT SID):
  AI traffics including AI/ML model and training/inference data are different n terms of QoS requirement e.g. experienced data throughput, latency
  Study is needed to figure out traffic model and potential area to improve
Cell level use cases are studied in RAN3(Data collection SID):
  Energy saving, load balancing, mobility enhancement etc.
  Principle and framework is captured in TR
RAN3 WID can be considered once study is concluded and standardization impact is identified
AI/ML could be also helpful to improve physical layer performance
  In terms of QoS requirement e.g. experienced data throughput, latency etc.
  Include but not limited to CSI compression, beam management, channel estimation, receiver enhancement….

## Slide 27: RAN enhancement for AI traffic(1/2)
Main use cases:
Split AI/ML image recognition
  To shift computing and storage from UE to server, uplink heavy
AI/ML model/data distribution
  To select optimum ML model in time, downlink heavy
Distributed/Federated Learning
  To train global model by aggregating local models partially-trained by each end devices based on the iterative model averaging, both uplink and downlink heavy

## Slide 28: RAN enhancement for AI traffic(2/2)
Chanllenge1:
  Extremely high UL experienced data rate e.g. AR displaying game, Remote driving and remote controlled robots etc.
Challenge2:
  Extremely high DL experienced data rate e.g. image recognition or speech recognition etc.
Challenge3:
  Challenge1+very low UP latency
Potential study area:
  Identify potential AI use cases whose challenge can be potentially met in 5G-Advanced
  Study AI traffic and their performance requirement
  Study potential enhancement area to meet those requirements
S1-211303 TR22.874 V1.1.0

## Slide 29: CSI compression
The basic idea:
  The measured raw CSI is compressed by a DML algorithm
The benefit:
  More precise channel status information can be transferred in order to improve MIMO performance
Measured raw CSI
DML F(x)
Compressed CSI
Measured raw CSI
DML F-1(x)
Compressed CSI
AI based CSI vs 3GPP CSI code book

## Slide 30
  Sidelink enhancement work
  Sidelink relay enhancement
  Sidelink positioning
  Redcap-wearable device
  NTN enhancement
  NR XR/Cloud gaming
  MIMO enhancement
  Enhancement for mm Wave spectrum
  XDD enhancement
  60GHz enhancement
  AI/ML in 5G
  Zero power IoT
eMBB
New area
Non-eMBB

## Slide 31: Zero power IoT (1/3)
Massive MTC is one important use cases for 5G. NB-IoT/MTC/RedCap have been specified in 3GPP for massive MTC.
Zero-power IoT UE utilizes technologies of back scattering and/or RF power harvesting. Zero-power IoT are very suitable to applications:
  with extreme conditions, e.g., high pressure, extremely high/low temperature, humid and other hazardous environments.
  Ultra-low cost, very smaller terminal size(e.g., slim),maintenance-free and longer life cycle are required.
Zero-power IoT would be complementary to current 3GPP IoT technologies.

## Slide 32: Zero power IoT (2/3)
Use Case 1: Industrial Wireless Sensor Network (IWSN)
  In some IWSN cases, the communication environments are harsh and hazardous:
    High/low temperature, moving or rotation parts, high vibration conditions, humidity etc.
  It require sensors with maintenance-free, battery-less, ultra-low power and long service life
Use case 2: Smart Logistics and smart Warehousing
  Huge amount of goods needs to be frequently transferred, stored, loaded/unloaded, and inventoried in the logistic station or warehouse (tens of thousands of m2).
  WPS communication is expected to enable Smart Logistics and smart Warehousing with its extremely-low cost, small size, maintenance-free , durable, long life span etc.
Use Case 3: Smart home
  WPS communication is attractive for smart home due to its characteristics of ultra-low cost, very smaller size, washable, flexible/foldable form factor and very long life time[2]

## Slide 33: Zero power IoT (3/3)
Illustration of zero-power communication

## Slide 34
eMBB
New area
Non-eMBB

## Slide 35: eMBB package

## Slide 36: Vertical package