## Slide 1: An overview of SL enhancement work in Rel-18
3GPP TSG RAN Rel-18 Workshop RWS-210046
Electronic Meeting, 22 June – 02 July, 2021
Agenda Item: 4.2 (Non-eMBB)
Document for: Discussion

## Slide 2: Outline
Part-1: General SL enhancement
Part-2: Enhanced SL Relay
Part-3: SL positioning
Annex: Detailed description on Part-1 and Part-2

## Slide 3: Part-1: General SL Enhancement

## Slide 4: Sidelink and Uu
Advantage of sidelink communication
  Latency reduction: Direct instead of indirect communication
  Traffic offloading: Traffic over Uu interface is offloaded to sidelink to avoid congestion
  Higher spectrum efficiency: Only one instead of two sets of radio resources
  Coverage extension
    UE can connect to network via relay (U2N) or
    UE can connect with each other out of coverage (U2U)
Integration between Sidelink and Uu
  Smooth mobility and service continuity
    Service can continue with normal indirect communication when a pair of UEs can’t reach with each other directly and vice versa
  Coordination
    For some use cases e.g. C-V2X, IIoT, NCIS, Uu link and sidelink communications are organic part of one system i.e. they collaborating with each other

## Slide 5: Sidelink for NR Rel-18 and beyond
Wider support of applications and services (refer to appendix for detailed use cases and requirement)
  Vehicle communication
    Better support for V2X to reach high data rate 1Gbps and high reliability of 10-5
    Inter- and intra-vehicle communications enabling wider range of applications and services
  Smart home IoT network
    High throughput, Internet connectivity and control via smartphone or CPE
    Direct / mesh connectivity between home devices to exchange contents and share resources (e.g., video/music, playing games, AR/VR experiences, printing, security and etc)
  IIoT / smart factories and warehouses
    Offload traffic from traditional centralized node (Uu communication) to PLC (sidelink communication)
    Shortened latency, improved reliability and reduced radio resource usage from direct short range communication
  Drones / UAV / Robots
    Direct communication and control among devices in areas without network coverage for commercial and public safety uses (e.g. tunnels, mines, coastal and rural areas)
  Healthcare sector
    Direct relaying of patient measurement / warning information from monitoring device to healthcare server via smartphone
    Redcap for sidelink: Better support for wearable and healthcare devices (e.g. reduced Tx/Rx antennas and SL bandwidth)

## Slide 6: Sidelink in NR Rel-18
Enabling features for NR sidelink (RAN1 focus):
  Wider frequency spectrum support
    Unlicensed frequency bands (FR1 and FR2), 5 / 6 / 60GHz (refer to appendix for unlicensed spectrum allocation and coexistence evaluation results between SL-U and Wi-Fi)
    Licensed frequency band (FR1 and FR2), additional bands depend on operator interests
  Higher data rate support
    Carrier aggregation / multi-carrier operation ((un)licensed + (un)licensed, FR1+FR2)
    Higher order MIMO (with enhanced CSI reporting)
  Reliability and coverage
    Beamforming in high frequency bands (FR2 and beyond)
    Packet duplication via multi-carrier operation
  Enhanced power saving
    WUS/GTS for SL DRX
    Power control enhancement for SL groupcast and/or unicast (including PSFCH)
    Refer to RWS-210047 for draft new WID on further enhancement for sidelink in R18

## Slide 7: Part-2: Enhanced SL Relay

## Slide 8: Sidelink Relay in R18: U2U Relay
  R17 study phase (in both RAN and SA) and concluded the feasibility of U2U relay (L2, L3)
  But U2U has been excluded from normative phase due to the limited capacity
  U2U Relay is clearly motivated for public safety use case, and thus have to supported in R18
 | RAN2 |  | SA2 | 
 | L2 | L3 | L2 | L3
Discovery | Studied |  | Model A, Model B | 
(re-)selection | Studied |  | Studied (Sol#8, Sol#50) | 
Authorization | No RAN2 impact |  |  | 
Protocol Stack | Studied | Up to SA2 | Studied (Sol#9) | Studied (Sol#10, Sol#32, Sol#49)
QoS | No AS impact | Up to SA2 | Studied (Sol#31, Concluded) | Studied (Sol#31)
Security | Studied | Up to SA2 | Up to RAN2 and SA3 | Up to SA3
Service Continuity | N.A. | N.A. | N.A. | N.A.
CP | Dependent on PC5-S design by SA2 | Up to SA2 | Studied (Sol#9) | Studied (Sol#8, Concluded)

## Slide 9: Sidelink Relay in R18: R17 Leftovers for U2N
  Enhanced service-continuity: to improve L2 U2N relay performance
    inter-gNB, direct/direct switching, Group-mobility
  Architecture enhancement: to extend L23 U2N Relay applicable scenarios
    X-RAT control, MR-DC
R17 | R18
Intra-gNB mobility for U2N | Inter-gNB mobility for U2N
Service continuity between direct and indirect | Service continuity between indirect1 and indirect2
No support for group-mobility | Support for group-mobility
gNB only, i.e., NR-Uu only | Cross-RAT control for eNB, i.e., LTE-Uu
NR SA, i.e., no support on DC | DC-compatible, i.e., (NG)EN/NE/NR-DC

## Slide 10: Sidelink Relay in R18: New enablers
Multi-hop:
  In 22.261 (as shown in the table), KPI for multi-hop UE-to-Network Relay has been provided
Multi-path (UP and/or CP):
  Of major interest in general during R17 SI phase
  The benefit can be scheme/scenario-dependent, i.e., robustness/throughput
MBS-based Relay:
  MBS-oriented Relaying helps at least Public Safety and V2X use case
  Although in LTE UE-based Relay from Day-1, but not in R17 due to the parallel MBS work in R17
Scenario | Estimated number of hops
InHome Scenario | 2 to 3
Factory Sensors | 2 to 3
Smart Metering | 2 to 5
Containers | 3 to 9
Freight Wagons | 10 to 15
Public Safety | 2 to 4
Wearables | 1 to 2

## Slide 11: Part-3: SL Positioning

## Slide 12: Sidelink positioning
  Target SL positioning services and operating scenarios
    V2X, public safety, and commercial
    In-coverage, partial coverage, out-of-coverage
  Enabling techniques
    Accurate absolute and relative positioning through direct wideband signal between devices
  How to organize this work in R18
    Option 1: Part of general sidelink further enhancement work
      Not preferred, no dependency to SL further enhancement work and likely not using dedicated carriers for V2X or public safety.
    Option 2: Independent / standalone item
      Preferred, better project management in RAN.
    Option 3: Part of general positioning further enhancement work
      OK, closely coupled with Uu positioning techniques when operating in network coverage. But not technically essential.
  Refer to RWS-210048 for further detailed discussions.

## Slide 13: Annex

## Slide 14: Appendix
Part-1: Sidelink background and use cases

## Slide 15: Sidelink in LTE
Applications and use cases
  Direct discovery and data communication exchange between devices (user traffic not routing via network BS)
    Shortened end-to-end communication latency via direct communication
    Reduced radio resource consumption / efficient communication (no UL and DL, only SL)
  Target for short distance/range communication of up to a few kilometers (depending on data rate and target reliability)
    Limited by UE power class / max output power
    Ideal for moving ad-hoc network (e.g., communication nodes are constantly moving and changing)
  Dedicated frequency spectrum for specific application (i.e., 700MHz for public safety / ITS in 5.9GHz for V2X)
    For security and interference control, guaranteed QoS
  Release 12 (D2D for public safety)
    Device discovery and mission critical voice/low data communication for public safety
    Support for different coverage operations: in-network, partial-network, out-of-network
  Release 13/14 (eD2D/FeD2D)
    Sidelink relay (L3 and L2 UE-NW) target for service continuity
  Release 14 (LTE-V2X / V2X phase 1)
    Sidelink frame structure update for V2V broadcast communication (i.e., basic safety messages)
    Discovery functionality incorporated into sidelink broadcast communication
  Release 15 (LTE-eV2X / V2X phase 2)
    Main enhancement to LTE-V2X
      Carrier aggregation / packet duplication for improved communication reliability
      UE power saving for P2X communication

## Slide 16: Sidelink in NR
Features and applications
  Main differences/enhancement to LTE-V2X:
    Shortened latency (longer subcarrier spacing, smaller periodicity)
    Improved reliability (HARQ, CSI feedback, SL power control)
    Support of all communication types (broadcast, multicast, unicast)
    FR2 compatible (PT-RS for phase tracking)
  Release 16 (NR-V2X / V2X phase 3)
    New NR sidelink frame structure to support V2X advanced use cases (i.e., platooning, extended sensor sharing, autonomous driving)
    Support for public safety use if requirement can be met
    Dedicated frequency spectrum (i.e., N14 (700MHz) for public safety; ITS in N47 (5.9GHz) for V2X)
  Release 17 (V2X / public safety / commercial)
    Power saving resource allocation schemes and DRX for power-constrained UEs (e.g., PUE, public safety (backpack) and commercial (AR/VR) devices)
    Inter-UE coordination for improved reliability
  Release 17 (NR sidelink relay – single hop)
    L2 and L3 for UE-NW

## Slide 17: Unlicensed spectrum
Notes: Huanglei: any impact to SL-U due to different regulation on transmission power e.g. indoor case
The EU part should be updated to 5.945GHz ~ 6.425GHz

## Slide 18: Co-existence simulation result
Solid line: Wi-Fi UEs only
Dashed line: 50% UE is replaced with SL-U UE
Observation: throughput of Wi-Fi UEs is actually improved after same amount of Wi-Fi UEs are replaced with SL-U UEs

## Slide 19: NCIS use cases
XR gaming
  Co-located users exchange live streams and control signal with each other and/or centralized game service
Real-time sharing of XR content
  A bidirectional or unidirectional A/V channel could be open between users to exchange real-time stream of motion signals and effects that influence the rendering of the 3D object
Media sharing
  Offline sharing is used for sharing 3D models/objects and 3D MR scenes amongst UEs
Wireless tethered connection
  AR/VR glass or helmet-mounted etc. could be tethered to a smart phone
[1] TR 26.928 Extended Reality (XR) in 5G

## Slide 20: NCIS Requirement(s)
[1] 22.261 table 7.6.1-1 KPI Table for additional high data rate and low latency service
Use Cases | Characteristic parameter (KPI) |  |  | Influence quantity |  | 
 | Max Allowed End-to-end latency | Service bit rate: user-experienced data rate | Reliability | # of UEs | UE Speed | Service Area (note 2)
Gaming or Interactive Data Exchanging (note 3) | 10ms (note 4) | 0.1-[1] Gbit/s supporting visual content (e.g. VR based or high definition video) with 4K, 8K resolution and up to120fps content. | 99.99% (note 4) | ≤ [10] | Stationary or Pedestrian | 20 m x 10 m; in one vehicle (up to 120 km/h) and in one train (up to 500 km/h)
Consume VR content via tethered VR headset (note 6) | [5 -10] ms (note 5) | 0.1-[10] Gbit/s (note 5) | [99,99%] | - | Stationary or Pedestrian | -
NOTE 2:Length x width (x height). NOTE 3:Communication includes direct wireless links (UE to UE). NOTE 4: Latency and reliability KPIs can vary based on specific use case/architecture, e.g. for cloud/edge/split rendering, and may be represented by a range of values. NOTE 5: The decoding capability in the VR headset and the encoding/decoding complexity/time of the stream will set the required bit rate and latency over the direct wireless link between the tethered VR headset and its connected UE, bit rate from 100 Mbit/s to [10] Gbit/s and latency from 5 ms to 10 ms. NOTE 6: The performance requirement is valid for the direct wireless link between the tethered VR headset and its connected UE. |  |  |  |  |  | 

## Slide 21: IIOT use case(1/2)
[MPR-22832-6.6-00a] The 5G system shall allow UEs to use ProSe communication when the UEs are not served by a RAN.
[MPR-22832-6.6-00b] The 5G system shall be able to support ProSe communication between UEs in close proximity using spectrum different than the spectrum being used for the 5GC-based communication.
[MPR-22832-6.6-00c] The 5G system shall be able to support 5G LAN-type service to UEs using ProSe communication.
[MPR-22832-6.6-00d] The 5G system shall be able to support multicast communication between the UEs within the group of UEs connected by ProSe communication.
[MPR-22832-6.6-00f] The 5G system shall be able to support mobility of the group of UEs connected by ProSe communication with respective service performance requirements in Table 6.4-1.
[MPR-22832-6.6-00i] The 5G system shall be able to support service continuity of a group of UEs using ProSe communication with respective service performance requirements in Table 6.4-1 when the group moves between a non-public network and a PLMN (subject to operator policies and agreement between the operators and service providers).
[1] 22.832 v17.20 Study on enhancements for cyber-physical control applications in vertical domains

## Slide 22: IIOT use case(2/2)
Use case | Characteristic parameter |  |  |  |  |  | Influence quantity |  |  |  | 
5.11 – Cooperative carrying of work pieces | Communication service availability: target value in % | Communication service reliability: Mean Time Between Failure | End-to-end latency: maximum | Bit rate | Direction | Message Size [byte] | Transfer interval [ms] (note 2) | Survival time [ms] (note 2) | UE speed [km/h] | # of UEs connection | Service Area [m³] (note 1)
Cooperative carrying – fragile work pieces | 99,9999 % to 99,999999 % | ~ 10 years | < 0.5 * Transfer interval | 2.5 Mbit/s | UE-UE (ProSe communication) | 250 500 with localisation information | > 5 >2.5 >1.7 | 0 Transfer interval 2 * Transfer interval | ≤6 | 2-8 | 10 x 10 x 5; 50 x 5 x 5
Cooperative carrying – elastic work pieces | 99,9999 % to 99,999999 % | ~ 10 years | < 0.5 * Transfer interval | 2.5 Mbit/s | UE-UE (ProSe communication) | 250 500 with localisation information | > 5 >2.5 >1.7 | 0 Transfer interval 2 * Transfer interval | ≤12 | 2-8 | 10 x 10 x 5; 50 x 5 x 5
NOTE 1: Service Area for direct communication. The group of UEs with direct communication might move throughout the whole factory site (up to several km²) NOTE 2: The first value is the application requirement, the other values are the requirement with multiple transmission of the same information (two or tree times respectively). |  |  |  |  |  |  |  |  |  |  | 
[1] 22.832 v17.20 Study on enhancements for cyber-physical control applications in vertical domains
Table 5.11.6-1: KPIs for ProSe communication for cyber-physical control applications

## Slide 23: CV2X use case
High degree or fully automation requires:
  Exchange of raw or processed data gathered through local sensors
  Live video images among vehicles, road site units, devices’ of pedestrian and V2X application servers
22.186 Enhancement of 3GPP support for V2X scenarios; stage 1
Communication scenario description |  | Req # | Payload (Bytes) | Tx rate (Message /Sec) | Max end-to-end latency (ms) | Reliability (%) | Data rate (Mbps) | Min required communication range (meters)
Scenario | Degree |  |  |  |  |  |  | 
Sensor information sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-001] | 1600 | 10 | 100 | 99 |  | 1000
 | Higher degree of automation | [R.5.4-002] |  |  | 10 | 95 | 25 (NOTE 1) | 
 |  | [R.5.4-003] |  |  | 3 | 99.999 | 50 | 200
 |  | [R.5.4-004] |  |  | 10 | 99.99 | 25 | 500
 |  | [R.5.4-005] |  |  | 50 | 99 | 10 | 1000
 |  | [R.5.4-006] (NOTE 2) |  |  | 10 | 99.99 | 1000 | 50
Video sharing between UEs supporting V2X application | Lower degree of automation | [R.5.4-007] |  |  | 50 | 90 | 10 | 100
 | Higher degree of automation | [R.5.4-008] |  |  | 10 | 99.99 | 700 | 200
 |  | [R.5.4-009] |  |  | 10 | 99.99 | 90 | 400
NOTE 1: This is peak data rate. NOTE 2: This is for imminent collision scenario. |  |  |  |  |  |  |  | 
Table 5.4-1 Performance requirements for extended sensors

## Slide 24: Smart home
Use case:
  Electronics at home could be connected with each other or controlled by smart devices
Requirements
  Data rate could be up to 500Mbps
  Latency could be low to 10ms
  Connectivity could be around 50+

## Slide 25: Healthcare use case
TR 22.866 enhanced Relays for Energy Efficiency and Extensive Coverage

## Slide 26: Appendix
Part-2: Enhanced SL Relay

## Slide 27: Background: R13 eD2D L3 Relay
SID/WID: SP-140386 (SA1), SP-140385 (SA2), RP-142311 (RAN)
Time: 2015~2016
Objective: Support the extension of network coverage using L3-based UE-to-Network Relays, including service continuity (if needed), based on Release 12 D2D communication, considering applicability to voice, video. [RAN2, RAN1, RAN3].

## Slide 28: Background: R15 FeD2D L2 Relay
SID/WID : SP-160511 (SA1), SP-160961 (SA2), RP-170295 (RAN)
Time: 2016~2017
Objective: Study the possibility of a common solution supporting the following use cases:[RAN2]
  i. UE to network relaying over non-3GPP access (Bluetooth / Wi-Fi).
  ii. UE to network relaying over LTE sidelink.
  iii. Unidirectional and bidirectional UE to network relay.
3GPP based UE-to-UE link

## Slide 29: Background
In LTE, although the UE-based relay has been specified (only in R13), it is quite limited in the sense that
  Single UE-to-UE protocol (i.e., LTE sidelink)
  Without scalability (single hop, single path)
  Supporting limited type of traffic (Public Safety oriented)

## Slide 30: R17 SL-Relay: L2/L3 Relay
WID : SP-190303 (SA1), SP-210272 (SA2), RP-210904 (RAN)
Time: 2019~2021 (SI converted to WI @ RP#91-e)
Objective: The objective of this work item is to specify solutions to enable single-hop, sidelink-based, L2 and L3 based UE-to-Network (U2N) relaying.
L2 UE-to-NW Relay
L3 UE-to-NW Relay (non-N3IWF scheme)

## Slide 31: R17 SL-Relay: L2/L3 Relay
State of the Art
  SI of RAN2/SA2 has been finished
  SI-to-WI conversion done @ RAN#91-e
  R17 Limited to single-hop, single-path, 3GPP UE-to-UE interface, unicast in R17, UE-to-Network Relay

## Slide 32: R18 SL-Relay
UE-to-Network Relay => UE-to-UE Relay
Single-hop Relay => Multi-hop Relay
Single-path (for relay/remote) => Multi-path (for relay/remote)
Unicast-only relaying => MBS-capable relaying
+ Other R17 left-overs

## Slide 33: R18 SL Relay: UE-to-UE relay
UE-to-UE relay are studied in both RAN2 and SA2 TR, and are captured as feasible.
  All UEs (Source UE, Relay UE, Destination UE) are in coverage.
  All UEs (Source UE, Relay UE, Destination UE) are out-of-coverage.
  Partial coverage where at least one UE is in-coverage, and at least one UE is out-of-coverage.
UE-to-UE relay is of high interest from public-safety perspective.
RAN2 recommends both L2 and L3 UE-to-Network and UE-to-UE Relay can proceed to normative work (The final decision depends on both SA and RAN TSGs#91e outcome).

## Slide 34: R18 SL Relay: Multi-Hop
Scenario | Max. data rate (DL) | Max. data rate (UL) | End-to-end latency (note 7) | Area traffic capacity (DL) | Area traffic capacity (UL) | Area user density | Area | Range of a single hop (note 8) | Estimated number of hops
InHome Scenario (note 1) | 1 Gbit/s | 500 Mbit/s | 10 ms | 5 Gbit/s/ home | 2 Gbit/s /home | 50 devices /house | 10 m x 10m – 3 floors | 10 m indoor | 2 to 3
Factory Sensors (note 2) | 100 kbit/s | 5 Mbit/s | 50 ms to 1 s | 1 Gbit/s /factory | 50 Gbit/s /factory | 10000 devices /factory | 100 m x 100 m | 30 m indoor / metallic | 2 to 3
Smart Metering (note 3) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /hectare | 200 x 100 bytes / 15 mins /hectare | 200 devices /hectare | 100 m x 100 m | > 100 m indoor / deep indoor | 2 to 5
Containers (note 4) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 15000 x 100 bytes / 15 mins /ship | 15000 x 100 bytes / 15 mins /ship | 15000 containers /ship | 400 m x 60 m x 40 m | > 100 m indoor / outdoor / metallic | 3 to 9
Freight Wagons | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /train | 200 x 100 bytes / 15 mins /train | 120 wagons /train | 1 km | > 100 m outdoor / tunnel | 10 to 15
Public Safety (note 5) | 12 Mbit/s | 12 Mbit/s | 30 ms | 20 Mbit/s /building | 40 Mbit/s /building | 30 devices /building | 100 m x 100 m – 3 floors | > 50 m indoor (floor or stairwell) | 2 to 4
Wearables (note 6) | 10 Mbit/s | 10 Mbit/s | 10 ms | 20 Mbit/s per 100 m2 | 20 Mbit/s per 100 m2 | 10 wearables per 100 m2 | 10 m x 10 m | 10 m indoor / outdoor | 1 to 2
In 22.261, KPI for multi-hop UE-to-Network Relay has been provided

## Slide 35: R18 SL Relay: Multi-Path
Multi-path relaying can apply to UP and/or CP
The benefit can be scheme/scenario-dependent, and of major interest in general during R17 SI phase
  Robustness
  throughput
 | Path-1 | Path-2
Scenario-1 | Direct UE-gNB link | Indirect UE-Relay_UE-gNB link
Scenario-2 | Indirect UE-Relay_UE1-gNB link | Indirect UE-Relay_UE2-gNB link
Scenario-3.. | More advanced scenario if considering multi-hop.. | 

## Slide 36: R18 SL Relay: MBS-oriented
MBS-oriented Relaying helps at least Public Safety and V2X use case
Although in LTE UE-based Relay from Day-1, but not in R17 NR UE-based Relay due to the parallel MBS work in R17
It should be included in R18 as Phase-II for NR UE-based Relay
NOTE 2: Support of non-unicast mode communication (i.e. one-to-many communication/broadcast or multicast) between network and UE-to-Network Relay UE and between UE-to-Network Relay and Remote UE(s) depends on the result of FS_5MBS work.

## Slide 37: R18 SL Relay: Other R17 left-overs
R17 as a start point focusing on the baseline function, but limited in different dimensions
R17 | R18
Intra-gNB mobility for U2N | Inter-gNB mobility for U2N
Service continuity between direct and indirect | Service continuity between indirect1 and indirect2
No support for group-mobility | Support for group-mobility
gNB only, i.e., NR-Uu only | Cross-RAT control for eNB, i.e., LTE-Uu
NR SA, i.e., no support on DC | DC-compatible, i.e., (NG)EN/NE/NR-DC

## Slide 38: Summary
WID Proposal: RWS-210045
R18 Enhancement aims at a UE-based relay architecture which is
  Compatible with various network architecture (EPS, DC, inter-gNB mobility, group-mobility)
  With enough scalability (UE-to-UE relay, single/multi-hop relay, single/multi-path relay)
  Support various traffic types (eMBB/URLLC/MTC, unicast/groupcast)