## Slide 1: Discussion on sidelink positioning
3GPP TSG RAN Rel-18 Workshop RWS-210048
Electronic Meeting, 22 June – 02 July, 2021
Agenda Item: 4.2 (Non-eMBB)
Document for: Discussion

## Slide 2: Requirement and use cases
  During RAN study phase, TR38.845 is to cover
    Positioning requirements for V2X and public safety use cases
    Operating scenarios include in-coverage, partial coverage, out-of-coverage
    For Public Safety, additional scenarios include: indoor and outdoor areas
  Positioning requirement covers both
    Absolute positioning (i.e., exact location / coordinates of a UE)
    Relative positioning (i.e., distance range / separation and direction between two UEs)
  Positioning requirement metrics
    Horizontal and vertical positioning accuracy (m)
    Positioning service availability (%)
    Positioning service latency (ms)
  During RAN WG normative phase:
    Proposal 1: Commercial use cases and positioning requirements are to be also considered
      NCIS: TR22.842
      Ranging-based services: TR22.855

## Slide 3: Requirement and use cases
  Enabling technologies
    Direct PRS transmission from one UE to other UEs (a.k.a. D2D / sidelink)
    To support high accuracy positioning, UE transmission / measurement of PRS should be wideband with high RS density and frequency
    When a stationary / fixed location device (e.g., roadside unit, positioning reference unit) is available, its absolute positioning information can be shared, along with SL-PRS transmitted over wideband for surrounding UE to derive its absolute positioning location, as well as ranging/distance information relative to the RSU/PRU.
    When only wideband SL-PRS is transmitted between UEs, sidelink-based positioning for ranging is supported.
  Consideration points
    SL operation for V2X and Public Safety is currently restricted to dedicated frequency spectrum with limited bandwidth per channel (i.e., 5, 10 MHz in B14 for PS) and (i.e., 10, 20MHz in B47 for V2X)
      SL-PRS should be transmitted in spectrum carrier(s) with sufficient bandwidth allocation instead
    Transmission of SL-PRS is independent to normal SL PSCCH/PSSCH operation and frequency carrier, does not need to follow existing SL frame structure and resource allocation schemes.
     No dependency to R18 sidelink enhancement work and the general network positioning work
  Proposal 2: SL positioning normative work is set up as an independent / standalone item in R18