## Slide 1: Motivation of study of RAN enhancement for AI/ML
3GPP TSG RAN Rel18 workshop RWS-210052
Electronic Meeting, March June, 2021

## Slide 2: Vision in decades on AI
eMBB
eMBB,XR,AI
XR,AI
2010
4G
2020
5G
2025
5G Pro
(AI for 5G)
2030
6G
AI of 5G
AI by 5G

## Slide 3: Experienced data evaluated for ITU-R submission
The average experienced data rate per 100MHz in average:
  DL on FDD carrier: 48.5Mbps
  DL on TDD carrier: 38.6Mbps
  UL on FDD carrier: 33.7Mbps
  UL on TDD carrier: 12.5Mbps
Note1: carrier frequency is 4GHz with channel model A/B for dense urban scenario
Note2: Average EDR per 100MHz is based on linear algorithm which maybe not very accurate

## Slide 4: Challenges of AI traffic for RAN
Chanllenge1:
  Extremely high UL experienced data rate e.g. AR displaying game, Remote driving and remote controlled robots etc.
Challenge2:
  Extremely high DL experienced data rate e.g. image recognition or speech recognition etc.
Challenge3:
  Challenge1+very low UP latency
S1-211303 TR22.874 V1.1.0
UL experienced data rate to ITU-R
DL experienced data rate to ITU-R

## Slide 5: AI traffic use case – Split AI/ML image recognition
  The AI/ML-based mobile applications are increasingly computation-intensive, memory-consuming and power-consuming
  Hence inference split between server and devices are necessary for:
    Alleviate the burden of device
    To protect user privacy
User application | Latency: maximum |  |  | User experienced UL data rate | 
 | End-to-end latency | Image recognition latency | Intermediate data uploading latency | AlexNet (Fig. 5.1.1-1, see note 4) | VGG-16 (Fig. 5.1.1-2, see note 4)
One-shot object recognition at smartphone | Several seconds | ~1s | ~100ms | 1.6~21.6Mbit/s | 8~240Mbit/s
Person identification in security surveillance system | Several seconds | ~1s | ~100ms | 1.6~21.6Mbit/s | 8~240Mbit/s
Photo enhancements at smartphone | Several seconds | ~1s | ~100ms | 1.6~21.6Mbit/s | 8~240Mbit/s
Video recognition | Several seconds | 33ms@30FPS | ~10ms | 16~216Mbit/s | 80Mbit/s~2.4Gbit/s
AR display/gaming | 7~15ms (see note 1) | <5ms | 2ms | 80Mbit/s~1.08Gbit/s | 0.4~12Gbit/s
Remote driving | 10ms (see note 2) | <5ms | 2ms | 80Mbit/s~1.08Gbit/s | 0.4~12Gbit/s
Remote-controlled robotics | 10~100ms (see note 3) | <5ms | 2ms | 80Mbit/s~1.08Gbit/s | 0.4~12Gbit/s
NOTE 1: According to [4][5], the VR motion-to-photon latency is in the range of 5-15ms. NOTE 2: According to [46] the one-way latency required for remote driving is 5ms. The round-trip latency is assumed to be 10ms. NOTE 3: According to [5] the end-to-end latency required for video-operated remote-controlled robotics is 10~100ms. NOTE 4: As listed in table 5.1.1-1 and table 5.1.1-2, the intermediate data size for the split points of AlexNet and VGG-16 is 0.02 ~ 0.27MByte and 0.1 ~ 3MByte respectively. |  |  |  |  | 

## Slide 6: AI traffic use case – Split AI/ML image recognition
  The model used for vision processing needs to be adaptively updated for different vision objects, backgrounds, lighting conditions etc.
  Optimum pre-trained AI/ML models need be downloaded temporarily in short duration
DNN model for image recognition | Number of parameters (Million) | 32 bits per parameter |  | 8 bits per parameter | 
 |  | Size of the model (MByte) | Required DL data rate (Mbit/s) | Size of the model (MByte) | Required DL data rate (Mbit/s)
AlexNet [7] | 60 | 240 | 1920 | 60 | 480
VGG16 [8] | 138 | 552 | 4416 | 138 | 1104
ResNet-152 [18] | 60 | 240 | 1920 | 60 | 480
ResNet-50 [18] | 25 | 100 | 800 | 25 | 200
GoogleNet [9] | 6.8 | 27.2 | 217.6 | 6.8 | 54.4
Inception-V3 [23] | 23 | 92 | 736 | 23 | 184
1.0 MobileNet-224 [19] | 4.2 | 16.8 | 134.4 | 4.2 | 33.6

## Slide 7: AI traffic use case – Uncompressed Federated Learning for image recognition
  Smartphone camera holds many valuable vision data for image recognition model training
  In Federated Learning mode, the cloud server trains a global model by aggregating local models partially-trained by each end devices based on the iterative model averaging
Mini-batch size (images) | GPU computation time (ms) | Maximum latency for trained gradient uploading and global model distribution (see note 1) | User experienced UL/DL data rate for trained gradient uploading and global model distribution (see note 2)
64 | 325 | 3.24s | 325Mbit/s
32 | 191 | 1.9s | 55Mbit/s
16 | 131 | 1.3s | 810Mbit/s
8 | 111 | 1.1s | 960Mbit/s
4 | 105 | 1.04s | 1.0Gbit/s
NOTE 1: Latency in this table is assumed 20 times the device GPU computation time for the given mini-batch size. |  |  | 

## Slide 8
Potential study area in Rel18:
  Identify potential AI use cases whose challenge can be potentially met in 5G-Advanced
    Use cases whose performance can be met with reasonable cost e.g. bandwidth
  Study AI traffic pattern of identified use case and their performance requirement
    Some coordination with SA WGs is necessary
  Study potential enhancement areas to meet those requirements
    Solutions in SA side and RAN side are not exclusive
    Solutions in both L2/3 or physical layer can be investigated