## Slide 1: Motivation for Rel-18 UAV
Ericsson
RWS-210190
3GPP TSG RAN - RAN-Rel-18 workshop
Online, 2021-06-28 - 2021-07-02

## Slide 2: Background
Rel-15 LTE WID on Drones added the following functionality:
  Aerial UE-specific reporting [RAN2]
    H1 and H2 which triggers when height is above/below configured thresholds.
    Measurement reports are triggered only if fulfilled by a configured number of cells
  Subscription-based identification [RAN3/RAN2]
  UP power control enhancements
  Flight path plan
An NR WID for Rel-17 was discussed by was postponed due to lack of time in Rel-17.

## Slide 3: Motivation for the WI
Serving drones via cellular networks is proving to be a significant opportunity for mobile operators.
LTE has already been enhanced with some features for UAVs. But so far NR has not been enhanced with such features.
As drones are expected to grow in number within coming years at the same time as NR deployments will grow, it would be essential to also evolve 5G NR to support aerial vehicles.

## Slide 4: Proposal
For NR:
  Specify measurement enhancements for drones:
    Height-, location- and flightpath reporting
    Controlling the amount of measurement reports
    Enhancements for conditional handover for UAVs
  Enable subscription-based identification
    Specify NG/Xn signalling to support subscription-based aerial UE identification
  To be discussed: Study the applicability of non-codebook based PUSCH transmission and fast beam switching that are specified in NR up to Release 17 for UAV use case in FR1, and specify enhancements if needed.
For both LTE and NR:
  Specify support for UAV-to-ground identification using LTE and NR PC5