## Slide 1: NTN Enhancements in Rel-18
Agenda Item: 4.2
Source: FGI, Asia Pacific Telecom
Document for: Discussion
3GPP TSG RAN Rel-18 workshop RWS-210194
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Justification (1/2)
[Background/observation]
Non-Terrestrial Networks (NTN) are expected to
  foster the roll out of 5G service in un-served areas (isolated/remote areas, on board aircrafts or vessels) and underserved areas (e.g., sub-urban/rural areas) to upgrade the performance of limited terrestrial networks in cost effective manner,
  reinforce the 5G service reliability by providing service continuity (e.g., passenger vehicles-aircraft, ships, high speed trains, bus) or ensuring service availability anywhere especially for critical communications, future railway/maritime/aeronautical communications, and to
  enable 5G network scalability by providing efficient multicast/broadcast resources for data delivery towards the network edges or even user terminal. See TR 38.811.
[Use case/scenario]
Use cases for Satellite access networks includes
  Fixed cell connectivity: Users in isolated villages or industry premises (Mining, offshore platform) access 5G services.
  Mobile cell connectivity: Passengers on board vessels or aircrafts access 5G services and benefit from 50 Mbps+.
  Wide area public safety: Emergency responders, such as police, fire brigade and medical personnel can exchange messaging and voice services in outdoor conditions anywhere they are and achieve continuity of service whatever mobility scenarios. See TR 38.811.

## Slide 3: Justification (2/2)
[Identified issues]
At the RAN#91-e meeting, Solutions for NR to support NTN was revised, with
  the core part completion by March 2022 (RAN#95), and
  the RAN4 performance part by September 2022 (RAN#97). See RP- 210887.
However, the overall completion level seems behind schedule, e.g.,
  for the core part is 20% with RAN1: 30%, RAN2: 20%, RAN3: 25%, and RAN4: 10%, and
  for the performance part is 0%. See RP-210726. (Note: the core part is 35% after the May meetings. See RP-210986)
To complete the WI on time, a work plan for the Rel-17 NR-NTN has been proposed in R2-2104963, in which
  for RAN1, polarization signaling, UL time and frequency synchronization, timing relationship, and HARQ enhancement must be concluded in 2 meetings, and
  for RAN2, MAC layer (including HARQ), RLC/PDCP, idle/connected mode mobility, NTN/TN service continuity, Location Services, and HAPS enhancement must be concluded in 3 meetings.
[Identified challenges]
The outcome of Rel-17 NTN will only provide essential features. As a result, some expected use cases of NTN shown in Table 4.2.1-1 of TR 38.811 will NOT be supported by the Rel-17 NTN, e.g., multi connectivity, network resilience, and mobile cell hybrid connectivity. How to enable full capacity of NTN shall be further investigated in Rel-18.

## Slide 4: Objectives (1/2)
[WID Objective: Rel-17 leftover]
Timing relationship enhancements [RAN1/2]
  TDD enhancement for ATG and HAPS/HIBS, e.g., SFI timing relationship, K1/K2 range extension, shall be carried on.
UL time and frequency synchronization [RAN1/2]
  Close control loop for UL frequency alignment, e.g., indicate UE-specific frequency offset for UL/DL shall be carried on.
HARQ enhancement [RAN1/2]
  Reliability enhancement when HARQ feedback is disabled, e.g., aggregated transmission (including repetition), MCS (including CQI report), and blind retransmission (NW schedules DL TBs without waiting for HARQ feedback)
User plane procedures [RAN2]
  Extension of RAR window: In the case UE cannot pre-compensate UL timing
  Adaptation for Msg-3 scheduling: enhancement if TA report can be carried via Msg1
  Enhancement on UL scheduling to reduce scheduling latency: BSR via 2-step RACH
  Enhancement on DRX: support DL blind retransmission for HARQ processes with HARQ feedback disabled
Control plane procedures [RAN2]
  Additional assistance information for cell selection/reselection, e.g., UE location information
  Definition of NTN (satellite/HAPS) cell specific information in SIB, e.g., earth-fixed or earth-moving
  Enhancement to SMTC/MG to address absolute propagation delay difference between satellites, e.g., UE assistant information [RAN2/4]
  Service continuity for mobility from TN to NTN and from NTN to TN systems, e.g., how to avoid ping-pong.
  Enhancement on Location Services (LCS) application protocols, e.g., how to prevent fake UE location. [RAN2/3]

## Slide 5: Objectives (2/2)
[WID Objective: Rel-18 new features]
Enhancement on the PRACH format and extension of the RAR duration [RAN1/2]
  Support UE with GNSS capability but without pre-compensation of timing and frequency offset capabilities.
    Enhanced PRACH formats and/or preamble sequences can be considered, e.g., a single Zadoff-Chu sequence based on larger SCS, repetition number.
Enhancement on Feeder link switch [RAN1/2]
  Support hard feeder link switch and discontinuous coverage.
    Study PHY layer procedures, transmissions and receptions of physical channels and signals to cope with feeder link switch.
Beam management and BWP operation [RAN1/2]
  Support L1-mobility for earth-moving cells.
    Enhance BWP operation to support frequency changes, e.g., increase the number of BWPs, and introduce beam-specific BWPs.
TN/NTN connectivity [RAN2]
  In Rel-17, the UE is not required to connect to both TN and NTN at the same time.
    For Rel-18, simultaneous connection to TN and NTN shall be supported, e.g., DAPS/RACH-less handover shall be supported to reduce handover interruption time.
Network based UE location [RAN2]
  In Rel-17, only UEs with GNSS capabilities are supported.
    For Rel-18, the NTN network-based positioning of UE should provide an accuracy comparable with the network-based UE location accuracy of TN, which is used for UL timing and frequency synchronization.

## Slide 6: Conclusion
[Summarization]
To support 5G use cases via NTN like fixed/mobile cell connectivity, direct to mobile broadcast, and wide area public safety, enhancing features to address the remaining/identified issues is necessary in Rel-18, e.g.,
  [Rel-17 leftover]: Timing relationship enhancements, UL time and frequency synchronization, HARQ enhancement, User plane procedures enhancement, and Control plane procedures enhancement.
  [Rel-18 new features]: PRACH format and extension of the RAR duration, enhancement on feeder link switch, and beam management and BWP operation, TN/NTN connectivity, and Network based UE location.
[Observations and proposals]
Observation #1: Considering the core part must be completed March 2022, Rel-17 NTN may only support minimum essential features to address the issues identified in TR 38.811 and TR 38.821.
Observation #2: Some of 5G use cases for satellite access networks provided by Table 4.2.1-1 in TR 38.811 may not be supported by the Rel-17 NTN, e.g., multi connectivity, network resilience, and mobile cell hybrid connectivity.
Proposal #1: Potential solutions to support TN and NTN connectivity should be enhanced in Rel-18.
Proposal #2: Considering DAPS and RACH-less HO as the potential solutions for Rel-18 NTN enhancement.