## Slide 1: Further MUSIM Enhancements for Rel-18
RWS-210208
Rel-18 Workshop

## Slide 2: Motivation
Rel-17 Multi-SIM WI has primarily focused on Single-RX and/or Single-TX UEs:
  Paging reception collision for IDLE/INACTIVE UEs (Single-Rx/Single-Tx)
  Network switching (Single-Rx/Single-Tx, Dual-Rx/Single-Tx)
The objectives of R17 MUSIM WIs address the minimum requirement for multi-SIM operation, which were mostly defined for single-RX/TX UEs
  More enhancements for double-RX/TX were held off due to time restrictions
  For instance, double-RX/TX UEs are capable of preserving/establishing RRC-Connected in Network A and Network B simultaneously and without any scheduling interruption, if procedures for partitioning UE resources are available
In Rel-17 Multi-SIM WI, scheduling gaps are used to address network switching
  Scheduling gaps are now used for various tasks e.g. cell (re)selection, location determination etc., and it is possible that the gaps overlap
  RAN should address possible overlapping scheduling gaps

## Slide 3: Possible Multi-SIM Enhancements
Study methods that enable resource partitioning of a multi-SIM UE to gracefully tune away to Network B without (scheduling) interruption in Network A [RAN2]
  Applicable UE architecture: Dual-Rx/Dual-Tx
Study methods to handle scheduling gaps for multi-SIM network switching possibly overlapping with scheduling gaps for other tasks [RAN2, RAN4]
  Applicable UE architecture: Single-Rx/Single-Tx, Dual-Rx/Single-Tx

## Slide 4: Thank you