## Slide 1: Coexistence between NR and Incumbents in Rel-18
RWS-210209
Rel-18 Workshop

## Slide 2: Motivation
Incumbent systems have prioritized channel usage and interference protection w.r.t NR eMBB services in shared/overlapping frequency spectrum scenarios.
For example: U.S. military/DoD operates a broad swathe of land-based, sea-based and airborne radar systems in the UHF and SHF bands between 300 MHz and 30 GHz.
Some of the frequencies with military radar operations that also overlap with current/potential 5G NR bands are:
  420–450 MHz
  902–928 MHz
  2900–3100 MHz
  3100–3650 MHz
  5250–5900 MHz
SPN-43 radar antenna on the USS ABRAHAM LINCOLN

## Slide 3: Interference protection requirements degrade NR QoS
Limits are usually placed on aggregate in-band and out-of-band interference from NR networks to incumbents.
  Power limits reduce NR coverage.
Worst case: spectrum administrator orders NR gNB to vacate a frequency channel(s) for purposes of incumbent interference protection.
  Cell tear-down, setup on a new channel and redirection of UEs leads to service interruptions and drop in QoS.
US CBRS example: If a radar system becomes active in a Dynamic Protection Area (DPA), NR cells with a large interference contribution to an activated DPA may have their spectrum grants suspended and be moved to another operating channel*.
          * CBRS Incumbent Protections and Encumbrances Overview WINNF-TR-5003-V1.0.0, 2020.

## Slide 4: Exploit incumbent signal characteristics for coexistence
Radar system pulse repetition rate, EIRP, antenna rotation period etc. can be inferred by gNB or provided by spectrum administrator.
  Exploit for improved coexistence and interference protection.
Time-domain channel sharing with TWS radar based on NR duty cycle:
  ON period when radar is rotated away, OFF otherwise.
Radar antenna rotation
gNB
ON
Frequency
Time
TON
ON
TON
OFF/Very low power
Data/control
TOFF
PRB blanking

## Slide 5: Scope for Rel-18 NR Study
Study methods for enhanced channel sharing between NR and incumbent systems based on a combination of one or more of:
  Time-domain NR duty cycle
  Beamforming that accounts for incumbent beam direction(s)
  Other mechanisms in time/frequency/power domain [RAN1]
Identify impacts of new coexistence methods on physical-layer procedures, if any [RAN1, RAN2]

## Slide 6: Thank you