## Slide 1: Improved Utilization of Fragmented Spectrum Holdings
RWS-210210
Rel-18 Workshop

## Slide 2: Motivation
Private 5G network providers, neutral hosts, and greenfield NR deployments may operate with fragmented licensed spectrum holdings spread across FR1 instead of a single, contiguous channel allocation of, e.g., 40 MHz in DL/UL.
Treating each sliver as a separate NR cell with CA has a non-negligible overhead cost.
Mixed progress on CA enhancements since R15
  Fast activation/deactivation and PSCell scheduled by SCell in Rel-16/17.
  Multi-cell scheduling of PDSCH with a single DCI was not agreed in Rel-17 under DSS agenda item.
600 MHz
1900 MHz
3550 MHz
10 MHz
20 MHz
30 MHz

## Slide 3: Scope for Rel-18 NR Study
Study methods of efficient scheduling, data channel transmission, and overhead reduction for a single cell with non-contiguous frequency resources. [RAN1]
  Baseline for enhancements is CA of the non-contiguous resources.
  Leverage as much as possible non-contiguous transmission mode with intra-carrier guardbands introduced in Rel-16 NR-U for channels wider than 20 MHz.
Identify impacts on physical-layer and higher-layer procedures [RAN1, RAN2]
Study effects on BS and UE RF requirements [RAN4]

## Slide 4: Thank you