## Slide 1: Agenda Item: 4.1 Source: AT&T Title: Views on eMBB-driven Functional Evolution for Rel-18 Document for: Discussion/Decision
3GPP TSG RAN Rel-18 workshop RWS-210212
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: eMBB-driven Functional Evolution
This contribution provides AT&T’s views on eMBB-driven enhancements for Rel-18
Specifically, the following eMBB-driven enhancements are proposed to be specified/studied in Rel-18, of which a subset are described further in this contribution, as indicated below:
    FWA enhancements
    Further enhancements on MIMO
    NR-U enhancements
    Intra-node full duplex
    DSS enhancements
    UL coverage enhancements
    Smart repeaters
    FR2 mobility enhancements
Note that AT&T’s high-level views on overall Rel-18 enhancements are provided in [1]
[1] RWS-210211, Views on 5G Enhancements for Release 18 and Beyond, AT&T
Enhancements further described in this contribution,
although some other features may be equally important

## Slide 3: FWA enhancements
UL MIMO Enhancements
    Target stationary devices with large number of antennas (CPE/FWA)
    Increase parity between UL and DL in capabilities and features
    UL TPMI enhancements incl. sub-band precoding
    Higher order SU-MIMO (>4 layers) in UL
    Simultaneous UL Transmissions (mTRP/mPanel enhancements)
Enhanced UL coverage
    Further enhance upon Rel. 17 coverage enhancements
    Focus on power domain enhancements
Higher order modulation alphabets
    Specify 4096 QAM for DL

## Slide 4: Further Enhancements on MIMO
Low FR1 band Enhancements Targeting low FR1 bands (<1GHz) CSI enhancements Enhancements to mTRP Mobility Enhancements CSI enhancements incl. Doppler domain exploitation/compensation to reduce the overhead of CSI feedback L1/L2 inter-cell mobility enhancements including inter-DU enhancements High Capability UEs and UL Enhancements Target devices with large number of antennas UL TPMI enhancements Higher order SU-MIMO (>4 layers) in UL | Multi-TRP/multi-Panel Enhancements Enhancements on inter-cell operation with non-ideal synchronization Multi-panel enhancements to consider self and cross-link interference Simultaneous multi-panel UL transmissions Multi-Beam/Multi-Panel Enhancements Enhancements on beam indication and measurement/reporting beyond Rel. 17 Enhancements on overhead and latency reduction beyond Rel. 17 Robust CSI Enhancements Further CSI enhancements for DL MIMO, MU-MIMO and UL MIMO CSI enhancements for feedback overhead and latency reduction

## Slide 5: Enhancements for NR operation in unlicensed spectrum
Receiver assisted channel access in Rel. 16 and Rel. 17
    Included in the Rel. 16 NR-U WID (down-scoped due to lack of time) and the Rel. 17 52.6-71 GHz WID
    Rel. 17, if anything, will only focus on Class A receiver assisted channel access
    Rel. 17 only introduces receiver assisted channel access for 52.6-71 GHz
Receiver assisted channel access in Rel. 18
    Specify Class B (and potentially Class A if it is not included in Rel. 17) receiver assisted channel access
    Allow Rel. 17/18 receiver assisted channel access enhancements in FR1
    Specifically target mTRP operation in unlicensed spectrum
This WID, while eMBB focused, can also cover sidelink enhancements and IAB enhancements specific to operation in unlicensed bands
Other left-overs that were down-scoped from the Rel. 16 NR-U and Rel. 17 52.6-71 GHz WIDs because of lack of TUs can also be considered for Rel. 18

## Slide 6: Intra-node Full Duplex
Full Duplex: Reduce PHY latency and improve UL coverage for TDD bands
Dynamically co-exist with half-duplex UEs/gNBs operating with the legacy frame structure
Support for interference measurement/management
Consider FR1/FR2 specific optimizations to enable sufficient spatial isolation
Top view of 28GHz phased array based Self Interference measurement system
Mean received power at Receiver 1 as a function of direction

## Slide 7: Dynamic Spectrum Sharing Enhancements
Improved NB-IoT Coexistence with NR
    Allow rate matching of NR channels/DMRS around a single PRB
  Improved coexistence between LTE PDCCH and NR
    Allow rate matching of NR PDCCH around LTE to prevent any zero-power resources for NR in a slot