## Slide 1: Agenda Item: 4.2 Source: AT&T Title: Views on Non-eMBB-driven Functional Evolution for Rel-18 Document for: Discussion/Decision
3GPP TSG RAN Rel-18 workshop RWS-210213
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Non-eMBB-driven Functional Evolution
This contribution provides AT&T’s views on non-eMBB-driven enhancements for Rel-18
Specifically, the following non-eMBB-driven enhancements are proposed to be specified/studied in Rel-18, of which a subset are described further in this contribution, as indicated below:
    Local routing and mesh networking*
    Mobile relays*
    UAV enhancements*
    Further MIMO enhancements*
    XR enhancements*
    Network coding*
Note that AT&T’s high-level views on overall Rel-18 enhancements are provided in [1]
[1] RWS-210211, Views on 5G Enhancements for Release 18 and Beyond, AT&T
  Further positioning enhancements
  SL positioning enhancements
  Multicast/broadcast enhancements
  Further IIoT/URLLC enhancements
  Further SL/V2X enhancements
  RedCap enhancements
* Features further described in this contribution, although some other features from above list may be equally important, e.g., positioning, M/B.

## Slide 3: Local Routing and Mesh Networking
Low-latency Sidelink mesh communications for public safety, V2X, and factory scenarios
  Enable more flexible deployment scenarios
  Enable architectures that reduce local latency for localized traffic
  Enable better inter-node coordination
Leverage network-affiliated L2 SL Relays (Local Managers) to coordinate local resources and traffic and support network coverage extension

## Slide 4: Further IAB Enhancements for Node Mobility
Introduce support for group signaling for intra-donor and inter-donor migration
Access UE enhancements to support awareness of IAB deployment architecture (e.g. hop count)
Leverage IAB-architecture to support formations of mobile (e.g. UAV-based) IAB nodes
Leverage CP-UP separation (FR1-FR2) being specified in Rel-17 to prevent C-plane disruption during IAB-node handover
Leverage NTN enhancements to support HAPS-like IAB-nodes
Public safety (FirstNet) and military use cases
Public transportation use cases with buses, trains, etc.
Split CP-UP IAB Topology
Donor
Hop 1
Hop 2
MT U-Plane
UE C/U-Plane
MT C-Plane
FirstNet
Military

## Slide 5: UAV Enhancements for NR
Bring NR specifications in line with LTE specifications for support of UAVs
  UE-triggered measurement reports based on configured height thresholds
  Reporting of height, location and speed in measurement reports
  Flight path reporting
  Signaling to support subscription-based aerial UE identification
  Reduction in amount of measurement reports
  Potential UAV-specific RRM or mobility enhancements
  Support remote ID broadcast over PC5

## Slide 6: Multi-Beam/Multi-Panel/Multi-TRP Enhancements
MIMO enhancements to facilitate use cases such as IAB, V2X, group mobility, FR4, etc.
Simultaneous multi-panel uplink transmission
Beam indication and beam measurement/reporting enhancements
Beam failure recovery enhancements
Enhancements to include power control/interference management aspects
SDM IAB
Full Duplex IAB
SDM IAB
Full Duplex IAB
  Multi-panel enhancements lead to a reduction in latency and more efficient frame structure for IAB nodes

## Slide 7: XR Deployment Scenarios
In Rel. 18, XR work item to serve as a continuation and introduce enhancements of Rel. 17 study item
XR use cases need to be supported in a range of environments including dense urban, suburban, transit/shopping centers, enterprise campuses, and parks/open spaces
Multi-connectivity between FR1 and FR2 provides service continuity, robustness, and high capacity hotspots
UL-heavy traffic may especially be a RAN bottleneck

## Slide 8: XR Enhancements

## Slide 9: Further Efficiency Enhancements with Network Coding
New verticals and use cases, such as XR services, may rely on Rel-16 packet duplication feature to improve reliability.
However, due to their corresponding high data rates, such new verticals may introduce network inefficiencies.
Use of network coding at the PDCP layer residing at the CU-UP can significantly help to reduce such inefficiency caused due to data duplication over multiple legs.
The use of outer codes, such as rateless fountain codes, can allow ‘spraying’ of encoded packets across more than one transmission leg, to enable successful reception while receiving only a subset of the transmitted packets.
Leverage packet duplication feature specified in Rel-16 with up to 4 RLC entities (4-way CA or CA+DC combination).
Applicability to URLLC and IAB, especially in a multi-frequency CA/DC scenario.
PDCP+NC
RLC 1
RLC 2
RLC 3
RLC 4
MAC
PHY
UE
CC2
CC1
CC4
CC3
CA-only
PDCP+NC
RLC 1
RLC 2
MAC
PHY
RLC 3
RLC 4
MAC
PHY
Xn
UE
CC2
CC1
CC4
CC3
MgNB
SgNB
NR-DC + CA