## Slide 1: Agenda Item: 4.3 Source: AT&T Title: Views on Machine Learning & Artificial Intelligence in RAN Document for: Discussion/Decision
3GPP TSG RAN Rel-18 workshop RWS-210214
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: ML/AI embedded in the RAN
Note: Architecture example shown here is for illustration purposes only and does not reflect AT&T’s deployment strategy in any way
The Way Forward
ML/AI algorithms embedded in functionality of the RAN to enable real-time decisions with distributed data
Interface enhancements to support training and model updates for non-real time and real-time use cases
State-of-the-Art
Disaggregated, heterogeneous and complex network architecture
ML/AI algorithms provide non-real time decisions based on centralized data sets
Regional Aggregation Site
TRP
TRP
TRP
Local Aggregation Site
gNB-CU
Local Core
Edge Computing
gNB-DU
gNB-DU
Switch/Router
Switch/Router
Regional Core
Regional Computing
NRT/Centralized
RT/Distributed
Key use cases
Mobility
MU-MIMO
Beam-management
Positioning / localization
App-specific PHY optimization

## Slide 3: Example Use Case 1: Online Learning for Enhanced MU-MIMO Scheduling
An online clustering and multi-user rate region learning approach that auto-tunes to different deployment scenarios
Greatly reduces complexity by clustering users for scheduling based on learning the channel state and capacity regions of the local environment
Specifically for MU-MIMO, significant gains in system throughput can be achieved by increasing the probability of successful user pairs
Example DU connected architecture
Example SLS results for a UMi scenario
Average throughput
Probability of successful transmissions
# of MU transmissions

## Slide 4: Example Use Case 2: Antenna Parameters Configuration and Optimization
Data-driven method to enable online and autonomous Tx parameter optimization locally
Greatly reduces overhead and latency constraints on network interfaces involved
Potential to scale to optimize a larger set of RAN parameters without centralization and offline aggregation of large data sets
Example Hybrid DU/CU connected architecture
Example SLS results for a HetNet scenario
UE SINR comparison
Outage probability comparison

## Slide 5: RAN-enabled AI/ML for Rel. 18
In Rel.17, RAN3 led item on high level principles of AI-enabled RAN, use cases with current NG-RAN architecture
In Rel. 18, RAN1/RAN2/RAN3 item
  Identify use cases where AI/ML methods lead to performance gains over current approaches
  Study standardization framework to enable AI/ML in RAN
  Study potential interface enhancements to support training and model updates
  Consider processing power/latency/availability requirements of RAN nodes
  Consider support for multi-vendor interoperability in ML/AI algorithm design