## Slide 1: TCP boosting

## Slide 2: Motivation
Up to Rel-17, NR is well-suited for DL TCP transmission.
  However, NR is not optimized for UL TCP ACK transmission.
NR aims at DL TCP throughput of ~20 Gbps...
  However, actual throughput in TCP layer is much less than 20 Gbps due to limitation by TCP ACK in UL.
  UL TCP ACK transmission is subject to head-of-line blocking by UL TCP transmission. TCP performance degrades if TCP ACKs are delayed.
TCP enhancement was already discussed in past meetings in NR Rel-15.
  However, RAN2#97bis finally concluded that this feature is not included in Rel-15 due to overload situation in RAN2. From then on, TCP enhancement has not been studied until Rel-17.
For the 5G-advanced to provide discriminatory impression to users, it is essential to maximize the DL TCP throughput in NR Rel-18.

## Slide 3: Potential enhancement
Prioritized TCP ACK processing in the transmitter side
  Head-of-line blocking problem of TCP ACK should be addressed.
  Mechanism can be considered in SDAP/PDCP/RLC/MAC depending on the targeted granularity for TCP ACK prioritization.
    E.g. Radio Bearer level, RLC bearer level, Logical channel level, etc.
Low latency TCP ACK transmission in the radio interface
  Scheduling and resource allocation enhancement for TCP ACK.
Prioritized TCP ACK processing in the receiver side
  Out-of-order delivery for TCP ACK.