## Slide 1: Enhancement for Mobility

## Slide 2: Justification for enhancement
Necessity of further mobility enhancements
  There is a potential for faster recovery via exploiting CHO/CPAC candidates and inter-cell mTRP resources.
    Higher bandwidth demands for advanced/industrial services necessitate ultra-dense-network (UDN) deployments. In FR2, link stability is relatively low due to narrow beams and vulnerability to blockages.
    There are more frequent link failures such as handover/radio link failures in UDN high frequency bands. To reduce service interruption caused by such failures, enhancements for faster recovery is useful.
    In case of MCG/SCG failure, CHO/CPAC candidates are currently unused as recovery target. In case of feMIMO, fast recovery to a non-serving cell mTRP resources may not be possible. In both cases, the chance of faster recovery is lost.
  Current dual connectivity is restricted to two cell groups. Lifting this restriction can provide a possibility for better performance
    Support for configuring more than two cell groups for a UE can enable a soft cell group switching as well as higher diversity gain.
  Further enhancement of Dual Active Protocol Stack to support CA/DC would be desirable for meaningful performance benefit
    Currently DAPS handover cannot support CA/DC. I.e., only PCell can be continued during DAPS handover. Advanced services with high data rate demand cannot benefit from DAPS handover.

## Slide 3: Areas for mobility enhancement
Enhancements for fast recovery in Rel-18
  Fast recovery with CHO/CPAC capabilities in DC
  Fast recovery via non-serving cell or SCell with inter-cell mTRP capabilities
Other enhancements in Rel-18
  Extension of Dual Connectivity
    Support of multi-connectivity beyond dual connectivity
    Enhancement of CG deactivation/activation scheme developed in Rel-17
  Support of CA/DC for Dual Active Protocol Stack

## Slide 4: Fast recovery with CHO/CPAC in DC
Data interruption due to radio link problem in DC
Fast recovery to CHO/CPAC candidates in DC
RLF
MCG/SCG failure information
MCG/SCG recovery message
Inter-node signaling
Recovery preparation
Inter-node signaling
Data interruption
This interruption can be reduced if CHO/CPAC candidate is used for fast recovery
RLF
MCG/SCG failure information
MCG/SCG recovery message
Inter-node signaling
Recovery preparation
Inter-node signaling
Data interruption
Mobility to CHO/CPAC candidates for recovery

## Slide 5: Fast recovery via multi-cell mTRP
Potential enhancements for robust connection with mTRP
  Fast recovery for PCell connection failure via multi-cell mTRP
    Recovery via non-serving cell or SCell
  Enhanced RLM for multi-cell mTRP
    Consolidated RLM over TRPs for maximal link availability
  Enhanced UL timing management for mTRP
TRP#1
Cell 1
TRP#2
Cell2
Consolidated RLM over mTRPs
Enhanced UL timing management for mTRP

## Slide 6: Other enhancement
Enhancements of DC
  Support of multi-connectivity (beyond dual-connectivity)
    The aim is to enable UE to support configuration of more than two cell groups.
    To avoid significant increase of UE complexity, the maximum number of active cell groups should be restrictive, e.g., up to two cell groups as of today.
    Dynamic change of active cell group among configured cell groups is supported for maximal diversity gain and low switching delay, i.e. softer cell group switching.
  Enhancement of CG deactivation/deactivation scheme developed in Rel-17
    Enhancement for balancing faster CG activation and UE power saving can be considered.
    The exact enhancement scope depends on Rel-17 progress of CG deactivation/activation.
Support of CA/DC for Dual Active Protocol Stack
  Support of CA/DC during DAPS is essential to support advanced services with consistent high data rate demands
    Currently, prior to DAPS handover, all secondary SCell and SCG shall be released.
  Sophisticated capability coordination between source and target during DAPS is essential.