## Slide 1: Factory IAB

## Slide 2: Motivation
New market demands for a private network is growing
  More diverse and stringent requirements are expected.
  Deploying wired backhaul within a private network is cost inefficient and inflexible, thus IAB would be considered.
However, IAB Rel-16/17 mainly designed for wide-area IAB node to support of wireless backhaul and relay links without the need for densifying the wired transport infrastructure
  Focus on basic procedures and providing general performance.
  Fixed or limited mobility is considered.
IAB Rel-16/17 has limitations to satisfy new market demands for a private network.

## Slide 3: Motivation
Factory IAB network is a promising use case for a private network, but this needs extreme performance
  Fixed or limited mobility for topology adaptation is considered in IAB Rel-16/17.
    However, factory IAB would encounter dynamic blockages by mobility of IAB nodes and moving objects. Given that a backhaul link blockage causes severe performance degradation, zero-interruption would be an important factor to increase system performance. Dynamic topology adaptation to reduce interruption by mobility should be considered.
  Static topological redundancy is considered in IAB Rel-16/17.
    However, mobility of nodes in factory IAB decreases overall network stability as well as packet routing performance. Given that factory IAB needs higher reliability and lower latency, topological redundancy in IAB Rel-16/17 has limitations to satisfy this stringent requirements for factory IAB. More proactive topological redundancy scheme should be considered.
  Semi-static interference coordination is used in IAB Rel-16/17.
    However, in factory IAB, interference situation changes dynamically due to mobility. Dynamic interference coordination among IAB nodes is needed to overcome interference by full mobility and sustain low interference level.

## Slide 4: Potential enhancement
Dynamic topology adaptation with zero-interruption mobility
  Enhanced DAPS or DC-based zero-interruption mobility.
  Controlled group mobility.
Dynamic topological redundancy with controlled duplication and express routing
  Controlled duplication based transmission.
  Express routing for delayed packets.
Dynamic interference coordination
  CLI enhancements to support dynamic interference coordination for intra- or inter-IAB networks.