## Slide 1: Inter-UE duplication avoidance

## Slide 2: Motivation
In an automated system, e.g., smart factory/city, transport/logistic system, in order to achieve higher reliability, multiple UEs will be given to the same mission, e.g., monitoring/detecting/report object/problem.
The UEs, involved in the same mission, will transmit the same message/information for the same event which occurs at the same time.
It is expected that very large size of high quality image/video is more widely used in real world due to improved signal processing ability with the help of AI or ML algorithm.
Redundant transmission of such large file would cause huge waste of radio resource.
…

## Slide 3: Motivation
Further, transmission of the same information/message, which the NW already knows, only delays the transmission of the next message/information, which is not desirable for e.g., urgent detection of sequential problem.
Therefore, redundant transmission of the same message/information from multiple UEs for a same event should be minimized as much as possible.
Event1
Event1
Event1, Event2
Cam1/Event1: Thank you 
Cam2/Event1: I knew it!
Cam3/Event1: I knew it!!
Cam3/Event2: It’s late!
Unnecessary Redundant tx
Successfully transmitted

## Slide 4: Potential enhancement
In order to minimize the redundant transmission of the same message/information between the UEs, who are involved in the same mission, the potential enhancement area includes,
  How to inform the UEs in the same group that the transmission of a message/information for a certain event is necessary or not.
    Evaluate which layer is suitable for handling this feedback.
    Evaluate which information should be provided with this feedback.
  How to avoid transmission of a message/information for a certain event if that is informed not necessary?
    Introduce a layer2 mechanism to avoid redundant transmission based on the feedback.