## Slide 1: Enhancement for NTN

## Slide 2: Motivation
In Rel-17, average per-UE throughput is quite restricted, because only single connection is supported per UE.
To meet the service requirements for satellite access, CA/DC should be supported to increase the throughput from NTN cell.
  KPIs for 5G system with satellite access (refer to TS 22.261):
    50 Mbit/s for vehicular connectivity
    360 Mbit/s/plane for airplanes connectivity
In NTN, there are various cases which may bring radio link failure to UE.
  e.g. feeder-link switch, disappearance of LEO satellite, and bad weather.
  If RLF happens, the UE performs RRC re-establishment procedure. But, due to long propagation delay in NTN, the service interruption time would be very long and may not be tolerable.
If CA/DC is supported in NTN, data rate will be increased and UE can recover the link failure quickly via another node.

## Slide 3: Motivation
In Rel-17, only transparent payload is considered
  The satellites communicate through gNBs on the ground, which would result in long signaling latency between the satellites.
If regenerative payload using inter-satellite link (ISL) is supported, the satellites can communicate directly, and the signaling delay can be reduced.
Inter-Satellite Link (ISL)
UE
NTN gateway
NTN gateway
Core
Network
gNB
gNB

## Slide 4: Potential enhancement
Support CA and DC in NTN networks, including:
  CA with LEO PCell + SCell: Increase data throughput
  DC with GEO (MN) + LEO (SN): MN manages UE mobility and MN takes role of data transmission
  DC with LEO(MN) + LEO (SN): Increase data throughput
  DC with TN (MN) + NTN (SN): SN complements weak signal area of MN
Support regenerative payload using inter-satellite link (ISL) to reduce signaling latency between satellites.