## Slide 1: ML-aided Predictive Mobility

## Slide 2: Challenges in comm. networks
Extreme and diverse KPIs for 5G and beyond communication systems
  Advanced services such as XR/AR and industrial applications require joint fulfillment of very high data rate, very robust connectivity, and very low delay .
  Sufficient network capacity and flexible network provisioning and adaptation are important for low CAPEX/OPEX of mobile network.
  KPIs of communication systems are getting more stringent and diverse. However, joint optimization of such KPIs is extremely challenging.
Utilization of Machine Learning for complex problems
  Due to recent success of deep learning, ML is re-gaining attention from whole industries.
  Function-approximation capabilities of ML are useful for jointly optimizing diverse KPIs in complex systems.
  In particular, prediction capabilities of ML allow for close-to-optimal mobility decisions.
Reciprocal evolution of communication and ML
  Communication for ML (C4ML): Communication enables distributed learning and task processing for efficient ML
  ML for communication (ML4C): Machine learning enables better communication performance and control strategy

## Slide 3: Adoption of ML in comm. industry
ITU-T
  ITU-TY.3170 series for machine learning in future network, specifying several ITU recommendations.
5GAA Study on QoS prediction framework:
  Work Item NESQO and eNESQO on study of a framework for QoS prediction and network reaction to such predictions, to meet automotive requirements of advanced services..
3GPP
  SA1 study on ML model distribution, applications and traffic analytics in TR 22.874.
  SA2 study on architectures and procedures for Network Data Analytics Function (NWDAF) in TR 23.288
  RAN3 study on ML applications in Rel-17 for NG-RAN intelligence.
  Adoption of ML into radio interfaces is uncharted. Adoption of ML into radio interface gives rise to profound questions and re-thinking.
  Rel-18 is a critical point in 3GPP milestone toward 5G Advance and 6G.
  Rel-18 is the right time to study adoption of ML into radio interfaces.

## Slide 4: Areas for ML in radio interface
Potential high-layer areas for ML adoption
  Scheduling
    Predictive BSR
    Predictive traffic prioritization, radio resource selection and duplication control
  Access Control
    Access control with predictive access cost evaluation
    Intelligent RACH resource selection and prioritization
  Mobility
    Predictive mobility decision
    Predictive RRM framework
  Link Management
    Predictive cell management for SCells/cell groups
    Predictive RLM
  Many other areas…

## Slide 5: Areas for ML in radio interface
Prioritized areas for ML adoption
  Mobility and link management are key areas for ML adoptions because these are severely challenged
    Ultra-dense mmWave deployments are required to meet very high bandwidth demands.
    Link stability and mobility performance are considered as blocking factors.
    Reactive mobility and link management in high frequency bands may not be timely enough to cope with highly dynamic link characteristics and stringent QoS requirements
  The current design of mobility and link management in 3GPP system is purely reactive (or short-term gain based), which often limits actual performance.
Exemplary test results: SCG mobility from 28GHz to sub-6GHz, provided by SKT

## Slide 6: Potentials of ML-aided mobility
ML-aided mobility
  ML’s prediction capabilities allow for close-to-optimal mobility decisions.
    Predictive mobility can be useful to avoid handover failures (too early/too late/wrong cell HO).
    Predictive mobility can be also useful to jointly meet both user QoE and network KPIs.
Preliminary simulation results
  ML-based handover decision can increase system performance.
  ML-based handover decision can reduce the rate of ping-pong.

## Slide 7: Two tracks for mobility in Rel-18
For mobility in Rel-18, two tracks can run in parallel:
TRACK1: Incremental evolution of technologies
  Enhancements of single-connectivity based mobility (e.g. DAPS, CHO); and/or
  Enhancements of multi-connectivity based mobility; and/or
  Enhancements of inter-cell multi-TRP based mobility
TRACK2: Exploration for ML-assisted mobility and link management
  Study on support of ML over radio interface is essential to identify achievable gain of ML as well as necessary enhancements of radio interfaces.
  Mobility and link management are key areas for ML applications over radio interfaces

## Slide 8: ML-aided predictive mobility
Axis for classification of ML-aided mobility
  Axis 1: Network-triggered versus UE-triggered
    Network triggered mobility, such as legacy handover including DAPS
    UE triggered mobility, such as CHO, CPAC
  Axis 2: UE-centric prediction versus network-centric prediction
    Network-centric prediction is baseline.
    UE-centric prediction may provide extra benefit if UE’s real-time local information is exploited for prediction as well as prediction model updates.
Classification of ML-aided mobility
  Category A) Handover control with network-centric prediction
    A-1) Network performs real-time prediction and network triggers handover
    A-2) Network performs real-time prediction and UE triggers handover.
  Category B) Handover control with UE-centric prediction
    B-1) UE performs real-time predictions and network triggers handover
    B-2) UE performs real-time predictions and UE triggers handover

## Slide 9: ML-aided predictive mobility and LM
Prediction tasks for ML-aided mobility and link management
  ML-enabled prediction of link quality
    Human mobility prediction with sensor fusion, LOS/NLOS prediction
    Prediction of beam/cell quality measurements and reporting
    Prediction of RLM, Predictive RRM
  ML-assisted mobility decision
    Prediction of optimal mobility timing, mobility candidate cell/beam
    QoS prediction
  ML-assisted link management
    Predictive SCell/cell group management, possibly including activation/deactivation state control and addition/removal/change of SCell/cell group
Further considerations
  Whether and how training models should be consolidated between UE and network?
  How can accommodate diverse training models and their evolution?
  What assistance information and how often such information should be provided to prediction entity?
  How to manage confidence level of prediction results? How to cope with time-varying prediction errors?
  How to validate prediction operations and inter-operability across different prediction models and across different prediction entities?

## Slide 10: Potential objectives
Identify possible scenarios that benefit from ML-aided mobility and link management (RAN2/RAN1)
Evaluate performance benefits and feasibility of ML-aided mobility and link management (RAN1/RAN2)
Study necessary enhancements to support ML-aided mobility and link management in areas including but not limited to RRM, RLM, and mobility procedures (RAN2/RAN3)
Study possible methodologies for testing and evaluation of ML-aided mobility and link management procedures (RAN4)