## Slide 1: Views on Rel-18 Mobility & DC/CA
NTT DOCOMO, INC.
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28th – July 2nd, 2021
RWS-210234

## Slide 2: Contents
FR2 Mobility
UL Flow Control Enhancements for DC

## Slide 3: FR2 Mobility – Views on FR2 Deployment
Non-contiguous deployment (mainly as SCG/SCell)
Contiguous deployment (can also consider FR2 PCell)
FR1/LTE Anchor
FR1/LTE Anchor
Will still remain in Rel-18 era (due to lack of coverage, site/cost limitation etc.)
Promising for e.g. low-latency services, densely populated urban area
Key challenge: Frequent SCG addition/failure
Key challenge: Continuity/reliability of FR2 usage and user data transfer
FR2 add-on cells
FR2 cells

## Slide 4: FR2 Mobility – Evolution
Non-Contiguous Deployment
Contiguous Deployment
Rel-18 Direction
Further improvement of latency and reliability of mobility
Improvements
Fast mobility
Reliability of user data during handover
Rel-18 Direction
Further optimizations against frequent SCG addition/failure, in terms of efficiency as well as latency
Improvements
Fast SCG addition
Features
Conditional PSCell addition
Features
Conditional handover
Conditional PSCell change
DAPS handover

## Slide 5: FR2 Mobility – Proposals
Rel-18 work should address non-contiguous FR2 deployments as SCG/SCell, as well as enhance the possibility/usability of FR2 PCell deployments
Further optimizations against frequent SCG addition/failure
  SCG deactivation for non-contiguous deployments
    Efficient SCG deactivation, e.g. UE autonomous SCG deactivation
    Fast and efficient SCG re-activation, e.g. w/o random access (potential Rel-17 leftover)
Further improvement of latency of mobility and reliability of user data during mobility
  Fast SCG/PCell Change (e.g. L1/L2-based mobility, see our MIMO slides)
  Multi-TRP operation through inter-gNB coordination (see our motivation paper)

## Slide 6: (Appendix) SCG Deactivation for FR2 mobility and blockage
DOCOMO would like to enhance fast recovery for FR2 mobility (Case 1) and SCG failure due to SCG blockage (Case 2)
Background and problem
  Case 1: Mobility in non-contiguous deployments
    For FR2, scenario that PSCells are placed in isolation is considered
    In the case, SCG failure happens between PSCells
Potential solution for solving above problem
  Enhance SCG deactivation (depending on progress of R17 DCCA WI)
    A UE is deactivated autonomously while SCG failure happens
    The UE is re-activated with RACH when SCG link is recovered
  Case 2: Blockage
    Even if the UE is located near the center of the cell, SCG RLF is considered to occur when using FR2
    Early recovery of the SCG radio link can be expected
deactivate
re-activate
SCG failure happens

## Slide 7: (Appendix) Previous mobility enhancements
Make-before-break(Rel-14)
Objective： Reduce Interruption Time
Method： Soft handover
  Constraints： Dual RF chain
RACH-less(Rel-14)
Objective： Reduce Interruption Time
Method： Skipping RA procedure
  Constraints： UL timing can be reused
Conditional HO(Rel-16)
Objective: Improve Robustness/reliability Method： Preparation-Suspension-Execution
  Prepare multiple Target cells Hold-off time
Dual Active Protocol Stack(Rel-16)
Objective： Reduce Interruption Time
Method： Soft Handover
  Uplink： Legacy way
  Downlink： Simultaneous transmission
  Common PDCP in order to guarantee SN sequence

## Slide 8: Uplink Flow Control Enhancements for DC – Background
EN-DC UL throughput issues
  At NR cell edge, low UL throughput is observed when UL is not transmitted on LTE link (e.g. due to ulDataSplitThreshold).
  When NR quality is good, low UL throughput due to transmitting on worse LTE link causing reordering delays is a concern
…
eNB
gNB
Poor UL quality due to
not transmitting data on good LTE link
(e.g. due to ulDataSplitThreshold)
…
eNB
gNB
…
Poor UL quality due to
transmitting data on poor LTE link
causing reordering delays

## Slide 9: Uplink Flow Control Enhancements for DC – Proposal
Rel-18 DCCA enhancement to discuss and resolve low UL throughput problem.
  Work on a smart UL flow control method at UE side by considering the condition of each leg.
…
eNB
gNB
…
UE
Conditions of each leg to be considered by UE to adaptively control sending UL data flow