## Slide 1: Study on RAN Evolution for Distributed Intelligence in Rel-18
5G Team / Lenovo Research / MBG
3GPP TSG RAN Rel-18 workshop RWS-210253
Electronic Meeting, Jun 28 – July 2, 2021
Agenda Item: 4.3
Source: Lenovo, Motorola Mobility
Document for: Discussion

## Slide 2: AI enabled RAN in Rel-17
  In Release 17, the study item of study on enhancement for data collection for NR and ENDC are mainly focusing on using AI technology to improve 5G network performance for some certain use cases e.g. energy saving, load balancing, traffic steering/mobility optimization.
Data
Collection
Model Training
Model Inference
Actor
Training Data
Inference Data
Model feedback
Model Update
Output
Feedback
Functional Framework for RAN Intelligence in TR 37.817

## Slide 3: Use Cases for Distributed Intelligence in RAN
5G network can provide AI services with distributed intelligence among RAN nodes and UE devices.
Use cases for distributed intelligence:
  With distributed intelligent capability and each dense RAN node and device can be a sensor, the RAN can provide intelligent sensing services such as real-time maps, environmental sensing, weather sensing and etc. For example, environmental sensing such as air quality monitoring requires collecting and processing large volumes of data from a variety of sensors resided in RAN nodes/devices spread across large geographical areas. An intelligent task can be performed for data collection, data pre-processing, data analysis and machine learning among the distrusted RAN nodes and devices.
  Intelligent RAN for MOBILE XR: To address the limitations of battery energy of devices, computation capacity and reduce end-to-end latency, intelligent task segmentation, computing offloading and learning model sharing among devices and RAN nodes will play a great role in bringing immersive experiences for users.
  Intelligent RAN for Autonomous Driving: Edge intelligence functionality (e.g. for sharing driving maps and etc. ) for autonomous driving can be located in the base station or road side units.

## Slide 4: Bring Distributed Intelligence in RAN
In SA TR 22.874, many use cases have been studied by SA for 5G system to better support distributed AI/ML operations among UEs and cloud/edge servers such as:
  Split AI/ML operation between AI/ML endpoints
  AI/ML model/data distribution and sharing over 5G system
  Distributed/Federated Learning over 5G system
Shifting the intelligence from central cloud and core network to RAN has the following benefits:
  Compared with deploying the intelligence in central cloud, deploying the intelligence in RAN has advantages on latency reduction and data privacy protection.
  The intelligence in RAN may not need core network involvement and can enable real-time networking among intelligent nodes.
RAN can be evolved to support any kind of AI services besides those studied in Release 17 for network optimization

## Slide 5: RAN evolution for AI Service
If we consider the scenario of dense RAN node deployment, distributed AI/ML operation among different RAN nodes and UE devices would be beneficial to improve the AI/ML efficiency, for example:
  The key factors of intelligence including data, computing power and AI working flow are distributed located in different RAN nodes and/or devices.
  For a certain AI task, intelligent task segmentation, data sharing, computing offloading and learning model sharing among devices and RAN nodes will play a great role in bringing immersive experiences for users.
AI Task Management
AI Signalling Plane
AI Data Plane
AI Computing Plane
Xn Interface
Uu
Uu

## Slide 6: Proposals
For Rel-18, the potential study area regarding RAN evolution for distributed intelligence includes
        Study RAN architecture evolution to support RAN enabled AI service;
        Study potential enhancements on RAN interfaces to support distributed intelligence, which may include intelligent task segmentation, data sharing, computing offloading and learning model sharing among devices and RAN nodes for a certain AI task;
        Study potential enhancements on air interface to address the QoS related requirements regarding data sharing, computing offloading and learning model sharing between UE and RAN node.