## Slide 1: Multi-carrier scheduling for Rel-18
5G Team / Lenovo Research / MBG
Agenda Item: 4.1
Source: Lenovo, Motorola Mobility
Document for: Discussion
3GPP TSG RAN Rel-18 workshop RWS-210258
Electronic Meeting, June 28 – July 2, 2021

## Slide 2: Motivation
Due to Rel-17 WID scope only focusing on two DL carriers within FR1, RAN1 did not study the potential benefits for more than 2 carriers for both UL and DL within FR1 and FR2.
According to Rel-17 SI, using a single DCI to schedule 2 carriers can save control resource and reduce PDCCH blocking probability.
It is worth studying in Rel-18 scheduling more than 2 carriers for both UL and DL within FR1 and FR2.
Using a single DCI to schedule 4 carriers

## Slide 3: Field types in DCI scheduling multiple carriers
Shared for the scheduled carriers
Modulation and coding scheme | 5
New data indicator | 1
Redundancy version | 2
HARQ process number | 4
Bandwidth part indicator | 2
Frequency domain resource assignment | 13
Time domain resource assignment | 4
VRB-to-PRB mapping | 1
PRB bundling size indicator | 1
Rate matching indicator | 2
ZP CSI-RS trigger | 2
Antenna port(s) | 4
Transmission configuration indication | 3
SRS request | 2
DMRS sequence initialization | 1
Identifier for DCI formats | 1
Carrier indicator | 3
Downlink assignment index | 4
TPC command for scheduled PUCCH | 2
PUCCH resource indicator | 3
HARQ timing indicator | 3
DCI fields/sizes of DCI format 1-1 (100 PRBs assumed)
Shared or separate up to network configuration
A single 24-bit CRC for the DCI
Separate for each scheduled carrier

## Slide 4: Proposed objectives
Objectives in Rel-18:
  Via link level simulation/system level simulation, study using a single DCI to schedule up to 4/8 carriers within FR1 and FR2.
  Both UL and DL scheduling are supported.
  Both licensed and unlicensed carriers can be scheduled by a single DCI.
  Both single-stage DCI and two-stage DCI are considered.
  “3+1” DCI size budget is kept.
Two-stage DCI