## Slide 1: On RedCAP enhancement in Rel-18
5G Team / Lenovo Research / MBG
Agenda Item: 4.2
Source: Lenovo, Motorola Mobility
Document for: Discussion
3GPP TSG RAN Rel-18 workshop RWS-210262
Electronic Meeting, June 28 – July 2, 2021

## Slide 2: Motivation
Rel.17 RedCap with 20MHz maximum UE BW for FR1, 100MHz maximum UE BW for FR2 meet the data rate requirement up to 150Mbps DL for high-end wearables and high-end videos.
Devices like industrial sensors, economic videos, etc., require much lower reference bit rate even less than 5Mbps, while cost reduction is significant for wide deployment of such devices and is vital for commercial success for RedCap.
Further cost/complexity breakdown specific for the low-end RedCap devices therefore needs to be studied and specified.
Besides, further power consumption needs to be studied to ensure longer battery life.
Use cases | Reference bit rate | Latency | Reliability | Battery life
Industrial wireless sensors | <2Mbps | <100ms; 5-10ms for safety related sensors. | 99.99% | At least few years.
Video surveillance | 2-4Mbps for economic video; 7.5-25Mbps for high-end video | <500ms | 99%-99.9% | NA
Wearables | 5-50Mbps in DL, 2-5Mbps in UL. peak data rate <=150Mbps in DL, <=50Mbps in UL. | NA | NA | <= 1-2 weeks
RedCap use case requirements

## Slide 3: Scope
Lower maximum BW supported in Rel.18 RedCap with e.g.,
  5MHz for FR1
  20MHz for FR2
Lower reference bit rate down to 5~10Mbps.
Lower UE power class with maximum transmit power of e.g., 14dBm.
Lower power consumption to ensure longer battery life.
Improved transmit efficiency/latency/reliability.

## Slide 4: Proposed objectives
Study the potential impact of BW reduction on both initial access and after initial access for both FR1 and FR2.
Study co-existence of Rel.18 RedCap UEs with legacy UEs (incl. Rel.17 RedCap UEs).
Study coverage enhancements for low power class UEs.
Study further power saving techniques e.g., PDCCH monitoring reduction.
Specify Rel.17 leftovers if any.