## Slide 1: Considerations on SON related enhancements in Rel-18
5G Team / Lenovo Research / MBG
3GPP TSG RAN Rel-18 workshop RWS-210263
Electronic Meeting, Jun 28 – July 2, 2021
Agenda Item: 4.1
Source: Lenovo, Motorola Mobility
Document for: Discussion

## Slide 2: Use Cases for SON Related Enhancements (1)
MRO enhancements for CPAC :
  In Rel-17, MRO enhancements for CHO is supported. However, MRO enhancements for CPAC (including conditional intra-SN PSCell change, conditional inter-SN PSCell addition, conditional inter-SN PSCell Change ) have been deprioritized due to timeline. The CPAC failure type definition and detection should be supported for MRO enhancements for CPAC.
Successful PSCell Change Reporting
  The MRO function is enhanced to provide a more robust mobility via reporting approximate failure events observed during successful handovers in Rel-17. Successful PSCell change reporting function is also beneficial for mobility robustness via reporting approximate failure events observed during PSCell change, which should be supported in Rel-18.
  MRO for fast MCG recovery (if it will not be supported in Rel-17)
  This fast MCG link recovery procedure is designed for UE to inform the MN about RLF on MCG via SN in Rel-16. A UE may experience failed fast MCG link recovery before re-establishment procedure and the UE may be hand-overed to a new target MN during fast MCG link recovery. It makes sense that the UE reports fast MCG link recovery information to the network for MCG failure diagnose.
  MRO for Inter-RAT HO from NR to E-UTRA for voice fallback
  Inter-RAT handover from NR to E-UTRA for voice fallback: the voiceFallbackIndication IE is introduced to be included in the MobilityFromNRCommand message for voice fallback purpose. UE shall select a suitable E-UTRA cell in priority after Inter-RAT HO failure happens. Failure reporting of Inter-RAT handover from NR to E-UTRA with the voice fallback purpose should be helpful.

## Slide 3: Use Cases for SON Related Enhancements (2)
MDT enhancements for NR MBS in idle/inactive
  The problem of verifying the performance of DL transmissions w/o UL feedback was discussed in LTE in the context of eMBMS and as solution the collection of MBMS related measurements using MDT was agreed in Rel-12.
  In view of the LTE solution for eMBMS, a similar solution can be adopted for MBS broadcast sessions by reusing the NR MDT functionality as much as possible. For example, the UE may be configured to log MBS related measurement information of broadcast sessions in RRC_IDLE and/or RRC_INACTIVE.
SON enhancements for IAB Topology and Routing Optimization
  SON enhancements for intra-donor IAB and inter-donor IAB topology integration and migration.
SON enhancements other aspects
  SON enhancement for NR V2X, e.g. resource allocation optimization for mode 2.
  SON enhancement for NTN mobility.

## Slide 4: Summary
The following use cases should be considered in Rel-18 SON enhancements WI:
  MRO enhancements for CPAC
  Successful PSCell Change Reporting
  MRO for fast MCG recovery (if it will not be supported in Rel-17)
  MRO for Inter-RAT from NR to E-UTRA for voice fallback
  MDT enhancements for NR MBS in idle/inactive
  SON enhancements for IAB Topology and Routing Optimization
  SON enhancement for NR V2X
  SON enhancement for NTN mobility