## Slide 1: Support of Ranging in Rel-18 xiaomi
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28 – July 2, 2021
RWS-210266

## Slide 2: Introduction
Open the door
if distance < e.g. 1m
Ranging: determining the distance or angle between two devices
Huge market potential
bed lamp
Phone pops up the control interface of TV
Phone pops up the control interface of bed lamp
point to TV
point to lamp
Smart Home
Smart City

## Slide 3: Introduction
Huge market potential
Smart Retailer
Smart Trip
α
d

## Slide 4: Introduction
Huge market potential
V2X
Public Safety

## Slide 5: SA1 Progress
SA1 has finished the “Ranging based service” SI/WI in May 2021
  Identify 19 Use cases, including: e.g.
      Distance based Smart Home Device Control Use Case
      Smart Home TV control
      Smart Vehicle key
      Find Items in a super market
      Distance based Intelligent Perception for Public Safety
      Picture and video sharing based on ranging results
      Hands Free Access
      Touchless Self-checkout Machine Control
      Smart Transportation Metro/Bus Validation
      Ranging of UE in front of a vending machine
      Find pets in a long distance
      Tracking of devices
      Immersive sound based on multiple-UE ranging

## Slide 6: SA1 Progress
KPIs examples of SA1 R18 WI: “Ranging based service”
Ranging scenario | Ranging Accuracy (95 % confidence level) |  | Availability | Latency | Effective Ranging distance, Coverage, NLOS/LOS, Relative UE velocity, Ranging interval, Number of concurrent ranging operation for a UE, Number of concurrent ranging operation in an area |  |  |  |  |  | 
 | Distance Accuracy | Direction Accuracy |  |  | Effective Ranging distance | Coverage | NLOS/LOS | Relative UE velocity | Ranging interval | Number of concurrent ranging operation for a UE | Number of concurrent ranging operation in an area
Smart TV remoter | 10cm up to 3 meter separation | ±2° horizontal direction accuracy at 0.1 to 3 meter separation and AoA coverage of (-60°) to (+60°); ±2° Elevation direction accuracy at 0.1 to 3 meter separation and AoA coverage of (-45°) to (+45°) | 99 % | 10ms | 10m | IC/PC/OOC | LOS | Static/ Moving (<1m/s) | 50ms | - | -
Smart Vehicle Key | 10 cm | - | 99 % | 50ms | 30m | IC/PC/OOC | LOS | Static/ Moving (<2m/s) | 25ms | - | 50UEs/ (104m2)
Finding Items in a supermarket | 50 cm | 5 degree | 95 % | 500ms | 100m | IC/PC/OOC | LOS | Static/ Moving (<1m/s) | 250ms | - | 100 UEs/ (3.14*104m2)
Hands Free Access | 10cm | - | [99 %] | 100ms | 10 m | IC/PC/OOC | LOS | Static/ Moving (1 m/s) | 50ms | - | 20 UEs/3.14*100m2
distance based intelligent perception for public safety | 50cm | - | 99 % | - | 20m | IC/PC/OOC | LOS | Static/ Moving (<20km/h) | - | 100 | -
Picture and video sharing based on ranging results | 10cm | 2° | 99 % | 50ms | 10m | IC/PC/OOC | LOS | Static/ Moving (<1m/s) | 50ms | - | -
Ranging of UE’s in front of vending machine | 20cm | 10° | - | 150ms | 5m | IC/PC/OOC | LOS | Static/ Moving (<1m/s) | 50ms | - | 10
Long Distance Search | 20m | 5° | 99 % | 1s | 100m-1km | IC/PC/OOC | LOS | Static/ Moving (up to 10m/s) | 5s | - | -

## Slide 7: Potential Scope
The objective is to study support of Ranging. The objective of the Ranging study includes the following objectives, considering in-network coverage, out-of-network coverage, and partial network coverage:
Study RAN level requirements and corresponding evaluation scenarios/methodologies to enable Ranging based on requirements defined in TS22.261[RAN1]
Study and evaluate potential solutions for support of Ranging based on the above identified requirements, evaluation scenarios/methodologies [RAN1/RAN2]
    The solution should support Ranging with the choices of measuring only distance, measuring only angle, and measuring both distance and angle.
    The solution should support different reference signal bandwidth for different distance/angle accuracy requirement.
    The solutions should consider enabling UE to discover other UEs supporting ranging.
    The solutions should consider supporting control signalling sent over licensed band, and Ranging signal over unlicensed band.
    Ranging signal bandwidth up to [400MHz] are considered.
    Unlicensed band up to 71 GHz for Ranging signal transmission are considered.
    The solution should support one-to-one Ranging & one-to-many Ranging.
    The solution should enable power efficient Ranging with one or multiple UEs.
    The solution should enable one-hop Ranging for UEs without LOS path.
    The solution should support Reduced capability UE.
    The solution should support both network initiated and UE initiated Ranging.

## Slide 8: Thanks