## Slide 1: Source: China Telecom
Discussion on Multi-SIM devices enhancement in Rel-18
3GPP TSG RAN Rel-18 workshop
Electronic Meeting, June 28-July 2, 2021
RWS-210299

## Slide 2: Introduction
NSA
NR downlink 2CC
Downlink 4*4 MIMO
Uplink
2*2 MIMO
In 5G generation, devices are equipped with more antennas and RF chains to support uplink/downlink MIMO, DC and CA as to meet the requirement of eMBB services. 5G UE supporting 2T/4R has been the mainstream in market.
Without adding new RF module, Multi-SIM UE can support dual Tx/ dual Rx by sharing one Tx and multiple Rx chains between two USIMs dynamically, and therefore provide a better user experience.

## Slide 3: Use case1
Multi-SIM mobile phones supporting dual Tx/ dual Rx can offer better user experience in voice service and data service
Scenarios | dual Tx/ dual Rx | single Tx/ dual Rx single Tx/ single Rx
Scenario1: UE is performing data services in USIM-1 and USIM-2 has an incoming call. | Data services can continue in USIM1. Voice service in USIM2 can be setup without any impact | Data services has to be interrupted in USIM1 Voice service in USIM2 can be setup without any impact
Scenario2: UE has a voice call ongoing in USIM1 and USIM 2 has an incoming call. | User will be notified the incoming call in USIM2 and can decide which call to continue. | User will lose call in USIM2 as UE won’t response to paging in USIM2 while USIM1 has an ongoing call.

## Slide 4: Use case 2
Multi-SIM module supporting dual Tx/ dual Rx can offer more reliable connections for vehicle communication.
Multi-SIM vehicle module with dual Tx/ dual Rx capabilities can set up connections with both NW-1 and NW-2 and application can route data packets through either or both network according to the network service quality. The server finally aggregates the packets from NW-1 and NW-2 in application layer.
NW-1
NW-2
Core network
Core network
Application Server

## Slide 5: Use case 3
Multi-SIM mobile phones supporting dual Tx/ dual Rx can activate 5G message services in both USIMs.
Traditional short message will gradually evolve to RCS message (rich communication message) defined by GSMA, which enable the users to exchange multimedia contents such as picture, video, audio and file via operators’ IMS core network. The UE has to keep alive for RCS message every three to five minutes. In addition, if RCS message service in USIM-1 and USIM-2 are frequently activated like wechat and whatsAPP, it is better for UE to keep connection with both NW-1 and NW-2 .

## Slide 6: To support Dual Tx/ Dual Rx Multi-SIM devices in Rel 18
In 3GPP rel 17, WID of support for Multi-SIM devices is still ongoing. The scope of the WI only covers the use cases for Multi-SIM devices with single Tx/ dual Rx and single Tx/ single Rx capability. Dual Rx/ dual Tx is excluded from the WI for lack of time budget. However, plenty of companies thought dual Tx/ dual Rx Multi-SIM devices deserve further study in future release.

## Slide 7: Key issues 1-1
Key issue1: UE capabilities are impacted when it tunes away partial of Tx or Rx chains from NW-1 for connected mode activates in USIM-2.
Case 1: Multi-SIM UE supports 2 Tx in NR SA with one Tx sharing between USIM-1 and USIM-2.
  When both USIM-1 and USIM-2 are in RRC CONNECTED state, UE has to tune away one Tx chain from USIM-1 to USIM-2 and the USIM-1 has to change from 2Tx to 1Tx in uplink. Therefore, the following UE capabilities may be impacted:
    maxNumberMIMO-LayersCB-PUSCH, maxNumberMIMO-LayersNonCB-PUSCH
    supportedSRS-TxPortSwitch :
    maxNumberSRS-Ports-PerResource,
    CA band combination
Notes: maxNumberSimultaneousSRS-ResourceTx
maxNumberMIMO-LayersCB-PUSCH
maxNumberMIMO-LayersNonCB-PUSCH
maxNumberSRS-ResourcePerSet
maxNumberSimultaneousSRS-ResourceTx
Defines the maximum number of simultaneous transmitted SRS resources at one symbol for non-codebook based transmission to the UE. This feature is not supported for SUL.

## Slide 8: Key issues 1-2
Case 2: Multi-SIM UE supports NSA with one Tx sharing between USIM-1 and USIM-2.
  When USIM-1 is in connected mode with SCG activated and USIM-2 also enter RRC CONNECTED state, UE has to tune away one Tx chain from USIM-1 to USIM-2 . The USIM-1 will encounter a SN failure.
Case 3: Partial of the Rx chains for NR in USIM-1 are sharing with USIM-2.
  When USIM-2 enters RRC CONNECTED states. The following capabilities of UE may change in network 1 when USIM-2 enters RRC CONNECTED states:
    maxNumberMIMO-LayersPDSCH
    CA band combination and DC band combination
Notes: maxNumberSimultaneousSRS-ResourceTx
maxNumberMIMO-LayersCB-PUSCH
maxNumberMIMO-LayersNonCB-PUSCH
maxNumberSRS-ResourcePerSet
maxNumberSimultaneousSRS-ResourceTx

## Slide 9: Key issues 2
Key issue2: UE transmitting power may be impacted for UL power sharing between two USIMs.
When dual Tx/ dual Rx UE are in RRC connected status in both USIMs and transmitting simultaneously with two networks, the total uplink transmitting power is shared by two USIMs. As restrained by SAR or RF structure implementation, the UE may not be able to support simultaneous transmition with maximum output power when both USIMs are active. Therefore, UE should reduce output power and the strategy of output power reduction maybe diverse for different type of devices.
Notes: maxNumberSimultaneousSRS-ResourceTx
maxNumberMIMO-LayersCB-PUSCH
maxNumberMIMO-LayersNonCB-PUSCH
maxNumberSRS-ResourcePerSet
maxNumberSimultaneousSRS-ResourceTx
Defines the maximum number of simultaneous transmitted SRS resources at one symbol for non-codebook based transmission to the UE. This feature is not supported for SUL.

## Slide 10: Key issues 3-1
Key issue3: Interference maybe exist between different USIMs.
For UE supporting dual Tx/dual Rx, kinds of interference signals (Harmonics Interference，Intermodulation Interference, Crossmodulation Interference，Blocking Interference,etc) between different RF transmission chains may exist. To solve complex problems of interference when UE activates two USIMs, interference control scheme needs to be considered for both chip design and device design.
Notes: maxNumberSimultaneousSRS-ResourceTx
maxNumberMIMO-LayersCB-PUSCH
maxNumberMIMO-LayersNonCB-PUSCH
maxNumberSRS-ResourcePerSet
maxNumberSimultaneousSRS-ResourceTx
Defines the maximum number of simultaneous transmitted SRS resources at one symbol for non-codebook based transmission to the UE. This feature is not supported for SUL.

## Slide 11: Key issues 3-2
Some interference examples:
1) If USIM1 runs NR 2100Mhz and USIM2 runs LTE 700Mhz meanwhile, then 3rd harmonics of 700Mhz from USIM2's Tx chians due to nonlinearity of RF ICs maybe exist in receiver of 2100Mhz from USIM1's RX chains, which can aggravate the sensibility of 2100MHz. To control the similar interference, some key RF specs must be considerd seriously, such as Output RF spectrum emissions.
2) If there are unwanted crossmodulation and intermodulation interference signals from one USIM's TX chian, then these bad signals can cause strong interference due to nonlinearity of RF ICs to the receiver of another RX chain even other devices which runs at same or similar frequency. Some key RF specs, such as ACLR must be consided seriously.
Notes: maxNumberSimultaneousSRS-ResourceTx
maxNumberMIMO-LayersCB-PUSCH
maxNumberMIMO-LayersNonCB-PUSCH
maxNumberSRS-ResourcePerSet
maxNumberSimultaneousSRS-ResourceTx
Defines the maximum number of simultaneous transmitted SRS resources at one symbol for non-codebook based transmission to the UE. This feature is not supported for SUL.

## Slide 12: Conclusion
Proposal: Enhancement on Multi-SIM devices supporting dual TX/ dual Rx are considered in a Rel-18 WI.
Specify mechanism for UE to notify Network A of its update in capabilities when it tune away partial of Tx or Rx chains from Network A.
Specify mechanism for UE to request Network A to release SCG or deactivate Scell for Multi-SIM purpose.
Specify power transmitting requirement and power control scheme for uplink power sharing between two USIMs.
For interferences between different USIMs, specify an interference control scheme if needed.
Notes: maxNumberSimultaneousSRS-ResourceTx
maxNumberMIMO-LayersCB-PUSCH
maxNumberMIMO-LayersNonCB-PUSCH
maxNumberSRS-ResourcePerSet
maxNumberSimultaneousSRS-ResourceTx
Defines the maximum number of simultaneous transmitted SRS resources at one symbol for non-codebook based transmission to the UE. This feature is not supported for SUL.

## Slide 13
THANK YOU .