## Slide 1
Advanced Modulation for 5G-Advanced
3GPP TSG RAN Rel-18 workshop
June 28-July 2, 2021
Agenda Item: 4.1
RWS-210305
Source: Sony

## Slide 2: Requirements to meet in 5G-Advanced
New use cases e.g. XR (26.928) & VIAPA (22.263) require:
  High throughput and/or low latency and/or high reliability
Low latency is achievable with:
  Higher channel bandwidths available at > 52.6GHz bands
High levels of PN at >52.6GHz
  Necessitates high PA back-off to achieve EVM targets
  High back-off translates to lower SINR
Among methods to achieve high throughput are:
  Larger constellation sizes
  Constellation shaping that reduces the required SINR decoding
Low latency can be achieved by:
  Larger SCS that makes short slots
High throughput + low latency can be achieved by:
  Large constellations shaped to require low SINR + wider bandwidths with large SCS

## Slide 3: Advanced Modulation Pros
For high TP: Large constellations carry more bits per RB than smaller constellations.
For low latency: we need shorter slots (shorter OFDM symbols, i.e. higher SCS).
  Higher SCS requires wider bandwidths that are only available at >52.6GHz bands.
  These bands suffer from a lot of phase noise and so there is a need for a large back-off of the PA in order to achieve required EVM.
  Large back-off means low SINR.
  Therefore, large constellations that can work at lower SINR are needed to achieve high TP and low latency at >52.6GHz bands.

## Slide 4: Advanced Modulation Schemes
Non-uniform constellations
  Shaping gain reduces required SINR
  Shaping gain increases with constellation size
Mixed Constellations
  Exploit channel selectivity to maximise throughput
Index modulation
  Introducing index bit in addition to conventional constellation
Enhanced CSI for channel measurement
  Better granularity – at least to SINR per PRB level

## Slide 5: Proposal for Advanced Modulation in Rel-18
Study advanced modulation techniques and their usefulness with attention to the following aspects:
High throughput
Decoding in lower SINR than current modulation schemes
New forms of CSI to support decoding of these modulations