## Slide 1: Views on NR positioning for Release 18
3GPP TSG RAN Rel-18 workshop RWS-210322
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Views on NR Positioning for Release 18 Low Power and Low Complexity Positioning (1)
Motivation
  Enable positioning for use cases with low complexity and low power industry devices.
  Support network low complex solutions and positioning methods
Low Power Applications
Smart Factory
Mission Critical Applications

## Slide 3
Objectives
  Support positioning for low-power devices with advanced positioning capabilities
  Support positioning for RedCap devices
  Study techniques and methods to reduce network complexity including
    Synchronization mitigation techniques
    5G DL-PRS Beacons or Positioning Reference Devices (PRD)
    Introduce reporting and signaling to support fingerprinting method
Views on NR Positioning for Release 18 Low Power and Low Complexity Positioning (2)

## Slide 4
Motivation
  Enhance the positioning accuracy and reliability in challenging environments
  Enhance UL resource utilization for multi-user scenarios
Impact of beam selection on the positioning accuracy:
CDF for 81 beam pair error on 8 positions (P1…P8) using
real-World FR2 evaluation on Rel-16 positioning signals
Views on NR Positioning for Release 18 Positioning Enhancements (1)
Seamless positioning for mobility scenarios

## Slide 5
Objectives
  Beam management enhancement for positioning in FR2
  Improvements for high accuracy continuous tracking
    Enable seamless positioning for mobility scenarios between positioning methods based on integrity and quality
    Increase efficiency of parallel tracking of many devices (reduce number of required REs, power consumption, overhead for assistance data delivery, overhead for power control and timing advance adjustment, etc.)
    Phase measurements for positioning
    SRS enhancement (support of multi-port SRS, phase correction for the staggered SRS, 1-symbol OFDM …)
Views on NR Positioning for Release 18 Positioning Enhancements (2)