## Slide 1: Views on Rel-18 IoT Topics
3GPP RAN Plenary Release 18 Workshop, June 28th – July 2nd 2021, eMeeting
Evolution towards 5G-Advanced
Rel-18
RedCap, PowSav, NB-IoT and IIoT

## Slide 2: Views on Rel-18 IoT Topics
Target NR low complexity devices
Enhancements for Power Saving
Enhancements for NB-IoT
Enhancements for Industrial-IoT
Motivation
  Target use cases below the current RedCap WI
  Further cost and capability reductions are required to cover the whole spectrum
Scope and Objective
  Small bandwidth support for RedCap devices (<=5MHz, NPN support)
  NR-U Enhancements for RedCap devices (WI PowSav, WI RedCap)
Motivation
  Expanding use cases and further reduced power consumption
  Energy harvesting devices for longer lifetime
Scope and Objective
  Power Saving in Connected Mode (measurements, PDCCH monitoring, mobility)
Motivation
  Energy efficient data transmission for low-priority, latency tolerant devices
  Enhancements for deep indoor coverage
Scope and Objective
  CB-PUR – Contention-based Preconfigured Uplink Resources
  Support small data transmission in preconfigured, shared uplink resources (NB-IOT)
Motivation
  Enable small scale industrial deployments in unlicensed spectrum
  Support for XR cloud services
Scope and Objective
  Enhanced URLLC support for IIoT/factory automation in unlicensed bands
  LBT enhancements, e.g. beam based access and directional LBT
  Enhancements for AR/VR applications
    High throughput
    Low latency HARQ improvements

## Slide 3: Target NR low complexity devices
RedCap
Support of small bandwidths down to 5MHz (or less)
  Enabling RedCap in non-terrestrial deployments
  RedCap for less then 5MHz to enable deployments in special licensed bands
Consider more use cases for RedCap
  Sparse MOD applications
  LTE-M use cases in 5G-NPN deployments
RedCap enhancements for licensed and unlicensed bands
  Enhanced beam-operation
  More flexible power saving techniques, considering also operation in unlicensed bands
  Coverage extension compared to Rel-17 RedCap devices

## Slide 4: Enhancements for Power Saving
Low-power use cases
Motivation:
  Enable more use cases requiring longer battery lifetime
Scope:
  Power Saving enhancements in RRC_Connected
    RRM Enhancements
    PDCCH Enhancements
  Energy harvesting for longer lifetime
    Further relaxation of timers and data rate
  Extend use of compact DCI
    Incremental DCI information for reduced signaling

## Slide 5: Enhancements for Industrial-IoT
IIOT/URLLC
Motivation:
  Small-scale deployments in unlicensed spectrum
  XR improvements
Scope:
  AR/VR need throughput and reliability
  Low-latency HARQ to improve spectral efficiency
    Early HARQ feedback to reduce the HARQ RTT

## Slide 6: Enhancements for NB-IoT
Narrowband IoT/LPWAN
Motivation:
  Extend NB-IoT use cases to even lower power consumption
Scope:
  Extend PUR with contention-based mode for
    Non critical sensor measurements
    Latency tolerant applications
    Energy harvesting devices
    Dedicated CB-PUR carrier