## Slide 1: Scope for Full Duplex Operation Study for Rel-18
3GPP TSG RAN Rel-18 workshop RWS-210326
Electronic Meeting, June 28th - July 2nd, 2021

## Slide 2: MOTIVATION & KEY CHALLENGES
In general, full-duplex (FD) duplexing scheme offers:
  Low latency bidirectional link enabled by DL and UL data channels coexistence over the same frequency bandwidth parts Reuse of the frequency spectrum recourses, and accordingly doubling the aggregated – DL and UL – data throughput
  Efficient spectral utilization while less spectrum pollution is occurred; due to the fact that OOB emissions are centered around single unpaired spectral band
Realization challenges /requirements for full-duplex (FD) duplexing:
  Severe self-interference at the FD Node that must be cancelled by the receiver without delay
  Inter cellular network entities interferences in association to flexible duplexing, full-duplex duplexing and flexible resource allocation
  Self-interference channel tracking for uninterrupted full-duplex wireless communication link
RWS-210326

## Slide 3: Full-Duplex gNB and Multi-User FDM Uplink (Flexible FDD UEs)
BS’s capabilities:
Self-interference cancellation /concurrent UL reception in presence of active DL transmission
Flexible UL-DL frequency sub-band allocation
UEs’ capabilities:
Flexible UL band allocation
[Optional] Partial self-interference cancellation
UL and DL share the same band (unpaired spectrum)
Flexible UL and DL band allocation within the shared band
RWS-210326

## Slide 4: Crosslink (UE-UE) Interference Handling Techniques for Full-Duplex gNB Operation
A UE subject to interference from other UE might hold a spatial signature that can exploit at the Interfered UE to be avoided/suppressed
A UE can implement a proactive inter-UE avoidance techniques. These technique can signaled to the UE by the BS to configure with respect to maximum interfered UE
Alternative methods at the UE side can be used to avoid interference with respect to the gNB full-duplex operation
RWS-210326

## Slide 5: Scope and Objectives of FDR Study Item (I)
Feasibility study for self-interference cancellation as an enabler and flexible duplexing and full-duplex duplexing use-cases [RAN1/RAN4]
  Study use-case for application for benefiting from full-duplex operation, such as latency reduction and throughput enhancement
  Define self-interference cancellation requirements with respect to (maximum) transmit power at gNB and UE
  Define achievable self-interference cancellation levels with respect to overlapping bandwidth and wireless transceiver characteristics at gNB and UE
  Study effectiveness of self-interference cancellation techniques in various bands of FR1 & FR2:
    Antenna separation and polarization techniques
    Beam and phased-array panel based self-interference cancellation
    Active hybrid and analog self-interference cancellation
    Solely digital self-interference cancellation
  Study impact of self-interference cancellation on the reciprocity of bidirectional FD radio communication channel
  Note: The study has the primary goal to investigate the flexible and full-duplex operation at the gNB, however, some of the results might be reused (adapt) for UEs as well.
  Note: The study has the primary goal to investigate the flexible and full-duplex operation in unpaired spectrum, however, paired spectrum bands are not excluded and can be covered within the study as well.
RWS-210326

## Slide 6: Scope and Objectives of FDR Study Item (II)
Standardization-impact study in presence of self-interference cancellation to enable flexible duplexing and full-duplex schemes [RAN1]
  Study legacy sounding reference signals for self-interference channel estimation and tracking
  Resource allocation and interference coordination in presence of CLI (gNB-to-gNB and UE-to-UE)
  Coexistence scenarios for operation of Full-Duplex and Half-Duplex for support of legacy UEs
  MIMO operation, including Beam Management, Multi-TRP, CSI, CLI measurements
  Note: The study has the primary goal to investigate the flexible and full-duplex operation at the gNB, however, some of the results might be reused (adapt) for UEs as well.
  Note: The study has the primary goal to investigate the flexible and full-duplex operation in unpaired spectrum, however, paired spectrum bands are not excluded and can be covered within the study as well.
RWS-210326

## Slide 7: Enhanced Sidelink Features
Summary of Objectives and Scope for Rel-18 SID
Objectives
  Definition of Self-and Cross-Link-Interference-Requirements
    Support of legacy devices
    Flexible sub-band allocation
Scope
  Study and categorize relevant Use Cases and Application Scenarios
  Enhanced throughput, reliability, sensing and positioning by supporting FDR
  Enhanced interference management in FDR scenarios e.g. by enhanced CLI reporting functionality
RWS-210326