## Slide 1: Requirements to URLLC, positioning and perception for automotive industry
CMCC, BMW Brilliance Automotive
3GPP TSG RAN Rel-18 workshop RWS-210350
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Outline
Overview on Automotive Industry
URLLC enhancement
Positioning enhancement
Perception（Passive IoT）

## Slide 3
Overview--5G Motivation From Automotive Industry Perspective
cables are difficult to move
unreliability of WiFi communication
high cost of UWB positioning
weak coverage of RFID based perception
Automotive industry requires one single network to support all the above capabilities.
Press & Body
Paint
Assembly
Wireless communication is playing great role throughout the whole automotive production process, including press, body, paint, assembly and the corresponding logistic
Pains for current automotive production communication system

## Slide 4
4 Capabilities are required to be supported by one network in the automotive industry:
Connection, Location, Timing, Perception.
Workers
Equipment
Material
Data Interoperability
Location
Timing
Connection
Connection service
Application components
Application development platform
APP（worker）
…
…
Information Feedback
Precise Control
Digital Platform
5G Network
Filed
APP（Equipment）
APP（Material）
Digital model library
Digital Plant
Positioning
Service
Identity/ID service
User service
Network Monitoring
Data Interoperability
Perception
Physical Plant
Overview--One network to support all the capabilities

## Slide 5
Overview--Use Cases for Automotive Industry
After field trial, we observed the above use cases marked with purple CANNOT be met by current 5G specification, which need further enhancement in Rel-18, including the support for Low-latency control of massive robotic arms, positioning for NLOS, perception of materials.
PTL Trolley
Machine Vision
Welding group control
5G Networking AGV
Automobile assembly workshop
Data center
Robot Control
5G could solve frequent Wi-Fi disconnection causes information loss and system confusion.
PTL trolley communication is 10 times/minute. Single-vehicle, 1000 square meters, 200 concurrent requests per minute, Wi-Fi cannot meet large concurrency requirements.
MCU Software 5G Loading
5G can provide software download for 100 vehicles at the same time, eliminating up to one hour of loading time and eliminating space consumption for centralized parking of vehicles.
Dozens of network cables between the 5G welding control cabinet and computer
5G Substitutes Wired for Low-Latency Control of Robotic Arm and Flexible Deployment
5G supports remote upgrade and maintenance.
Positioning
Perception
multiple inbound and outbound crossings、asset stocktaking
Logistics Management 、vehicle positioning in product line
Purple
The above use cases marked with green can be met by current 5G specification.
Green
5G can satisfy several use cases, but some use cases (URLLC, Positioning and Perception) still need to be further enhanced to meet the requirement from automotive industry.

## Slide 6
Overview--Requirements for 5G-Advanced
 | Expected performance for 5G-Advanced | Comparison Technology in industry | Pain Point of comparison Technology
URLLC | Low latency and high reliability at high density factory: 4ms, 99.9999% @ 400UE/5000m2 | Cable/wifi | Flexibility Constraint for cable and performance disadvantages for wifi
Positioning | Accuracy for NLOS indoor scenario: 0.1m(Horizontal)@90%, 0.5m(Horizontal)@99.99% Battery life: ~ 1 year Low positioning interruption time when switching from indoor cellular positioning to outdoor GPS positioning. | UWB | equipment cost
Perception (Passive IoT) | Coverage capability: communication distance should support more than 30 meters to construct a feasible network coverage in the 5000 m2 warehouse. UE power consumption: <0.1mW to support working without battery. Low cost: <0.1￥(~0.02$) to meet cost-sensitive applications. Positioning accuracy： 3~5m(Horizontal&Vertical) @90% for positioning. | RFID | weak coverage
Automotive industry expects one single network to support the following capabilities.

## Slide 7: Outline
Overview on Automotive Industry
URLLC enhancement
Positioning enhancement
Perception（Passive IoT）

## Slide 8
URLLC enhancement--Motivation
The gripper and its actuators mounted on industrial robots would currently be connected via cables.
Motivation：
Cable-connected robot repetitively twists, turns, and bends with restricted motion trajectories leads to cable wear off and robot downtime;
Regular EOAT switching such as different sizes of grippers leads to interface (probes) wear off and downtime;
The product line would currently be connected via cables.
Motivation：
1、Resolves complex networks and complex installation and cabling；Resolves high hardware costs and maintenance.
2、 Support flexible production in future with fast reconfiguration to product line.
Line controller
Robot controller
MURR module
frequency
converter
Robot controller
Wireless EOAT for Robots
EOAT：End of arm tool
Wireless product line
Use cases and Motivation
Wireless Slide Rail
The AGV slides on the rail for transport and would currently be connected via copper core deployed aligned with the rail.
Motivation：
Unstable signal transmission and high fault rate due to sliding on the Rail.
The transmission media(copper) oxidizes easily. Large effort on Deployment、Operation & Maintenance、

## Slide 9
URLLC enhancement--Requirement
  Automotive industry requirement for URLLC enhancement:
  Low latency and high reliability at high density factory: 4ms, 99.9999% @ 400UE/5000m2. The latency and reliability should be close to current wired system, while supporting high density UEs in the factory, e.g. 100 line PLC in a Body shop (about 100000 m2), each PLC consist of average 80 slave stations with wireless requirement.
  Compatibility with OT network: Integrated with industrial Ethernet, e.g. Profinet RT. Profinet is widely used in some Automotive Industry like BMW Brilliance Automotive (BBA). Note: mainly SA2 impact
  In addition, 5G-Advanced network for vertical user should take following aspects into consideration：
    One network supporting multi-functions: URLLC should co-exist with other eMBB services with high uplink rate, e.g. Machine vision；
    Indoor and outdoor interference coordination, when different TDD configuration is applied
    Chip capability: Self-contained is not supported in the chip and URLLC should be compatible with the current chip ecosystem.
Requirement

## Slide 10: Outline
Overview on Automotive Industry
URLLC enhancement
Positioning enhancement
Perception（Passive IoT）

## Slide 11
Positioning Enhancement--Motivation
Motivation: Real-time tracking of vehicle locations on the assembly line, achieving visualized and precise management of the entire production process. Deploying 1 single network to provide capabilities of radio connection and indoor positioning will reduce the cost of investment, comparing with the current deployed cable connection + UWB positioning
Positioning accuracy：0.1m for NLOS
Car positioning in factory
Use case and Motivation

## Slide 12
Positioning enhancement--Requirement
Accuracy for NLOS indoor scenario: 0.1m(Horizontal)@90%, 0.5m(Horizontal)@99.99%
Battery life: ~ 1 year
Low positioning interruption time when switching from indoor cellular positioning to outdoor GPS positioning.
Requirement

## Slide 13: Outline
Overview on Automotive Industry
URLLC enhancement
Positioning enhancement
Perception（Passive IoT）

## Slide 14
Passive IoT enabled Perception--Motivation
We have considered RFID technology, but RFID is not good.
Bad performance: Based on our test, RFID can only read labels in case the labels are not blocked. On the other words, in case the label attached on the bin is blocked, e.g. by another metal bin, RFID always fail to read it.
High Cost: The transmission distance for RFID readers is short, about 8 meters based on test. We need to deploy a lot of RFID readers to cover the whole warehouse(about 5000m2) and the network cost is very high.
Bin management at the Gate of the warehouse
Scenario: unique identify the bins for logistic management. E.g.
Identify which bins move in or out of the warehouse, at the Gate of the warehouse.
Identify the bins in a specific area inside the warehouse.
Currently, bins are manually managed via scanning the barcode attached on each bin.
Causes：
High OPEX: OPEX of warehouse management is very high for us;
Manual error: Manual work often cause errors and many bins lost;
We are considering Automatic bin Management in the warehouse with a quite low cost.
Use cases and Motivation
Bin management inside the warehouse

## Slide 15
Passive IoT enabled Perception--Requirement
Coverage capability: communication distance should be enhanced to 30 meters to construct a feasible network coverage in the 5000 m2 warehouse.
UE power consumption: <0.1mW to support working without battery.
UE cost: <0.1￥(~0.02$) to meet cost-sensitive applications.
Positioning accuracy： 3~5m(Horizontal&Vertical) @ 90% for positioning .
There is no battery in the terminal and the terminal accumulate the energy from radio signaling. Additionally, the terminal may also accumulate energy from solar energy as supplement.
Requirement to support Passive IoT
What is Passive IoT

## Slide 16
Thank You

## Slide 17
Annex:
Introduction of a New 3GPP member: BMW Brilliance Automotive (BBA)
  Founded in May 2003, BMW Brilliance Automotive Ltd. (BBA) is a joint venture between the BMW Group and Brilliance China Automotive Holdings Ltd. Business operations of BBA include production, sales and after-sales services of BMW automobiles in China. BBA has a state-of-the-art production base in Shenyang, a branch company in Beijing and an extensive national sales and service network. The joint venture employees around 20,000 people and has a network of nearly 400 local suppliers.
  BMW Brilliance’s production base in Shenyang is the BMW Group’s largest production base worldwide. It currently manufactures six BMW models: BMW 5 Series (long wheelbase), BMW 3 Series (long wheelbase and standard wheelbase), BMW X3, BMW X2, BMW X1 (long wheelbase) and BMW 1 Series Sedan.
  BBA’s production system applies innovative technologies, sustainable production and the latest Industry 4.0 manufacturing technologies, and it continues to promote these initiatives with its partners.
Please find more at: http://www.bmw-brilliance.cn/cn/en/index.html